## Slide 1: Telecom Italia vision and requirements on 5G
RWS-150041
3GPPRAN-workshop on 5G
17-18 September 2015, Phoenix, USA

## Slide 2: Statement
Telecom Italia endorses the contribution from NGMN
This contribution describes the overall vision and highlights some requirements of relevance from Telecom Italia
RWS-150041

## Slide 3: 5G Pillars
xMBB Extreme Mobile Broadband
  High dense scenario and extreme high throughput where and when needed
mMTC Massive Machine-Type Communication
  Extreme high number of low bit rate connections
uMTC Ultra-reliable MTC
  Including factory automation, mission critical services, Public Safety,….
Source METIS
The identified pillars have the same importance and priority for Telecom Italia
The radio design should encompass all use cases from the beginning and be forward compatible to new requirements
5G RAN: a family of radio access techniques based on LTE Evolution plus new RAT(s) for specific use cases
RWS-150041

## Slide 4
New spectrum to be identified below and above 6 GHz
Licensed and unlicensed, including tight interworking with WiFi
From sub-GHz to mm-wave
  Lower frequencies to be used for coverage, included deep indoor, and moderate traffic capacity  scenarios and use cases covered by LTE evolution
  Higher frequencies to be used in a complementary approach for extreme traffic capacity in dense scenarios and specific use case  mainly for new RAT(s)
Spectrum framework evolution
5G Wireless Access = LTE Evolution + new RAT(s)
Lte MACRO
IT and Network virtualization
SON
NETAPI
CONTROL
BSS
OSS
BIG DATA
Digital factory
Service Layer/Cloud
RWS-150041

## Slide 5
xMBB
  a new RAT shall be designed in order to benefit from large bandwidth and cope with radio propagation at high frequency (> 6GHz)
  integration with an LTE control layer at lower frequency (<6Ghz) is a key enabler for early and successful deployment of 5G
uMTC and mMTC
  Evolution of LTE and introduction of a new RAT depending on the use case specific requirements
  Flexible accommodation of the new RAT at the lower frequency in order to ensure efficient spectrum allocation and refarming
Spectrum framework evolution
RWS-150041

## Slide 6
Aware of user and application needs and always able to assign Network resources based on those needs
  E.g. in terms of required performance at IP layer and/or app/use-case specific (new KPIs and finer granularity QCIs)
Extend Performance Management and MDT from network performance to user experience
  User / application level QoS and QoE monitoring capability supported by UEs and networks
  Interaction between (RAN/CN) control/management layer and service management layers
Maximize synergies of new RAT(s) (e.g. tight interworking) with LTE evolution
Management of 5G Radio Access Network shall benefit from Virtualization and provide:
  Standard definition of virtual RAN functions and interfaces to support management and orchestration in a flexible architecture, integrating LTE and new RAT
  Convergence of control plane and network management plane to support Autonomic/Self-management functions coping with different use cases and deployment
  A layered architecture, with standard and open API (open source)
Virtualized RAN shall be based on a standard and effective fronthauling solution:
  RAN and radio access dynamic re-configuration
  Ultra-high bitrate on 5G local access have to be transported by efficient fronthaul solutions
  Unique standard framework to allow simple operations and consistent behaviour in multi-vendor scenarios
  Fast standardization to avoid fragmentation on de-facto standards
5G: use case driven, configurable, dynamic radio access (1/2)
RWS-150041

## Slide 7
5G: use case driven, configurable, dynamic radio access (2/2)
Several services typically labeled as 5G services are already in the market or under development/regulation (smart capillary, m2m, Public Safety,…). The relations between ecosystems, markets, regulatory frameworks, assigned spectrum etc needs to be taken into consideration when defining service requirements and corresponding technical solutions
Standardization effort on LTE evolution shall be kept, being an integral part of 5G
Reinforce LTE techniques
  Network densification and HetNet
  Massive MIMO (>> than 8x8 antennas)
  Advanced receivers and interference coordination
  Enhanced multi-RAT coordination
  Wireless back/fronthaul; enhanced fronthaul (innovative split BBU-RRH)
5G radio access(es), including LTE evolution, shall be submitted to ITU-R to be included in IMT-2020
RWS-150041

## Slide 8
5G: virtualization
A 5G network architecture with native support for NFV enables fast creation of dedicated network instances optimized for specific customers, service scenarios and/or terminal types (network slices), potentially improving user experience and infrastructure resources
Network slices could be created by the operator combining elementary functions available in a catalogue. Composition of functions to create slices can be managed by the operator though the NFV Orchestration Platform
Integration of multiple RATs in the network slices, including WiFi
Examples of slices:
  Smartphone: fully-fledged functions distributed across the network
  Automotive: security, reliability, latency at the edge. Cloud node + open API for vertical applications.
  Sensors: avoid mobility, basic Control plane functions (e.g. authentication)
RWS-150041

## Slide 9
Energy efficiency
    Energy efficiency must be one of the drivers from the beginning
    Holistic approach to define solutions to improve energy efficiency
      E.g. to consider as normal operating conditions more challenging values (temperature, humidity, …) in the meantime ensuring long life cycles  avoid as much as possible air conditioning in equipment rooms (where people stays only for emergency operations or to install equipment)
      Switch on / switch off procedures
      …
    Define KPI to be fulfilled by RAN design
RWS-150041

## Slide 10: What is 5G for Telecom Italia
An extremely flexible and highly programmable e2e system, including evolution of LTE access and providing complementary solutions to LTE use cases. The system shall:
Serve at best high diversity types of communications (Human & Machine) with different performance attributes
Natively leverage NFV technologies:
  Support on demand composition of network functions and capabilities, enforcing flexible assignment of capability/capacity “where and when needed”
  Compatible evolution of standardization activities on LTE virtualization
Profitably support new business opportunities and provide sustainability thanks to cost saving, solutions for services low cost deployment, synergies with LTE evolution
Be future-proof and ready to serve even not yet identified use case and radio technologies
RWS-150041

## Slide 11
RWS-150041