## Slide 1: Feasibility Study on 5G Small-cell Deployment with a Beam-domain Processed Large-scale Antenna Array in High-frequency Bands
ASUSTeK, CCU and ITRI
September 2015
RWS-150077
(Revision of RWS-150025)
3GPP RAN Workshop on 5G
Phoenix, USA, 17 – 18 September, 2015

## Slide 2: INTRODUCTION
Key capabilities for the enhanced mobile broadband application set forth by ITU-R
  User experienced data rate : 100-1000 Mbps
  Area traffic capacity: 10 Mbps/m2
  etc.
A contiguous bandwidth of a few hundreds MHz is widely regarded as needed to meet the requirements.
  Such a large bandwidth may only be available at high frequency bands (above 6 GHz).
  Small cell with high antenna gain is essential for compensating the huge propagation loss incurred in high frequency bands.

## Slide 3
A small-cell system with a beam-domain processed large-scale antenna array, called Beam-group Division Multiple Access (BgDMA), in high-frequency bands is studied against the ITU-R 5G requirements.
  Achievable system capacity and user data rate are evaluated in a realistic outdoor environment based on ray-tracing channel modeling.

## Slide 4: KEY FEATURES OF BgDMA
Feature 1: Channel’s frequency selectivity is resolved by a beam-domain processing along with delay compensation.
  Fixed beam-book,
    ||
    : number of RF transceiver units
    : number of antenna at eNB
  The set of beams used by UEk, , can be found by a beam finding/tracking procedure.
  Delay spread is small over an individual beam.

## Slide 5
Feature 2: More than one beam can be utilized simultaneously by a UE to obtain diversity/spatial multiplexing gains and reduce blockage probability.

## Slide 6
Feature 3: High-order MU-MIMO (multi-user MIMO) is achieved with a low-complexity beam-group based joint spatial division/multiplexing.
  A fixed beamformer for beam-group based spatial division
  Outer precoding for multiplexing users in the same user-group (spatial multiplexing)

## Slide 7: Summary of BgDMA Key Features (1/2)

## Slide 8: Summary of BgDMA Key Features (2/2)

## Slide 9: RAY-TRACING BASED CHANNEL MODELING
Wireless InSite 2.7.1
  A ray-tracing based simulation tool that provides results over a frequency range from 50MHz to 100GHz.
  Bern/Switzerland, CCU/Taiwan
Configuration
  Antenna Height: eNB (10m, 6m); UE (1.8m, 1.5m)
  Carrier Frequencies:10,20,30,40 GHz
  Ray parameters
    AOA,AOD, power, phase, delay

## Slide 10: Bern/Switzerland
35 eNBs with cell radius around 100m
3268 outdoor UEs (approximately 100 UEs per eNB, uniformly distributed over the coverage area)
Simulation area
Reference: Google Earth Pro 7.1.2.2041

## Slide 11
3D map and UE distribution

## Slide 12
System Setup
Parameters |  | Values
Cell Architecture (ISD=200m) |  | 35 base stations
Number of UEs |  | 3268
Carrier Frequencies (GHz) |  | 10,20,30,40
Signal bandwidth (MHz) |  | 500
Antenna at eNB (linear array) | Number | 64,32
 | Antenna spacing | /2
 | Height(meter) | 10
Antenna at UE | Number | 1
 | Pattern | Omni-directional
 | Height(meter) | 1.8
Transmit Power (dBm) |  | 23
Beambook | Type | DFT-based
 | Number of Beams, | 128, 64
(dBm) |  | -174 dBm + 87 + 6 = -81 dBm
 | Noise Figure | 
Power Threshold for Examined Rays (dBm) |  | -140
SINR Threshold for Detectable Beams(dB) |  | -15
SINR Threshold for Outage(dB) |  | -6
Parameters |  | Values
Cell Architecture (ISD=200m) |  | 35 base stations
Number of UEs |  | 3268
 |  | 10,20,30,40
Signal bandwidth (MHz) |  | 500
Antenna at eNB (linear array) | Number | 64,32
 | Antenna spacing | 
 | Height(meter) | 10
Antenna at UE | Number | 1
 | Pattern | Omni-directional
 | Height(meter) | 1.8
Transmit Power (dBm) |  | 23
Beambook | Type | DFT-based
 |  | 128, 64
 |  | -174 dBm + 87 + 6 = -81 dBm
Power Threshold for Examined Rays (dBm) |  | -140
SINR Threshold for Detectable Beams(dB) |  | -15
SINR Threshold for Outage(dB) |  | -6

## Slide 13
Outage probability

## Slide 14: UPLINK PERFORMANCE (Single-User) Delay Spread (1/2)
-power delay spread
Beam set selection: power loss less than 0.5dB

## Slide 15: Delay Spread (2/2)

## Slide 16: Number of Beams in a Beam Set

## Slide 17: Achievable Rates(1/2)
bit/s/Hz
k largest beams in the beam-set

## Slide 18: Achievable Rates(2/2)

## Slide 19: UPLINK PERFORMANCE (Multi-User)
, the set of beams used by UEk, is found with a beam finding/tracking procedure.
User grouping
  UEs with overlapping beams are put into same user-group; that is, UE and UE are in the same user-group iff

## Slide 20: Number of Users in a Group
: user density

## Slide 21: Number of Beams in a Group

## Slide 22: Dimension of Group MU-MIMO Channel (1/2)

## Slide 23: Dimension of Group MU-MIMO Channel (2/2)

## Slide 24: Uplink Achievable Rates
One antenna per UE
Capacity-approaching channel coding for each UE
MMSE receiver

## Slide 25: UE Achievable Rates (1/2)

## Slide 26: UE Achievable Rates (2/2)

## Slide 27: Average Sum Rate Per Cell

## Slide 28: BEAM FINDING AND TRACKING
Single-subcarrier beam finding
reference signal
Multiple-subcarrier beam finding
reference signal
reference signal
reference signal

## Slide 29
Simulation routes

## Slide 30
Extra beams found by multiple sub-carrier beam finding
number of beams in a beam set Extra beams found probability by multiple subcarrier beam finding | 1 | 2 | 3 | 4 | 5
1 | 0.012 | 0.008 | 0.036 | 0.016 | 0.028
2 | 0 | 0 | 0 | 0 | 0
3 | 0 | 0 | 0 | 0 | 0

## Slide 31
Performance loss due to less frequent beam finding/tracking

## Slide 32: CONCLUSIONS
The feasibility of small-cell deployment with a large-scale antenna array in high-frequency bands is investigated against the ITU-R 5G requirements.
Initial results show that:
  The use of small-cell deployment with large-scale antenna technology in high frequency bands is promising to meet the ITU-R 5G requirements set forth on the enhanced mobile broadband application .
  With a beam-domain processing, the merits of using a large-scale antenna array can be reaped at a complexity-effective way.

## Slide 33: Thanks