## Slide 1: Views on 5G New RAT in 3GPP
3GPP RAN workshop on 5G
Phoenix, AZ, USA, September 17-18, 2015.
RWS-150085
CATR, CATT, CMCC, China Telecom, China Unicom, Coolpad, HiSilicon, Huawei, OPPO, Potevio, ZTE, Alcatel-lucent, Alcatel-lucent Shanghai Bell

## Slide 2: ITU 5G vision
IMT-2020 (“5G”) usage scenario
Usage scenarios extend from MBB to Internet of Things.
IMT-2020 (“5G”) Key capabilities
Different usage scenarios have quite different capability requirements.
Recommendation ITU-R M.[IMT.VISION]

## Slide 3: 5G overview in 3GPP
Target: Highly flexible and capable 5G system to meet diverse requirements for 3 usage scenarios envisaged for 2020 and beyond.
New RAT for 5G that is not constrained by backward compatibility to LTE needs to be studied to fulfill all the requirements.
  needs to enable new service using the same air interface framework to fulfill all IMT-2020 requirements. Flexible design to support 3 usage scenarios.
  supports scalable numerology and flexible frame structure.
  considers new waveform, coding scheme, and multiple access.
The 5G new RAT will tightly integrate with LTE-A evolution.
3GPP will take three releases (Rel-14, 15, and 16) to accomplish the ITU IMT-2020 submission.

## Slide 4: Considerations for new RAT
5G new RAT shall apply at both low and high frequency band. However low frequency market is more urgent and has higher priority.
  Vertical market is very important for mobile industry and is mainly deployed in sub 6GHz.
  New sub 6GHz IMT spectrum will be identified in WRC15.
  Air interface design for high frequency is based on high frequency channel model which is not ready.
  High frequency spectrum for IMT will be identified in WRC19.

## Slide 5: Organize 5G RAN SIs and WIs and Time Plan
Rel-14
Rel-15
(Initial 5G)
Rel-16
(Comprehensive 5G)
5G phase 2 WI(s)
5G phase 1 WI(s)
5G SI(s): Scenario and Requirements…
2016.3
2017.6
2018.9
2019.12
5G SI(s):
Fundamental features of new RAT.
Sub 6GHz, support both eMBB and IoT
Other features and enhancements.
Meet all IMT-2020 requirements
Proposal
Spec
ITU process
Other features / Enhancements
New RAT framework
Start from sub 6GHz
SI: HF (>6GHz) channel model
High frequency (>6GHz) specific feature design

## Slide 6: Summary
Highly flexible and capable 5G system is required to fulfill all diverse requirements for usage scenarios envisaged for 2020 and beyond.
A new RAT needs to be specified in 3GPP to fulfill all IMT-2020 requirements.
Study item to target all IMT-2020 requirements.
5G new RAT shall apply at both low and high frequency band. However low frequency has higher priority.
Phased WIs will be accomplished in Rel-15 and 16, respectively.
  Rel-15 (to 2018.09): Phase 1 specification, fundamental features of new RAT, both eMBB and IoT at sub 6GHz, with priorities to be set at launch of WI.
  Rel-16 (to 2019.12): Phase 2 specification, covering all scenarios and bands, fulfilling all IMT-2020 requirements.

## Slide 7: Thank You
3GPP RAN workshop on 5G
Phoenix, AZ, USA, September 17-18, 2015.