## Slide 1: SA WG3 Status report for FS_5WWC_Ph2_Sec
Saurabh Khare
Nokia, Nokia Shanghai Bell

## Slide 2
August meeting:
  Add solutions for current key issues KIs.
October meeting:
  Add new KIs and
  Concentrate on solution update and conclusion.
November meeting:
  Add new KIs and
  Concentrate on solution update and conclusion.
January meeting:
  Conclude pending KIs
  Agree on WID draft
  The TR is expected to sent for information.
February meeting:
  Start normative work and Additional conclusion in TR may also be added. Agree on the WID
April and May meeting:
  Normative work
  Conclude KI4. TR is sent for approval.
Aug meeting:
  Complete remaining normative work
Overall plan
FS_5WWC_Ph2_Sec Status

## Slide 3
TR Summary
FS_5WWC_Ph2_Sec Status
Key Issues | Solutions | Solution status
#1: Authentication of AUN3 device behind RG and supporting EAP | Solution #1 EAP_AKA prime based authentication for AUN3 devices Solution #2 EAP base authentication for AUN3 devices behind RG in PLMN Solution #3 EAP base authentication for AUN3 devices behind RG in SNPN Solution #4 EAP base authentication for AUN3 devices behind RG in SNPN by AAA server Solution #9: AUN3 device supporting 5G Key hierarchy (i.e. N5CW) | concluded Solution #2 is used as the basis for PLMN Solution #3 and #4 are used as the basis for SNPN. Solution #9 is used for N5CW device
#2: Security aspect of slice information exposure of N3IWF/TNGF to UE |  | concluded Due to SA2 progress on the issues, there is no normative work needed for this KI
#3: Security aspect of slice information exposure of N3IWF/TNGF | Solution #11: Security of N3IWF/TNGF reallocation | concluded Solution 11 is used for the normative work
Key issue #4: Security aspect of TNAP mobility without full authentication | Solution #5: TNAP mobility solution with rand Solution #6: TNAP mobility solution with count Solution #7: Using Fast BSS Transition for TNAP mobility Solution #8: Security Establishment for TNAP Mobility Solution #10: TNAP mobility solution without full authentication Solution #13: TNAP mobility using modified ERP | Concluded As there is no agreement, then KI is closed without any conclusion.
KI #5: Authentication of UE connecting to RG using NSWO procedure | Solution #12: Authentication of UE connecting to RG by NSWO | concluded Solution 12 is used for the normative work

## Slide 4
General
  TR 33.887 v0.6.0 contains 5 key issues and related 13 solutions.
  All KIs are concluded and closed. However, KI4 is concluded with "no conclusion" because we could not conclude on the solutions.
  Normative work will be completed in Aug meeting.
Dependencies:
  None
FS_5WWC_Ph2_Sec status after SA3#111
UID | Name | Acronym | Rel | WG | Target | Old % | New % | Change or comment
960030 | Study on Security aspects for 5WWC Phase 2 | FS_5WWC_Ph2_Sec | Rel-18 | S3 | May-2023 | 80% | 100% | TR 33.887 is updated for all KIs and solutions, and cleanup is also done.