## Slide 1: Technical aspects of LI for AKMA with Roaming
Input to joint SA3/SA3LI call, Sep 7 2022
Source: NDRE
NOTE: The slides in their present form do not constitute an official, agreed view of SA3LI

## Slide 2: Scenario in scope
HPLMN
VPLMN
AAnF
UE
(outbound roamer from HPLMN)
AF
AKMA-enabled encryption
UPF
UPF
AMF/SEAF
AUSF
NOTE 1: LI-solution for non-roaming case exists in 33.127
NOTE 2: The roaming case with AF in VPLMN believed “straightforward”
NOTE 3: AF could also be in external DN, this is out-of-scope/FFS

## Slide 3: Most relevant requirements (TS 33.126)
R6.4 - 175 CSP provided cryptographic parameters in roaming – When a home CSP’s subscriber is roaming, independently of whether or not the subscriber is an LI Target in the VPLMN, the home CSP shall provide to the visited CSP the means to decrypt user services which are encrypted between the ME and an entity outside the visited CSP and using cryptographic parameters established in the home CSP.
R6.4 - 180 Retroactive Decryption - The CSP shall ensure that the crypto keys, algorithm and parameters delivered to the LEA enable the LEA to decrypt encrypted Target Communications retroactively.
R6.4 - 190 Mid Communication Interception - The CSP shall retain sufficient key material for the duration of any communications such that it is possible to decrypt already on going communications, when using CSP provided or managed encryption.
R6.6 - 50 Undetectability across CSPs - The CSP shall be able to perform interception such that no CSP not obligated by the warrant can detect that interception is taking place.

## Slide 4: Implications on information & functionality
”cryptographic parameters” , ”means to decrypt” needs to comprise:
  Selected encryption algorithms / cipher suite
  All inputs to encryption algorithms: key(s), nonce(s), counter(s), etc
”undetectability across CSPs” + ”retroactive decryption” 
  The parameters have to be provided from HPLMN always and for all outbound roamers (regardless of whether they are LI Targets in HPLMN or not)
”undetectability across CSPs” + ”mid communication intercept” 
  crypto parameters needs to be provided as soon as the AKMA context is established
Last but not least: The AKMA roaming architecture should define a ”point of decryption” in the VPLMN (e.g. a ”middlebox” in a UPF)

## Slide 5: Implications on interface usage
We wish to avoid interfaces between LI domains of two different CSPs as it jeopardizes security/undetecability across CSPs/jurisdictions
Therefore, the transfer of ”cryptographic parameters” should to be integrated into a normal signaling (SBI) interface between HPLMN and VPLMN
  Potential idea: transfer keys/parameters from one of {AUSF, AAnF, AF} in HPLMN to AMF/SEAF in VPLMN
  The SEAF can then provide the parameters to the VPLMN ”point of decryption”

## Slide 6: Final aspects
Some of the crypto parameters may only be known at AF
  E.g. nonce, selected cipher suite, etc
Standard TLS cipher suites might include Diffie-Hellman derived key material, so AKMA-specific keys only might be insufficient
  Provide all necessary key material or simply avoid DH cipher suites