## Slide 1
Source: China Unicom
China Unicom view on SA5 Rel-20 5G-Advanced Priorities

## Slide 2: TU allocation portion
Since 6G requirements have not been clearly defined, China Unicom’s opinion on TU allocation portion of 5GA part/6G part in Rel-20:
  2/3 TU for 5GA
  1/3 TU for 6G

## Slide 3: Overall View on Rel-20 Topics
No. | Use cases | Brief Descriptions | Related Specs /WIs
1 | Management of AIoT | New management architecture and functions of A-loT Enhancements on management aspects of A-loT Business level requirements for OAM&P of A-loT | TS 28.541/TS 28.552 /TS28.554/New TS
2 | Management of Network Sharing Phase 4 | Enhance IOCs to support plmn-granularity measurements Potential enhancements to support management of shared satellite NG-RAN Potential enhancements to support management of INS utilizing in disaster scenarios | TS 22.261/TS 23.501
3 | Management of ISAC | Enhancements to support management of Sensing function Enhancements to support management of Sensing data Enhancing management mechanism with Sensing | TS 22.261/TS 23.501
4 | Knowledge-assisted management | 1. Knowledge representation 2. Knowledge-assisted closed loop & intent management 3. Explainable AI/ML | 
5 | Trace-based User-level measurement | Investigation on trace as new data source in NG RAN Introduction on trace-based UE level measurements Enhancements on existing UE-level measurements | TS 28.558/TS 28.550
6 | NTN managements | Further enhancement on existing UCs Management support for service continuity and different services with multi-orbit satellites Management support for Broadcast services with satellite access | 

## Slide 4: Use Case 1: Management of Ambient IoT
Background：
Ambient IoT (A-IoT) aims to provide complexity and power consumption significantly lower than the existing 3GPP IoT technologies (e.g. NB-IoT and eMTC) for supporting higher local device density in the order of magnitude.
RAN WGs has investigated RAN level solutions for Ambient loT in TR 38.769 and new WID on Rel-19 Ambient loT was approved in RP- 243326.
SA1 has finished some standardization of Ambient IoT in TR 22.840 and TS 22.369.
SA2 has studied to investigate solutions for architectures to support Ambient IoT in TR 23.700-13.
Potential Objectives:
New management architecture and functions for A-IoT
  AloT RAN：Network element management functions of common reader function and AIoT RAN node function for topology 1.
  AloT CN：Network element management function of AIoTF.
Business level requirements for OAM&P of A-IoT
  Management support for A-IoT consumers, including interface configuration, relevant data collection.
  Management capabilities exposure to A-IoT consumers: upper Layer functions (e.g. Inventory, Command).
  Management of Topology and Workflows for Common Reader Function and A-IoT RAN Node Function.

## Slide 5: Use Case 2: Management of Network Sharing Ph4
Potential enhancements to support management of shared satellite NG-RAN
Investigate potential network sharing management architecture enhancements
Investigate potential management enhancements to enable plmn-granularity configurations for different deployment scenarios of satellites
Investigate potential CN configuration enhancements to support using INS to share NG-RAN
Potential enhancements to support management of INS utilizing in disaster scenarios
Management architecture enhancements to support sending disaster notice to POP by OAM.
Potential configuration enhancements in the scenarios NG-RAN , NFs of 5GC or the whole 5GC with the disaster condition. Possible disaster scenarios are depicted as follows:
Potential enhancements to support management of identifying INS case
Investigate potential management enhancements to configure AMF/UDM/SMF/PCF to identify whether it is the Indirect Network Sharing case or other home routing cases.
Only NG-RAN is broken
NG-RAN and part of NFs are broken
NG-RAN and 5GC are broken
3GPP Management System

## Slide 6: Use Case 3: Management of ISAC
Enhancements to support management of Integrated Sensing and Communication
Investigate potential management architecture
Investigate potential IOCs、measurements、KPIs related to ISAC
Investigate potential configurations and policy mangement for ISAC
Categories | KPI | Descriptions
Estimation | Accuracy of Positioning Estimate | Describes the closeness of the measured sensing result (i.e., position) of the target object to its true position value.
 | Accuracy of Velocity Estimate | Describes the closeness of the measured sensing result (i.e., velocity) of the target object to its true velocity.
Sensing | Confidence Level | Describes the percentage of all possible measured sensing results that can be expected to include the true sensing result considering the accuracy
 | Sensing Resolution | Describes the minimum difference in the measured magnitude of target objects (e.g., range, velocity) that allows detecting objects of different magnitudes.
Detection | Missed Detection Probability | Describes the conditional probability of not detecting the presence of a target object/environment when the target object/environment is present.
 | False Alarm Probability | Describes the conditional probability of falsely detecting the presence of a target object/environment when the target object/environment is not present.
Common | Max Sensing Service Latency | Time elapsed between the event triggering the determination of the sensing result and the availability of the sensing result at the sensing system interface.
 | Refreshing Rate | Rate at which the sensing result is generated by the sensing system. It is the inverse of the time elapsed between two successive sensing results

## Slide 7: Use Case 4: Knowledge-assisted Management
    Knowledge representation: Knowledge management function provides a unified representation and query approach to make optimization expertise characterized as highly-fragmentation and hardly-reused flexible to access.
    Knowledge-assisted closed loop: Knowledge management function gets involved instead of experts to increase the automation efficiency.
    Explainable AI/ML: Knowledge management function provides experts with explainable human-friendly intelligence.
Existing automated optimization(human involved any time especially in decision)
Analytics
Execution
Observation
Decision
Data
MNO experts
Enhanced automated optimization(Knowledge management function involved instead of human)
Analytics
Execution
Observation
Reason
Data
Extract (Explicit knowledge)
Decision
Knowledge(Tacit knowledge
    Potential Capabilities:
      OA&M knowledge management function
      Unified knowledge representation
      Knowledge collection, storage and query interfaces
      Knowledge services for automated reason and decision
OA&M knowledge management function
Knowledge extraction
Knowledge storage
Knowledge representation
Knowledge reason
Query interfaces
evolve
MNO experts
Input expertise as knowledge
Query&reuse knowledge
undefined
    Reference
      [1]TMF IG1130F “SDN/NFV impacts on TAM Knowledge Management”
      [2]TMF IG1190E “AIOps Knowledge Management ”
      [3]ETSI GR ENI 031 “Construction and application of fault maintenance network knowledge graphs.”
      [4]ITU-T SG2/Q6 M.fkmtom“Framework of knowledge management for telecom operation and management”

## Slide 8: Use Case 5: Trace-based UE-level measurements for NG-RAN
SA5: TS 28.558 specifies the UE-level measurements for 5G system, and the corresponding collection and reporting mechanisms.
Background
RAN- support AI/ML enabled NG-RAN: AI/ML function can analyze metrics related to UE level performance related to perform optimal resource management and mobility decisions for network slicing.(TR 38.743、TR 38.744)
SA2- support analytics conducted by NWDAF: Packet delay between PSA UPF and UE, and packet delay in NG-RAN for a specific UE.（S5-233839）
Potential objectives
Investigate the feasibility of introducing Trace mechanism on data collection and reporting for NG-RAN UE-level measurements
Investigate new Trace-based UE-level measurements for NG-RAN
Potential enhancements on existing UE-level measurements in the aspets of measurement object and UE identifier
MDT triggered by event is supported by measurement of M1-M9.
Trace has the capability to log data on any interface at call level for a specific user or mobile type
Research status
Measurement object and UE identifier need to be clear.
Existing UE-level measurements for NG-RAN is limited. Some analysis requirements such as mobility cannot be satisfied in NG-RAN.

## Slide 9: Use Case 5: Trace-based UE-level measurements for NG-RAN
SA5: TS 28.558 specifies the UE-level measurements for 5G system, and the corresponding collection and reporting mechanisms.
Background
RAN- support AI/ML enabled NG-RAN: AI/ML function can analyze metrics related to UE level performance related to perform optimal resource management and mobility decisions for network slicing.(TR 38.743、TR 38.744)
SA2- support analytics conducted by NWDAF: Packet delay between PSA UPF and UE, and packet delay in NG-RAN for a specific UE.（S5-233839）
Potential objectives
Investigate the feasibility of introducing Trace mechanism on data collection and reporting for NG-RAN UE-level measurements
Investigate new Trace-based UE-level measurements for NG-RAN
Potential enhancements on existing UE-level measurements in the aspets of measurement object and UE identifier
MDT triggered by event is supported by measurement of M1-M9.
Trace has the capability to log data on any interface at call level for a specific user or mobile type
Research status
Measurement object and UE identifier need to be clear.
Existing UE-level measurements for NG-RAN is limited. Some analysis requirements such as mobility cannot be satisfied in NG-RAN.

## Slide 10: Use Case 5: NTN Management(OAM_NTN_Ph3)
NTN management enhancements on transparent mode and regenerative mode with gNB/eNB &5GS functions on-board the NTN
  Further enhancement on existing UCs
    Management of connections and associations between satellite and ground systems
    NTN mobility management enhancement
    Management support of Store and Forward Satellite operation
    UE-Satellite-UE communication
    Energy efficiency on satellite access system
  Management support for service continuity and different services with multi-orbit satellites
  Management support for Broadcast services with satellite access
Maybe other management requirements will be added depending on RAN and SA2 groups.
Example of service continuity through multi-orbit satellite access

## Slide 11: Thank You !