## Slide 1
Source: NTT DOCOMO, INC.
NTT DOCOMO view
on SA5 Rel-20 5G-Advanced Priorities

## Slide 2: NTT DOCOMO view summary on SA5 Rel-20
Potential topics and directions
  Intent enhancement, NDT enhancement, AIML enhancement, CMO enhancement, CCL enhancement, EE enhancement, Femto SON
TU allocation portion of 5GA part/6G part in Rel-20
  We think that the time allocations for 5GA part and 6G part should be 30% and 70%. Because there is a lot to discuss regarding the topics related to 6G.

## Slide 3: #1 Intent enhancement
Directions
  Clarify the relationship with other similar technologies (e.g. CCL, AI/ML, Policy, RIC)
    Which system should be connected to which system based on which concept?
  Add intent routing controlling
    Intent routing refers to the process of handling an intent through IDMS(s) other than the one originally submitted by the intent owner.
    As specified in TS 28.312 Clause 4.2.3, an IDMS can be consumer of another IDMS, which enables intent routing.
    There is a need to enable controlling intent routing to other IDMSs as this may lead to undesired impacts on other domains, such as increased costs.

## Slide 4: #1 Intent enhancement
Directions
  Add Expectation for IDMS of AIML
    Consumer can express high level requirements of an AIML model (i.e. accuracy, energy consumption) and IDMS can interact with AIML mgmt. of TS 28.105, TR 28.858 (ML Training MnS, etc.)
    IDMS can provide feasibility report, fulfilment report as well as any conflict report for AIML model expectation.
  Add resilient intent concept
    Resilient intent is the medium to long-term intent.
    Resilient intent helps with medium to long-term resource changes and planning.
    Resilient intent does not interfere with normal intent behavior
  Conflicts handling and resolution regarding automation functions

## Slide 5: #2 Network Digital Twin enhancement
Directions
  Use Network Digital Twin to support autonomous network and provide additional value with exposing mobile network data and using external data
  Data collection
    Standardize mechanism (use existing mechanism/new mechanism) and data format/attributes for data collection to Network Digital Twin from following:
      RAN/Core/UE
      Transport network
      Cloud (collaboration with ETSI NFV)
  Data exposure
    Expose simulation/emulation result data to outside of 3GPP network
    Expose collected data to outside of 3GPP network

## Slide 6: #3 AIML enhancement
Directions
  Further development of AIML which is currently under consideration
    AI sustainability
      AIML energy efficiency
        Control mechanisms of associated energy consumption/carbon emissions, such as those incurred in training and inference phases.
        Computation and/or collection of energy consumption information of ML Training and ML Inference
    Data transaction
  Add use and management of Generative AI
    There is a need for training data generation/ enhancement using Generative AI for specific ML context as training data is a backbone of AIML to achieve certain accuracy/ precision.

## Slide 7: #4 CMO enhancement
Directions
  Finalize TR 28.869
    Address the concerns documented in S5-246790 DP on CMO blocking points and how to move forward.
    Based on the progress of WT-1 and WT-2 analyse the borderline and touchpoints between the 3GPP management system and the external orchestration and management systems for the case of cloud-native environments for both 4G and 5G deployments
      For example analyse if specs like TS 28.533, TS 28.531, TS 28.510, TS 28.511, TS 28.512, TS 28.513 need to be updated
  Based on TR 28.869 work, consider both WT-1 and WT-2 in the WID for Release 20
  Fulfil the gap between cloud-native OAM and telecom operations
    Example target operations: software management, heartbeat monitoring, access control
    Investigate how to connect the 3GPP management system with external orchestration, management and operations systems.

## Slide 8: #5 CCL enhancement
Directions
  Enhance coordination CCLs with other management functions
    Rel-19 only focused on coordination CCLs with other management functions for execution but coordination should be done for other functional stages of CCL (i.e. data collection, analytics, making decisions)
  CCLs to support lifecycle management aspects of NFs.

## Slide 9: #6 Energy efficiency enhancement
Directions
  Enhance the collection of energy-related metrics and enable the optimization of the number of instances and overall energy usage, through collaboration with ETSI NFV and O-RAN
  RAN/Core Management to save energy
    Changing power states of the RAN/Core nodes.
    Optimization of management system functionalities, procedures and distribution to save energy such as being able to activate/de-activate management services upon energy consumption policies/requirements
  RAN/Core Management to use more renewable energy

## Slide 10: #7 Management and SON for 5G Femto
Directions
  Add Management and SON for Femto
    There is no management and SON specification for 5G Femto
    Consider requirements and specification such as 5.1.1 Configuration Management, 5.1.2 Performance Management, 5.1.3 Fault Management and 5.1.4 Security Management in TS 32.581

## Slide 11: Thank You !