## Slide 1
Automotive Requirements for Non-Terrestrial Network (NTN) Enhancements for Release 19

## Slide 2: Background and Summary
5GAA provided their input to the 3GPP RAN-19 WS in June [RWS-230164]
Further discussions on a dedicated automotive NTN UE type with optimized characteristics have been performed in the meantime
  Enabling improved DL and UL throughput due to higher antenna gain and higher UE Tx Power compared to current releases
5GAA also reviewed current potential objectives for the Rel-19 NR NTN WI (based on the moderator’s summary from RAN#101 in RP-232610) and discussed objectives of highest importance for 5GAA
  Further improvements for mobility between TN and NTN are of highest importance for 5GAA (depending on final Rel-18 outcome)

## Slide 3: 5GAA proposal for additional automotive NR NTN UE types
S-/L- Band: at LEO-600
For DL:
NF = 7 dB
Max. Gain, boresight of main lobe = 0 and 3 dBi
For UL:
Tx power: PC3 (23 dBm) and PC2 (26 dBm)
Max. Gain, boresight of main lobe = 0 and 3 dBi
Ka- Band: Flat antenna with beamforming has been considered, different from VSAT, assuming a new satellite EIRP density of 16 dBW/MHz at LEO-600; UE antenna temperature 150 K.
For DL:
NF = 4 and 6 dB
Min. Gain and Max. Gain, boresight of main lobe = 25 and 31 dBi
For UL:
Tx power：37 dBm and 38.5 dBm
Min. Gain and Max. Gain, boresight of main lobe = 25 and 31 dBi
Min. EIRP and Max. EIRP, boresight of main lobe = 32dBW and 39.5 dBW
5GAA kindly request 3GPP to perform relevant analysis (according to the methodology used for creation of 3GPP TR 38.821) and required normative work to enable these additional automotive NR NTN UE types as part of Rel-19. For constellations other than LEO-600, appropriate compensation for satellite EIRP density is to be accounted for.
Recommendations to 3GPP:
Notes: To consider DL and UL gain

## Slide 4: 5GAA review on potential NR NTN objectives for Rel-19 after RAN#101 (based on moderator’s summary in RP-232610)
5GAA automotive use cases require seamless mobility between TN and NTN (as already indicated in RWS-230164)
5GAA kindly requests 3GPP to consider further mobility enhancements to enable seamless mobility between TN and NTN as part of Rel-19.
Recommendations to 3GPP: