## Slide 1: Way Forward to the Working Agreement from CT1#152 5G Steering of Roaming (SOR-CMCI)
NTT DOCOMO, Telefonica, BT, KDDI, Vodafone, KT, NTT, SKY Perfect JSAT Corporation, Softbank, Telecom Italia, SK Telecom, Telstra, STC.

## Slide 2: [Intro] What is SoR and its importance for MNOs
Steering of Roaming (SoR):
  A mechanism for HPLMN to ensure roaming UEs are directed to a preferred VPLMN
SoR is used by HPLMN:
when HPLMN and VPLMN are from :
  The same Group Operator Company or from Operator Alliance
to guide UEs to operators with Reasonable inter-operator tariff negotiated between the H/VPLMN
to Back off UEs from operators with Unreasonable inter-operator tariff between H/VPLMN
  i.e. relationship established for backup purpose only
HPLMN
VPLMN 1
VPLMN 2
VPLMN 3
5GC introduced CP-SOR and eCPSOR-CON in Rel15 and Rel16 allowing SoR to be performed precisely during and after initial registration.
(legacy solutions in 4G or earlier were with proprietary and negative user experience (e.g. delayed attach to VPLMN))

## Slide 3: [Intro] What is Rel-17 SOR-CMCI, why required
SOR-CMCI
  Moves UEs to higher priority PLMN in connected mode to improve effectiveness
  SoR in connected mode is important, because most UEs on 5G are in connected mode
The most important is EFFECTIVENESS
HPLMN sometimes needs to move all UE to a different PLMN with immediate effect,
to evade catastrophic User experience and business (charging) impacts, etc..
HPLMN
VPLMN 1
VPLMN 2
VPLMN 3
New policy
SOR-CMCI
information
HPLMN
VPLMN 2
VPLMN 3
VPLMN 1
CP-SOR
Information during registration
Initially
SOR-CMCI is used by HPLMN:
during Inter-Operator Tariff negotiation
  withdraw all UEs from registered VPLMN to give pressure among roaming coordinators…
when Technology / user experience issues are found in VPLMN
when severe disruption happens in VPLMN
etc, etc…
Change of policy

## Slide 4: GSMA Requirements
  GSMA already has the following requirement in IR.73 v10 (current)
  GSMA Requirement :
  It is mandatory for the UE to support the SOR-CMCI. The support and offer of SOR-CMCI by the home operator is based on its policy

## Slide 5: Working Agreement from CT1 (Nov 2024)
Rel-17 Agreement: | Mandatory UE support of SOR-CMCI to ensure effectiveness
Latest CT1 discussion: | Optional UE support of SOR-CMCI Show of hands was conducted and the optionality of UE support of SOR-CMCI was agreed as working agreement
Issues:
[3GPP perspective] : Working agreement contradicts to GSMA requirements
  Agreement taken with NO PRIOR consulting with GSMA
[MNO’s business perspective] MNOs will lose access to effective SoR in connected mode solution for 5GC Roaming
  Demotivates even more the global deployment of 5G Roaming, let alone the roaming hub/VAS ...
WAY FORWARD: Send LS to GSMA to confirm requirements,
before approving CT1 CRs

## Slide 6: Observations and concerns
It is not (good) common practice at 3GPP to approve major changes to the specification with “FASMO” CRs in deeply frozen release.
If we open the door to removing things or making significant changes from deep frozen releases because some companies have not implemented them or not interested in it or whatever. That would not be good for the ecosystem of the industry (3GPP) and could lead to market fragmentations.
The 3GPP leadership should be stricter when it comes to allowing “FASMO” implementations (especially CRs that propose significant changes) in deeply frozen releases.

## Slide 7: (Annex) Discussion in CT1 #152 (Nov 2024)
Proposal in CT1#152 to make support of SOR-CMCI optional in the UE from Rel-17 onwards.
  CRs discussed:
      (Stage2) C1-246694/TS23.122-Making SOR-CMCI support optional for UE (Rel-17)
        C1-246210 (Rel-18 Mirror), C1-246211 (Rel-19 Mirror)
      (Stage3) C1-246212/TS24.501-Making SOR-CMCI support optional for UE (Rel-17)
        C1-246213 (Rel-18 Mirror), C1-246215 (Rel-19 Mirror)
    Co-signing companies:
      Huawei, HiSilicon, Qualcomm Incorporated, LG Electronics, Samsung, MediaTek Inc., OPPO, vivo, Apple, InterDigital, China Telecom, Xiaomi, Google, CATT, TD Tech, Lenovo.
    Opposing companies:
      NTT DOCOMO, NTT, KDDI, Ericsson and NEC
  Discussion:
    Questions whether these CRs (i.e. CRs C1-246694, 6212 and the corresponding mirrors) are FASMO.
    Compromised proposed:
      (Alt1) Solution to reduce the number of rules where UE shall support minimum of Two rules. Also some additional reduction to use one timer for IMS voice call and IMS video.
        CRs C1-246395, C1-246397, C1-246399/ 23.122 and C1-246401, C1-246403, C1-246404/24.501.
        During show of hands, this solution was opposed by 8 companies, and supported by 3 companies.
      (Alt2) Another simplified solution was proposed during the meeting, to make it mandatory for the UE to support IMS voice call, IMS video call and match all criteria and all other rules are optionally supported by the UE.
        The CRs were provided in C1-246695 - C1-246697/23.122 and C1-246698-C1-246700/24.501 that was also co-signed by Ericsson in addition to NTT DOCOMO, NTT and KDDI.
        During show of hands, this proposal was objected by 14 companies, and supported by 4 companies.
  Conclusion:
    CRs (6694, 6212) are taken as the working agreement.

## Slide 8: (Annex) GSMA requirements in IR.73
  9.3 Security mechanisms for Steering of Roaming in 5GS
The necessary security functions to support the CP-SOR in the 5GS are defined in 3GPP TS 33.501, section 6.14 (Rel 15) [16]. Mechanisms to ensure message security and integrity have been developed and can be found in 3GPP TS 31.115 Rel. 15 [19].
  9.4 Steering of roaming control information (SOR-CMCI):
Additional requirements specific for CP-SOR were introduced in Rel-17 allowing the home operator to control the timing to when a roaming user's equipment (UE) registered on an operator's network (VPMN), in automatic network selection mode and currently in CONNECTED mode, enters IDLE mode and initiates higher priority network operator selection (PLMN selection) by taking into consideration the type of the ongoing communication in the UE.
As such, Rel. 17 CP-SOR enhancement introduces means to send additional steering of roaming information, called Steering of Roaming Connected Mode Control Information (SOR-CMCI) that carries information to control the timing for a roaming UE in connected mode to when it moves to IDLE mode to perform the steering of roaming, taking into consideration the ongoing communication / session(s).
SOR-CMCI consists of SOR-CMCI rules. Each SOR-CMCI rule consists of the following parameters (see 3GPP TS 23.122 Annex C [11]):
1. a criterion of one of the following types:
Packet Data Unit (PDU) session attribute type criterion includes the type of session attributes, slice type, data network to connect to.
Service type criterion includes the type of service voice, video, short message service.
SOR security check criterion, covering the condition if security check of the SOR-info fails at the UE.
Match all type criterion, where the UE has any PDU sessions or services for which there is no matching criterion defined in the SOR-CMCI.
2. a value for SOR-CMCI criteria timer associated with each criterion presented in i) indicating the time the UE shall wait before releasing the PDU sessions or the services and entering IDLE mode to perform SOR.
The high priority services and emergency services are exempted from being interrupted (i.e. this feature is not applicable).
It is mandatory for the UE to support the SOR-CMCI. The support and offer of SOR-CMCI by the home operator is based on its policy.
For more details see 3GPP TS 23.122 Annex C [11].
Note: The operator (HPMN) deploying CP-SOR can enforce the interruption of the ongoing sessions in the UE to perform SOR based on specific criteria provided in the SOR-CMCI. Also, the UE can send information back to the HPMN over the SOR-ACK (SOR-information container), for more details see 3GPP TS 23.122 Annex C [11] and 3GPP TS 24.501 [12], that cannot be fulfilled in the rejection based SOR. Using CP-SOR or rejection based SOR are mutually excluded, and thus it is up to the operator to select the appropriate solution for its operation.

## Slide 9: (Annex) Stage1 requirements in TS 22.261
Described in clause 6.30.2 of TS 22.261
6.30 Steering of roaming
6.30.1 Description
Steering of roaming allows the HPLMN (or subscribed NPN) to steer a UE to a VPLMN or NPN on which the HPLMN (or subscribed NPN) wants the UE to register, when the UE registers on another VPLMN or NPN. This capability can be needed for reasons e.g. reselection to a higher priority PLMN, or NPNs, based on business arrangements.
6.30.2 Requirements
The following set of requirements complement the requirements listed in 3GPP TS 22.011 [3], clause 3.2.2.8.
The 5G system shall support a mechanism for the HPLMN to control the timing when a UE registered on a VPLMN, in automatic mode (see clause 3.1 of TS 23.122 [25]) and currently in CONNECTED mode, enters IDLE mode and initiates higher priority PLMN selection based on the type of ongoing communication.
NOTE 1: Changes needed to support the above requirement are expected to have minimum impact on the 5G system. UE is expected to initiate the above-mentioned PLMN selection e.g. by locally releasing the established N1 NAS signalling connection.
NOTE 1a: The requirement above applies also to the case of a UE registered to a non-subscribed (standalone) NPN, in order to select a higher priority PLMN or NPN.
The UE shall be able to delay conforming to steering of roaming control information from the HPLMN while it is engaged in priority service (e.g. emergency call, MPS session), or a service defined by HPLMN policy not to be interrupted (e.g. MMTEL voice/video call).
NOTE 2: The HPLMN policy can take into account the user's preference for the service(s) not to be interrupted. User preferences can be communicated utilizing non-standard operator-specific mechanisms, e.g. web-based.
The mechanism mentioned above in this clause shall be available to the HPLMN even if the VPLMN the UE is registered on is compliant to an earlier release of the 5G system.
The 5G system shall support mechanisms to enable a credentials holder (e.g. HPLMN or subscribed standalone NPN) to send steering of roaming information to a UE for selecting standalone NPNs (e.g prioritized list of preferred NPNs).
1 Scope
The present document describes the service and operational requirements for a 5G system, including a UE, NG-RAN, and 5G Core network. Requirements for a 5G E-UTRA-NR Dual Connectivity in E-UTRAN connected to EPC are found in TS 22.278 [5].