## Slide 1
Packet priority-based access control for
Rel-20 5G-Advanced
RP-242589
3GPP TSG RAN #106
Madrid, Spain, 9th - 12th, Dec. 2024
Agenda item: 15.2
Source : SK Telecom, LG Uplus

## Slide 2
Introduction
In congestion situation (e.g., subway station during rush hour), user’s quality of experience (QoE) is very poor (e.g., more than 3 sec for web page loading) due to RRC connection failure rate increases
  For example, RRC connection success rate is decreased from 99.9% to 96% when around 500 users in a cell.
  Also, in subway station during rush hour, SK telecom’s own ‘web QoE success (=download 4.5Mbyte within 3 seconds) rate indicator’ is decreased from >99% to 87% with around 160 users in a cell.
From our analysis using test UE, RRC connection attempts for data services can be classified into two types, foreground (UE screen on) and background (UE screen off), depending on the Active ↔ Idle switching pattern.
  If there is a regular pattern in RRC connected ↔ RRC idle switching, it can be assumed that it originated from the background App.
  From our estimation with above assumption, quite large portion of RRC attempts seem to be originated from the background App (i.e., 30~40% of total RRC connection attempt in busy hour)
However, existing access control mechanism does not support access control based on packet priority from same App. So, we strongly believe that ‘Packet Priority based Access Control’ is needed to be discussed and specified in Rel-20 5G-Advanced.
  Existing access control mechanism such as UAC(Unified Access Control) and ACDC(Application specific Congestion control for Data Communication) support access barring based on ‘access ID’ or ‘application category'. but they do not support access barring that separates ‘packet priority’ from same App depend on user’s activity (e.g., UE screen on/off).
  Rel-20 is the final release before 6G normative work. So, we should focus on the feature to resolve pain points in commercial networks.

## Slide 3
Discussion
In congestion situation (e.g., subway station during rush hour), user’s quality of experience (QoE) is very poor (e.g., more than 3 sec for web page loading) due to RRC connection failure rate increases
RRC connected UE and RRC connection success rate
Observation 1
For example, RRC connection success rate is decreased from 99.9% to 96% when the number of RRC UE suddenly increases upto 500 users in a cell. It severely degrade our customer’s QoE
Number of RACH attempts and RACH success rate
RRC Connected
User
RRC connection
success rate
Num.of RACH
Attempts
RACH success
rate
Also, in subway station during rush hour, SK telecom’s own ‘web QoE success (=download 4.5Mbyte within 3 seconds) rate indicator’ is decreased from >99% to 87% with around 160 users in a cell.

## Slide 4
Discussion
From our analysis using test UE, RRC connection attempts for data services can be classified into two types, foreground (UE screen on) and background (UE screen off), depending on the Active ↔ Idle switching pattern
RRC Connected ↔ RRC Idle switching pattern according to UE screen on/off (test UE)
Observation 2
Screen On
(User active packet / Passive packet)
Avg. Idle time
Avg. Connection
time
Screen Off
Screen On
Screen Off
(Passive packet)
RRC conn.
(LTE)
RRC Idle
RRC conn.
(NR)
RRC Idle
RRC conn.
(LTE)
When UE screen is on, it has no pattern and seem to be random. (i.e., it depends on actual usage pattern of customer)
When UE screen is off, it has a regular pattern: RRC Connected: 11~15 sec → RRC Idle: around 50 sec → RRC Connected (for test UE)

## Slide 5
Discussion
Quite large portion of RRC attempts seem to be originated from the background app (i.e., from UE with screen off). However, existing access control mechanism does not support access control based on packet priority
Estimation of the ratio of RRC connection attempt originated from the background app in commercial network
Observation 3
For example, RRC connection success rate is decreased from 99.9% to 96% when the number of RRC UE suddenly increases upto 500 users in a cell. It severely degrade our customer’s QoE
[Basic] Access Barring supporting separates ‘voice’ and ‘data' calls
Also, below two conditions are met, we consider that this RRC connection attempt is originated from the background app.
  The RRC Idle state is maintained for longer than 30 seconds before start to switch to RRC Connected state.
  And switch back to RRC Idle state within 15 seconds.
Time | 5G/LTE | Ratio of RRC Connection Attempt | 
 |  | Estimated to be screen off (~Background App, Passive Packet) | Estimated to be screen on (~Foreground App, Active Packet)
Low Load (4 am) | 5G | 56% | 44%
 | LTE | 63% | 37%
Busy Hour (18 pm) | 5G | 28% | 72%
 | LTE | 37% | 63%
[Rel13 ACDC] Access Barring supporting separates ‘application ID’
Voice
Data
[SIB2]
ac-BarringForMO-Data (50%)
App
Category 1
[SIB2]
BarringPerACDC-Category-r13 (category 2=50%)
App
Category 2
User active
packet
There is no way to delay for passive call
Passive packet
[Not Support] Access Barring supporting separates
‘packet priority’ form same app
Screen On
Screen Off

## Slide 6
Conclusion
Based on the previous observations, we strongly suggest as following;
Proposal 1: Define a low-priority packet that has no impact on the user experience service quality
  When the screen of user device is off, there is a pattern of RRC connection attempts. However, since most of these packets are not generated through using by the user, they have little impact on the user experience service quality
  Data packets that do not affect the user experience service quality. We propose a definition that can define these data packets as low-priority packets
Proposal 2: Restrict RRC connection attempts considering low priority packets
  gNB transmits the msg. through SIBx., which restricts the attempt to RRC connect by low-priority packets. (probability-based RRC connection attempts). UE device that receives the msg should attempt to connect probably when a predefined low-priority packet occurs
  UE device that receives the SIBx msg should probabilistically attempt to connect when low-priority packet occurs
  When non low-priority packet occurs, UE device attempts to connect without restriction
gNB
UE
SIB signaling
(ex. ac-BarringForLow-PriorityPacket )
Low-priority packet
occurs
Non low-priority packet
occurs, attempt to connect
∙ ∙ ∙
RRC connection attempts
based on probability at SIB msg.
∙ ∙ ∙

## Slide 7
Thank You.