## Slide 1: ETRI’s views on Rel-20 5G-Advanced
Electronics and Telecommunications Research Institute
RP-242774
3GPP TSG RAN Meeting #106
Madrid, Spain, December 9-12, 2024
Source: ETRI
Agenda item: 15.1

## Slide 2: General Considerations on Rel-20 5G-Advanced
The 3rd release of 5G-Advanced and last release before 6G normative work
  Focusing on the completion of 5G-Advanced rather than introducing new one
Considering parallel 6G Study, TUs should be managed carefully
  Prefer more TUs for 6G rather than 5G-Advanced
Continuous essential study on 6G for smooth transition
  Focusing on the limited items which are related to 6G, however can be easily adopted in 5G-Advanced

## Slide 3: AI/ML Enhancements
Ongoing work item on AI/ML for air interface in Rel-19 is expected to cover limited areas
  Focus on only one-sided model and limited use cases and study two-sided model continuously
Initiate Rel-20 work item on AI/ML for mobility
  RRM measurement prediction, measurement event predictions and RLF prediction based on the study
For completed AI/ML support, at least the followings should be specified
  Two sided model for CSI compression
  AI/ML prediction based handover
AI/ML prediction based handover
Two-sided model for CSI compression
CSI generation (compression)
CSI reconstruction
(decompression)

## Slide 4: MIMO Phase 6
MIMO enhancements in 5G-Advanced are still on progress
  Rel-19 supports UE-initiated/event-driven beam reporting, larger array, and asymmetric UE/TRP
Further reduction of overhead and improvement of performance can be possible with following considerations
  Some of leftovers in Rel-19 and new events (e.g., predictive events) can be considered for beam reporting
    In addition, UE-initiated beam switching can be further considered.
  MU-MIMO enhancements by increasing DM-RS layers (by x2 capacity) with incorporating the large array specified in Rel-19
  More flexible mTRP operations, e.g., sTmR TRP enhancements for non-connected UEs, TRP-level on/off for interference handling, on top of Rel-19 features can be supported.
  Further UL enhancement targeting xTyR UE, e.g., STxMP SDM/SFN enhancements for xTyR UE, on top of Rel-18/-19 features

## Slide 5: Ambient IoT
TR 38.848 “Study on Ambient IoT (Internet of Things) in RAN” has identified 8 use cases
  Rel-19 Ambient IoT is expected to cover indoor scenarios (Inventory & Command)
  Remaining use cases (esp. outdoor) are also important and need to be considered in Rel-20
Need to consider the followings
  Enhancement of A-IoT to support remaining use cases: Outdoor inventory/sensor/command
  Active devices with enhanced capabilities can be considered to increase coverage
  Reduced TUs compare to Rel-19 will be fine since Rel-19 spec can be a baseline
Outdoor Inventory
Outdoor Sensor
Outdoor Command

## Slide 6: Duplex Evolution Phase 2
Ongoing work item for sub-band non-overlapping full duplex (SBFD) in Rel-19 is expected to be concluded with the followings
  Network-side full duplex via semi-static and cell-specific uplink(up to 1)/downlink(up to 2) subbands
For more efficient commercialization of SBFD, the following objectives should be studied or specified in Rel-20
  Study on feasibility of SBFD from UE perspectives
  Study on feasibility of overlapping full duplex from network and/or UE perspectives
  Specify dynamic transition between SBFD and non-SBFD
UL SB
DL SB
DL SB
UL SB
Half duplex at UE side in Rel-19
Full duplex at UE side in Rel-20
DL SB
DL SB
DL SB
DL SB
UL SB
DL SB
DL SB
UL SB
Slot #n
Slot #m
DL SB
DL SB
UL SB
DL SB
DL SB
UL SB
Slot #n
Slot #m
Semi-static SBFD resources in Rel-19
Dynamic SBFD resources in Rel-20

## Slide 7: Non-Terrestrial Networks Phase 4
Motivation for NTN phase 4 specifications
  Fundamental studies are required to enable NTN to everything
  Some of leftovers from NTN phase 1~3 due to limited TUs need to be specified
Potential objectives
  Specify E-UTRA TN to NR NTN mobility for CONNECTED mode UEs
    NTN phase 3 only supports E-UTRA TN to NR NTN mobility for IDLE mode UEs
    Need to avoid unnecessary cell reselection, e.g., via enabling multiple SMTCs
  Study on NTN supports for non-GNSS capable UEs
  Multi-polarization support for NR NTN
    Currently, the network broadcasts the polarization type of satellite (circular or linear)
    Further enhance NTN coverage by satellite-UE polarization alignment
  Leftovers from Rel-19, including further optimization for longer SSB periodicity/hopping

## Slide 8: Network Controlled Repeater Phase 2
Rel-18 NCR supports single beam & single cell operation only
  Only a single access link beam can be allocated for a given NCR-MT cell (across whole operating bands)
  NCR shall select a single access link beam for a given time instance, if multiple beams are indicated
  No specification supports for NCRs covering both of FR1 and FR2
Need to consider the following enhancements for Rel-20 NCR/RIS
  Multi-beam allocation for access link and backhaul/control links
  Multi-carrier operation for NCR
Control link = BH link
A single access link
Rel-18 NCR
Control link ≤ BH link
(enable DC/CA)
Multiple access links
(enable MU / high rank)
Rel-20 NCR/RIS

## Slide 9: Summary
For successful delivery of new/enhanced features in 5G-Advanced and Considering parallel 6G Study, the following items should have 1st priority in Rel-20 NR
  AI/ML Phase 2
  MIMO Phase 6
  Ambient IoT Phase 2
  Duplex Evolution Phase 2
  Non-Terrestrial Networks Phase 4
  Network Controlled Repeater Phase 2
Other items can be also considered with 2nd priority
  NES enhancements: on-demand SIB1 (single cell operation)
  Coverage enhancements: multi-beam PRACH repetition, Msg5 PUSCH repetition