## Slide 1: 5G-Advanced Rel-20 - Views and priorities from Satellite community
Novamint, Thales, Inmarsat, Viasat, Ligado, Omnispace, Iridium, Airbus, Gatehouse, SES, Sateliot, Terrestar, Thuraya, TNO, ESA, EchoStar, EDF, PSCE, Softil, Eutelsat Group, Obvios

## Slide 2: Outline
Where we are:
  SA2 5GSAT_Ph3_ARCH almost completed in Release 19. Main topics covered were:
    Regenerative Payload
    Store and Forward Satellite operation
    UE-Satellite-UE communication
  for Release 20, SA1 FS_5GSAT phase 4 has addressed the following: :
    new capabilities such as:
      multi-orbit satellite access for multiple services
      resilient notification service
    Enhancements of the following aspects:
      support for emergency communications and mission critical services using satellite access
      support IMS voice calls using GEO satellite access
      support Broadcast services with satellite access for unregistered UEs
What is expected:
  The next slides are listing the candidate features for R20 SA2 5GSAT_Ph4_ARCH as well as other topics representing the views from the satellite community

## Slide 3: Overall View on Rel-20 5G-A Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Integration of satellite components in the 5G architecture Phase 4 (5GSAT_Ph4_ARCH) (See slides 4 to 8 for more details) | The study aims at investigating on further 3GPP core network functions enhancements to support satellite access based for the new uses cases as introduced in TR 22.887 with the following architectural considerations and tasks: Key Work Tasks includes the following - Multi-Orbit Remaining UE-SAT-UE communication aspects (i.e., MCC & IOPS, non-IMS services) 5GC supporting IoT NTN Resilient Notification Broadcast services via satellite to unregistered UE | Yes, TS 22.261 (TR 22.887) Yes, TS 22.261 (TR 22.887) Yes, TS 22.261 Yes, TS 22.261 (TR 22.887) Yes, TS 22.261 (TR 22.887) | SA2 | Yes, Alignment mostly Yes, Alignment Yes, Alignment Yes, Alignment Yes, Major Yes, Alignment | SA3 for security, SA5 for charging
2. | IMS voice calls using GEO satellite access (See slide 9) | Optimized IMS voice (call setup, transmission overhead) considering the transmission data rate, latency and packet size | Yes, TS 22.261 (TR 22.887) | SA2 | Yes, Alignment | SA4 for codec
3 | Emergency SMS (See slide 10) | SMS to emergency centre over Non-Access Stratum (NAS) for Terrestrial and Satellite access | Yes, TS 22.101 | SA2 | Yes, Alignment | SA3 for security, CT1

## Slide 4: #1.1 Multi-Orbit
Multi-orbit is the key topic for SA1 FS_5GSAT_ph4: 18 use cases of TR 22.887 are related to multi-orbit (out of 24)
A multi-orbit satellite access system in 5G networks leverages satellites in different orbits (GEO, MEO, LEO) to balance their unique advantages and challenges. Among those, we can highlight the benefits in terms of coverage, connectivity, performance, and energy efficiency. With a multi-orbit satellite access system, the following different use cases are expected to be covered:
  Hybrid satellite networks combining LEO, MEO, and GEO services are essential for future satellite communications, especially in maritime and aviation sectors. They support autonomous ships by providing global coverage and seamless connectivity, overcoming LEO constellation rollout challenges with multi-orbit satellite access.
  Mobile base station relays (MBSRs) connected through non-terrestrial networks (NTN) ensure continuous connectivity for UEs. 5G’s multi-dimensional architecture supports various satellites for different services, with multi-orbit switching covering all use cases, especially in isolated and remote areas.
  Different satellite altitudes and movements affect performance. For remote monitoring, devices connect to GEO satellites for resilience and energy savings, switching to LEO for higher capacity and lower latency during data transmission, optimizing connectivity and resource usage.
  GEO satellites, with their wide field of view and longer active duty cycles, efficiently transmit cell broadcast signals over large areas, simplifying cell search and network entry. They bridge coverage gaps caused by NGSO satellites’ power constraints, providing initial access and network registration, before handing over to NGSO satellites for service continuity. This approach ensures seamless connectivity and optimizes the use of satellite resources.
  NGSO satellites offer lower latency and higher capacity but face power and mobility constraints. By intelligently managing connections and power, the system ensures optimal energy and resource efficiency.
  For instance, NGSO satellites can be powered down during low usage, with GEO satellites maintaining coverage. Additionally, devices can initially connect to GEO satellites to avoid frequent NGSO handovers, switching to NGSO only when necessary for data transmission. This approach maximizes the benefits of each orbit type.
Multi-Orbit is the keystone of any future constellations which are 3GPP NR NTN based
A study is proposed to identify the related key issues to support these use cases and solutions to address them
Note: Simultaneous UE connections with multi-orbits are out of scope

## Slide 5: #1.2 Remaining UE-SAT-UE com aspects
Justification
  For UE-SAT-UE communication, only the support of IMS including MCC was addressed in Rel-19.
  UE-SAT-UE communication should support non-IMS services
    e.g. support of VPNs between two UEs or between at least two IOPS (Isolated Operation for Public Safety) is also needed for disaster relief purposes
  In addition, roaming was not supported, with as consequence that only two UEs belonging to the same satellite serviced PLMN can perform IMS communication.
Areas for study:
  Non-IMS data services other than IMS and MCC
  Support of roaming according to the approved Rel-19 architecture and solution.
  1-to-N Communication for Mission Critical.
  Support of UPF only onboard, including support of 5G LAN via satellite access.
  IOPS

## Slide 6: #1.3 5GC supporting IoT-NTN
Justification
  IoT-NTN is supported by EPC only.
  Implementations of integrated NR-NTN and IoT-NTN services provided by one network, highly benefit from harmonizing 5GC support also for IoT-NTN
  Several satellite operators and future constellations are planning new deployment of 3GPP technologies based on NR NTN to support multiple services including IoT
  Therefore, it is important to have 5GC support of IoT to have integrated NR-NTN and IoT-NTN services.
Areas for study:
  specific impacts, if any, on interfaces and protocols of 5GC supporting IoT-NTN (NB-IoT and eMTC)

## Slide 7: #1.4 Resilient Notification
Justification
  The use case of Resilient Notification Service has been studied in SA1 in Rel-20 and consolidated with potential requirements captured in TR 22.887
  The service is to notify users, with valid subscription to the notification service, about a missed mobile terminated service when the user is unreachable via satellite access.
  Need to conduct related SA2 work
Areas for study:
  Study the Resilient Notification Service via NTN (IoT NTN and NR NTN)
  Strong dependency to RAN

## Slide 8: #1.5 Broadcast services via satellite to unregistered UE
Justification
  Current specifications do not support broadcast services to unregistered UEs
  Operators with Legacy fixed VSAT (with legacy broadcast services) could be migrated to UE with only broadcast receiver
  New use cases (e.g. moving platform, direct-to-car …) will have UE with the 2 components (broadcast receiver + independent unicast)
  Operators need this capability for public service and safety related uses such as warning populations before/after natural disasters/catastrophic events. These notifications should be available to all UE, not just registered ones in order to meet public service communications objectives.
  Includes both MSS narrowband services and broadband broadcast services
  Capabilities related to 4G and TV services have been addressed with Free-to-air (FTA) in a 4G context
    but not in the context of 5G system and not taking into account satellite access as such as part of the 5G system
Areas for study:
  Study the support of broadcast services via satellite to unregistered UE

## Slide 9: #2 IMS voice call over GEO
Justification
  The use case of IMS voice call over GEO has been studied in SA1 in Rel-20 and consolidated with potential requirements and KPIs captured in TR 22.887
  Corresponding SA/RAN work in Rel-20 is needed to enable the low data rate (1~3kbps) IMS voice call using GEO satellite.
  In particular, need to improve the IMS service by leveraging NB-IoT (GEO) satellite access (transparent payload) and address the specific architecture enhancements for IMS voice call capabilities in satellite communications.
  This feature may be applicable to UE operating in terrestrial networks that follow a unified design approach.
Areas for study:
  How to enhance QoS policies based on the characteristics of GEO access type (SA2)
  How to optimize the delay of IMS voice call setup (SA2)
  Define a voice codec considering the transmission data rate and latency of GEO satellite access (SA4)

## Slide 10: #3 Emergency SMS
3GPP specifications support Emergency Calls with voice and other media, but this does not include SMS.
Service requirements for SMS to emergency centre have been specified in Rel-18 in clause 10.11 of TS 22.101, but there was no time to specify stage-2 impacts during Rel-18 timeframe and no consensus to find a technically agreeable solution in SA2 in Rel-19.
Objective: to study architectural and procedural enhancements to support Emergency SMS for EPS and 5GS for terrestrial and satellite.
The objectives allow to study solutions for emergency SMS both over IP (using IMS) and over NAS
Work tasks associated:
  Identify network capability for support of Emergency SMS.
  Identifying Emergency SMS based on the use of emergency numbers.
  Identifying the type of emergency service (police, ambulance, fire brigade, etc.) using the same identification methods as for emergency calls.
  Routing of the Emergency SMS to different emergency response centres, depending on the type of emergency, in accordance with national regulations (e.g., to a dedicated SMSC in the country of the UE serving PLMN or to emergency response centre serving the UE location, including in roaming case)
UE in limited service state will be supported in this study item.

## Slide 11: Summary
The key priorities for Rel-20 are the following:
  Integration of satellite components in the 5G architecture Phase 4 (5GSAT_Ph4_ARC) including the following topics:
    Multi-Orbit
    Remaining UE-SAT-UE communication aspects
    5GC supporting IoT NTN
    Resilient Notification
    Broadcast services via satellite to unregistered UE
  IMS voice calls using GEO satellite access
  Emergency SMS for both terrestrial and satellite access
These priorities are motivated by the following considerations:
  key capability needed to support commercial deployments
  evolutions of the satellite access including future constellations who are committed to 3GPP NR NTN
  new business opportunities/new services