## Slide 1: AI/ML cross-domain coordination aspects
Qualcomm Incorporated

## Slide 2: SA2 status
FS_AIML_CN was approved in SA#102 with a check point for WT#1 (“AI/ML cross-domain coordination aspects”)
  WT1.1 –Study whether and how to support UE data collection to meet requirements for RAN AI support for air interface operation (for RAN) for UE-side model training documented in 3GPP TR 38.843 clause 7.2.1.3.2. This includes identifying what benefit can be achieved from enhanced UE data collection in 5G System, and the potential impacts on the 5G framework, including potential enhancements to policy control and OAM. The WT will also discuss the possible data leakage from the operator’s domain which should be avoided and the network control over data collection.
  WT1.2 –Study whether (and how) to support model transfer/delivery to the UE according to RAN1/RAN2 considerations documented in 3GPP TR 38.843 clause 7.1.2.4, including potential enhancements to policy control and OAM. Whether and what entities or functions transfer the AI/ML model or information to the UE will be studied as part of the work. This WT will also discuss the possible data leakage from the operator’s domain which should be avoided.
  WT1.3: Study whether and how to support the alignment of model identification and model management between SA2 and RAN. Work will be based on the possible requirements defined by RAN1 and RAN2 considering the conclusions in 3GPP TR 38.843.
NOTE 2: Whether SA2 can start work on WT 1.1, 1.2 and 1.3 will be discussed at SA#105 (Sep. 2024) based on the outcome of the related work in the involved RAN WGs(s). Further change in description of WT 1.1, 1.2, 1.3 can be discussed at SA#105.

## Slide 3: RAN status
In RAN2 agreed under FS_NR_AIML_Air in R2-2407807, which includes the RAN2 status of data collection for UE-side model training.
  For Data collection for UE-side model training, four solutions were discussed and analysed the potential spec impact with different metrics. See the table in next slide.
Other aspects in TR 38.843 may have impacts in ongoing work for AI/ML in TSG SA

## Slide 4: Analysis of different data collection options for UE-side model training
Options | Option 1a) | Option 1b) | Option 2 | Option 3
First termination entity | Training entity (e.g., Over-The-Top (OTT) server) | Server for data collection for UE-side model training | Inside the CN | Inside OAM domain
AI/ML-specific Data Transfer Path | UE to OTT server via either 3GPP or non-3GPP network | UE ->Server for data collection for UE-side model training/OTT server (Note 4) | UE-> CN -> Server for data collection for UE-side model training/OTT server (Note 4) | UE-> gNB->OAM -> Server for data collection for UE-side model training/OTT server (Note 4)
UP/CP tunnel | UP tunnel (for the case of data transfer from UE to OTT server via 3GPP network) | UP tunnel | CP tunnel (provided that the data volume remains within the NAS signalling capacity) FFS: UP tunnel (Note 7) | CP tunnel (provided that the data volume remains within the RRC signalling capacity) FFS: UP tunnel (Note 7)
Protocol layer for data transfer | Application layer | Application layer | NAS layer for CP tunnel FFS: the protocol layer for UP tunnel | RRC layer for CP tunnel FFS: the protocol layer for UP tunnel
Controllability of MNO on data transfer | No AI/ML specific controllability | FFS: level of controllability (Note 5) (Note 1) | Full controllability (Note 1) | Full controllability (Note 1)
Solution for network controllability | N/A (the OTT server can directly request data from the UE) | Example: per PDU sessions | Via NAS procedure, FFS other procedures | Via RRC procedure
Possible Options for data content visibility in MNO (Note 2, Note 3) | No standardized visibility | FFS on level of visibility (Note 5) | Opt A) Full visibility for standardized data contents. Opt B) Partial visibility for partially standardized data contents. (Note 6) Opt C) No standardized visibility. (Note 6) | Opt A) Full visibility for standardized data contents. Opt B) Partial visibility for partially standardized data contents. (Note 6) Opt C) No standardized visibility. (Note 6)
Impacted WGs | N/A | SA2, SA3, RAN2, RAN3, CT1 | SA2, SA3, RAN3, RAN2, CT1 and CT3 | RAN2, RAN3, SA3, SA5, SA2
Note 1: Full controllability: The MNO can manage data transfer to the server for UE-side data collection, without the need of SLA. This includes initiating, terminating, and fully managing data transfer. Note 2: Visibility of data content signifies that the MNO can, at least, be aware of, access, and comprehend the data without the need of SLA. Note 3: The following options are identified to realize the different levels of data content visibility to the MNO: Full visibility for standardized data content. Partial visibility for partially standardized data content (e.g. UE proprietary information can be included transparently together with the standardized data message). No standardized visibility (e.g. UE proprietary information can only be included transparently). Note 4: The potential involvement of NF or other higher layers entities/functionalities should be discussed in other WGs. Impact on the OTT server is not in the scope of RAN2 discussion. Note 5: RAN2 cannot reach consensus on the level of possible MNO controllability and visibility via Option 1b without input from SA groups. Note 6: RAN2 has not concluded on the need for partial and no visibility options. Note 7: RAN2 cannot reach consensus on the feasibility of UP tunnel in Options 2 and 3. |  |  |  | 

## Slide 5: Analysis of different data collection options for UE-side model training
Option 1b, option 2 and option 3 require studies in different SA WGs.
In more detail we propose:
  Option 1b and Option 2: SA2 leads the discussion and coordinates with other WGs.
  Option 3: SA5 leads discussion and coordinates with other WGs.

## Slide 6: Proposals
Proposal 1: SA plenary discusses the work allocation to different SA WGs for the potential options of data collection for UE-side model training in RAN2’s table in 3GPP TR 38.843 and possible other aspects included in 3GPP TR 38.843.
Proposal 2: The technical discussion for different options of data collection for UE-side model training in RAN2’s table in 3GPP TR 38.843 are discussed in specific SA WGs.
  Option 1b and Option 2: SA2 leads the discussion and coordinates with other WGs.
  Option 3: SA5 leads discussion and coordinates with other WGs.
Proposal 3: The TU allocation and study scope corresponding to different options should be discussed in SA2 and SA5 respectively.