## Slide 1: Discussion on NEF’s role in VFL process
SA2#166
vivo
S2-24xxxxxx

## Slide 2: NEF’s role in VFL process
Some roles of NEF during VFL process have been discussed and agreed in the last two meetings:
  For a untrusted AF as VFL server case, discovering NWDAF as VFL clients from NRF for the untrusted AF;
  For a untrusted AF as VFL server case , anonymizing real NWDAF instances ID from the untrusted AF by using temporary NWDAF ID.
  For either case (untrusted AF as VFL server or VFL client), forwarding intermediate results from NWDAF to AF and vice versa, in which translating between external and internal IDs (e.g., UE IDs) happens.
However, there are still concerns about Other NEF’s roles in VFL process. The following editor’s notes are captured in TS 23.288 or approved CR:
  Editor's note: If any of the Consumer, Server and clients are untrusted AF(s), how the NEF assists the VFL inference process, and whether the existing or new NEF service should be invoked are FFS. (CR: 2411192 – OPPO; Clause 6.2H.2.4.1)
  Editor's Note: How the NEF assists the VFL training process as well as whether the service operations going via NEF is using the existing or new service operation are FFS. (CR: 2411194 – CMCC; Clause: 6.2H.2.3.1)
  Editor’s note: It is FFS, whether NEF should perform VFL NWDAF selection (or shortlisting) or it should only discover NWDAF client candidates without any further selection. (CR: 2411193 – vivo; Clause: 6.2H.2.1.2)

## Slide 3: NEF’s role in VFL process
As a summary, some key points to be discussed for this issue :
  Sub-issue 1: For the VFL client(s) discovery procedure, whether and how NEF does further NWDAF client shortlisting or selection based on the discovery result from NRF?
  Sub-issue 2: For the VFL preparation procedure, whether and how NEF does pre-work of sample IDs intersection before the VFL server determines the final sample IDs?
  Sub-issue 3: For the VFL training procedure, how does the NEF assist the VFL training process?
  Sub-issue 4: For the VFL inference procedure, how does the NEF assist the VFL inference process?
  Sub-issue 5: Whether new NEF’s service operations should be defined for the VFL or existing ones will be reused? How to define or enhance them correspondingly?

## Slide 4: Sub-issue 1 (see P5 for related procedure)
For the VFL client(s) discovery procedure, whether and how NEF does further NWDAF client shortlisting or selection based on the discovery result from NRF?
Companies | View (whether) | Explanation (how)
vivo | Neutral to negative | - NEF internal implementation, maybe no need to standardized
Nokia | Y | - NEF needs to consider aspects such as load or geographic proximity
ZTE | Slightly negative | -implementation aspects
OPPO | Neutral | Compare with the samples, the number of the clients will be quite small, no benefit to let NWDAF do further down selection.
Samsung | Neutral | The technical aspects provided by Nokia makes sense to us. But as mentioned by OPPO, the benefit of this enhancement might be not significant, considering the small number of NWDAF(s) currently deployed.
Huawei | N | - It is based on NEF internal logic. We only standardize inputs for NF selection.
ETRI | Neutral | Same view as OPPO and Samsung
KDDI | Slightly negative | -implementation aspects
LGE | Slightly negative | - Implementation aspects
Way forward:

## Slide 5
  CR: S2-2411193(vivo), Clause: 6.2H.2.1.2, step 8 .
  Editor’s note: It is FFS, whether NEF should perform VFL NWDAF selection (or shortlisting) or it should only discover NWDAF client candidates without any further selection.
Registration and Discovery procedure for VFL when AF as the VFL server

## Slide 6: Sub-issue 2 (see P7, P8 P8-10 for related solutions)
For the VFL preparation procedure, whether and how NEF does pre-work of sample IDs intersection before the VFL server determines the final sample IDs?
Companies | View (whether) | Explanation (how)
vivo | Y | Role: Before determining final intersection by the VFL server, the NEF can help to obtain a intersection from untrusted AF and NWDAF as candidates, no matter who acts as VFL server or VFL client (i.e. in either case); Benefit: See the next two pages (P7,P8) for details of solution and benefits comparing. But the most important benefit is to achieving less sample IDs revealing from 5GC to AF Note: SA3 has related requirement and is discussing it.
Nokia | Complicated, need more clarification of gain | No clear gain, may be done by AF as VFL server
ZTE | Y | Avoid sample information exchange inside 5GC and outside 5GC. Reduce the number of samples to be carried in service operation.
OPPO | Y | Support the Alt2. When multi AFs are involved, the NEF can first determine the intersection of samples for every AF then performing the ID mapping. It will significantly reduce the number of the IDs to be mapped in NEF.
Ericsson | Positive to the idea to reduce the load in NEF | Need more justification on how Alternative 2 reduces the load
Samsung | Y | We support the enhancement to NEF in Alt2. But the steps in Alt2 need more justification, e.g. if step 8 is performed by the server, whether the NEF still needs to perform step 6 which may increase NEF workload; if step 6 is not needed at NEF, whether the 100K sample IDs need to be sent to NEF in step1, etc. (NWDAF as server). e.g. currently both the VFL server (step 8) and NEF (step 5) determine the sample IDs intersection among VFL client and servers, we wonder whether the NEF in step 5 calculates the intersection among VFL clients and server, or calculates the intersection among VFL clients only. If 1), the function of step 5 and step 8 seems duplicated; if 2), whether the 100K sample IDs need to be sent to NEF in step1.
Updated with some blue words

## Slide 7: Sub-issue 2
Companies | View (whether) | Explanation (how)
Huawei | See details | When untrusted AF is the VFL server, the AF should not get the sample info which is not controlled by the AF. Thus, the NEF should do sample IDs intersection (together with translating between external and internal IDs of course). When NWDAF is the VFL server, the NWDAF can do intersection and translating between external and internal IDs (e.g., UE IDs) by itself. NEF just needs to transfer the related info. (PS: there is no need for server to first send out simple IDs first)
ETRI | Y | Support Alt2. As mentioned above by other companies, it can reduce signaling load while minimizing the amount of sample information exposed between inside and outside 5GC.
KDDI | Prefer alt 1. | Prefer alt 1 to reduce NEF load. Alt 2 is too complex to specify. There are many sample intersection mechanism which is up to VFL Server.
LGE | Prefer alt 1. | This may be done by VFL Server.
Way forward:

## Slide 8
NWDAF
(server)
NEF
2. 100K Sample IDs mapping from internal to external
1.Preparation/sample alignment request
(e.g. 100K sample IDs provided by NWDAF as server, other parameters)
3a. Preparation/sample alignment request
(e.g. 100K sample IDs mapped by the NEF , other parameters)
Untrusted AF
(client)
4a. Decides whether to joint, and if there are overlapping sample IDs, takes out the intersection
Untrusted AF
(client)
5a. Preparation/sample alignment response
(e.g. 10K intersection sample IDs selected by the AF)
6a. 10K Sample IDs mapping from external to internal
7a. Preparation/sample alignment response
(e.g. 10k sample IDs mapped by the NEF)
8. Determines the final intersection(e.g.6k) of sample IDs
4b.
3b.
5b.
6b.
7b.
Alt 1: NEF only supports normal sample ID mapping
Cons: (comparing with Alt 2)
In step 2, the NEF needs to map more sample IDs (e.g. 100k) from internal to external type.
In step 3. and the NEF exposes large scale of sample IDs (e.g. 100k) to 3rd party.
In step 6, inverse mapping from external to internal still needs to be done in NEF.
If more than one AF as the clients, then the step 2-7 need to be implemented more than one time corresponding to each AF.

## Slide 9
NWDAF
(server)
NEF
(enhanced)
1.Preparation/sample alignment request
(e.g. 100K sample IDs provided by NWDAF as server(optional), other parameters)
2a. Preparation/sample alignment request (other parameters(analytics ID, application ID…AOI))
Untrusted AF
(client)
3a. Decide whether to joint in the VFL process
Untrusted AF
(client)
4a. Preparation/sample alignment response
(e.g. 10k sample IDs selected by the AF)
5. Obtains the intersection (e.g. 8K) of sample IDs provided by NWDAF and the AF(s), and optional ones from NWDAF
7. Preparation/sample alignment response
(e.g. 8k sample IDs mapped by the NEF)
8. Determines the final intersection (e.g.6k) of sample IDs
6. The intersection (e.g. 8K) sample IDs mapping from external to internal
2b.
4b.
3b.
Alt 2 (preferred): enhanced NEF supports sample intersection
Pros: (comparing with Alt 1):
In step 2, no need to expose sample IDs from NWDAF by the NEF to 3rd party, and consequently no need to map IDs from internal to external type, less length of signaling .
In step 5, the NEF can aggregate and generate the intersection for NWDAF and all the AFs, and optional ones from NWDAF.
Only mapping from external to internal needs to be done in step 6, and the NEF will map less sample IDs (e.g. 8k).
Only one response message in step 7.
Summary: comparing with Alt 1, more secure for MNO by revealing no/less sample IDs (most important benefit), less mapping work load for the NEF, and less signaling overhead.
Note: in case of untrusted AF as VFL server, similar solution and benefit is applicable. (updated, see next page )
Note：This Alt2 has been discussed in TR solution, but the details were not concluded due to time limitation. It is not conflict with the HL principle (i.e. P#2.3: For sample alignment for VFL) agreed in TR conclusion.
NWDAF as VFL server case
Updated with some blue words

## Slide 10
NEF
(enhanced)
1.Preparation/sample alignment request
(e.g. 100K sample IDs provided by AF as server(optional), other parameters(analytics ID, application ID…AOI)
2a. Preparation/sample alignment request (100K sample IDs provided by AF as server(optional), other parameters(analytics ID, application ID…AOI))
3a. Decide whether to joint in the VFL process
Untrusted AF
(server)
4a. Preparation/sample alignment response
(e.g. 50k sample IDs selected by the NWDAF)
5. Obtains the intersection (e.g. 12K) of sample IDs provided by the NWDAFs, and optional ones from AF
7. Preparation/sample alignment response
(e.g. only 12k sample IDs mapped by the NEF)
8. Determines the final intersection (e.g.8k) of sample IDs
6. The intersection (e.g. 12K) sample IDs mapping from internal to external
2b.
4b.
3b.
Alt 2 (preferred): enhanced NEF supports sample intersection
Pros: (comparing with Alt 1):
In step 2, sending 100k samples from NEF to NWDAF is optional, thus mapping from external to internal work may can be avoided.
In step 5, the NEF can aggregate and generate the intersection all the NWDAFs, and optional ones from AF. Then only 12k sample IDs will be exposed from 5GC to AF rather than 50k or more（if for multiple NWDAFs）
Only mapping from internal to external needs to be done in step 6, and the NEF will map less sample IDs (e.g. 12k).
Only one response message in step 7.
Summary: More secure for MNO by revealing less sample IDs from 5GC to AF(the most important benefit), less mapping work load for the NEF, and less signaling overhead.
NWDAF
(client)
NWDAF
(client)
Untrusted AF as VFL server case
Newly added page

## Slide 11: Sub-issue 3 2 (see P1012 for related procedure)
Sub-issue 3: For the VFL training procedure, how does the NEF assist the VFL training process?
Companies | Explanation (how)
vivo | The roles that have been agreed and shown in 1st part, page 2;
Nokia | - The roles that have been agreed and shown in 1st part, page 2;
ZTE | - The roles that have been agreed and shown in 1st part, page 2;
OPPO | Put all the intermedia results from the different VFL client into one message and send on message to the VFL server. NEF no need to aware the VFL logic.
Samsung | Same view as OPPO. Enhancing NEF to accumulate the results from multiple VFL clients can reduce the signalling between NEF and VFL server and NEF load significantly.
Huawei | - The roles that have been agreed and shown in 1st part, page 2;
ETRI | Same view as OPPO. Signaling can be significantly reduced between NEF and VFL server (AF or NWDAF).
KDDI | - The roles that have been agreed and shown in 1st part, page 2;
LGE | - The roles that have been agreed and shown in 1st part, page 2;
Way forward:

## Slide 12
  CR: S2-2411194 (CMCC), Clause: 6.2H.2.3.1
  Please note：when AF as VFL server, the similar issue should also be considered
  Editor's Note: How the NEF assists the VFL training process as well as whether the service operations going via NEF is using the existing or new service operation are FFS.
Figure 6.2H.2.3.1-1Training procedure for Vertical Federated Learning when NWDAF is acting as VFL server

## Slide 13: Sub-issue 4 (see P1214 for related procedure)
How does the NEF assist the VFL inference process?
Companies | Explanation (how)
vivo | Similar as the Nokia’s view on this aspect
Nokia | - Same roles that have been agreed and shown in 1st part, page 2; - supporting service operations (e.g. new analytics service or reusing event exposure service ) to trigger inference from 5GC to untrusted AF
ZTE | - Same as Nokia’s view
OPPO | Put all the intermedia results from the different VFL client into one message and send on message to the VFL server. NEF no need to aware the VFL logic.
Samsung | See P9
Huawei | See P9
ETRI | Same view as OPPO. See P9
KDDI | See P9
LGE | See P9
Way forward:

## Slide 14
  CR: S2-2411192 (OPPO), Clause: Clause 6.2H.2.4.1
  Please note：when AF as VFL server, the similar issue should also be considered
  Editor's note: If any of the Consumer, Server and clients are untrusted AF(s), how the NEF assists the VFL inference process, and whether the existing or new NEF service should be invoked are FFS.
Figure 6.2H.2.4.2-1: Inference procedure for vertical federated learning when NWDAF is acting as VFL server

## Slide 15: Sub-issue 5
Whether new NEF’s service operations should be defined for the VFL or existing ones will be reused? How to define or enhance them correspondingly?
Way forward: suggest to discuss from functionality point of view in this DP, i.e. identify what functions should the NEF support for VFL. And we leave the service operations (new or existing) to the DP of the other issue 7.

## Slide 16: [supramental] Concern on NEF’s support on intersection selection alt 2 in page 10 from KDDI
We are concerned about having tremendous NEF functionality.
There are many sample intersection selection methods. How to select an intersection is up to implementation, which should be determined by the VFL server (i.e., AF or NWDAF), taking other criteria (e.g., feature importance) into account.
If NEF selects a sample intersection, the flexibility of the VFL server's sample intersection selection is reduced.
1
NF instance A
NF instance C
NF instance B
sample space
The right Fig shows an example of sample distribution among 3 NFs. Sample #1 belongs to NF A, B, and C. Sample 2 belongs to NF B and C.
Which samples should be used for VFL is up to implementation.
3
2
4