## Slide 1: Discussion on VFL
SA2#165
vivo (Rapporteur)
S2-24xxxxxx

## Slide 2: Issue 1 --- AF as VFL Server (1/3)
The following editor’s note is captured in TS 23.288, DP S2-2409927, S2-2410278 and some CRs for VFL:
Editor's Note: Further extensions are needed to show when any of the VFL participants are untrusted AF(s). In this case the procedure below will contain a NEF, and how the NEF assists the VFL training process as well as whether the service operations going via NEF is using the existing or new service operation are FFS. (9927)(10278)
Nokia (DP: 9927)
  Proposal 1: Allow Option 1 for a trusted AF as VFL server (A trusted AF as VFL server directly accesses NRF, select NWDAFs as VFL clients, and communicates with them directly without an intermediate NEF)
  Proposal 2: Use Option 3 for an untrusted AF as VFL server (NEF selects VFL clients based on NRF entries and requirements provided by AF as VFL server, provides temporary IDs for those VFL clients to the AF, and proxies subsequent communication based on those IDs)
  Proposal 5: The NEF supports sample alignment by proxying related messages and modifying the identifiers/description of samples between an external and internal format where required
KDDI (DP: 10278)
Option 1 : AF integrates data from multiple NWDAFs
• AF is aware of multiple NWDAFs, separately, i.e., 5GC exposes multiple NWDAFs' information, (e.g., NWDAF IDs and data source of NWDAF), separately.
• NEF’s role:
  • translation of external and internal IDs, (e.g., UE IDs).
  • forward intermediate results from NWDAF to AF and from AF to NWDAF.
Option 2: NEF integrates data from multiple NWDAFs
• AF is aware of multiple NWDAFs, separately, i.e., 5GC exposes multiple NWDAFs' information, (e.g., NWDAF IDs and data source of NWDAF), separately.
• NEF’s role:
  • translation of external and internal IDs (e.g., UE IDs).
  • determining candidate sample for AF (taking Rel18 member UE selection into consideration)
  • Integrate and forward intermediate results from NWDAF to AF, and that from AF to NWDAF.
  • anonymize network topology, e.g., using temporal NWDAF ID.

## Slide 3: Issue 1 --- AF as VFL Server (2/3)
ETRI (CR: 10145)
  For trusted AF, AF as VFL Server could interact with VFL Clients directly.
  For untrusted AF, AF as VFL Server interacts with VFL Clients indirectly via NEF. The NEF is only involved for an untrusted AF and maps the external UE IDs (e.g. GPSIs) to the internal UE IDs (e.g. SUPIs).
vivo (CR: 9716)
  For trusted AF, AF could interact with VFL Server or VFL Clients directly.
  For untrusted AF, AF could interact with VFL Server or VFL Clients via NEF. During discovery, the NEF discovers VFL client (i.e. NWDAF) on behalf of the untrusted AF from the NRF, and anonymizes NWDAF instances ID(s) into temporary NWDAF ID(s). During sample alignment, the NEF generates an intermediate intersection of sample IDs based on samples of untrusted AF and NWDAF(s).
Observation: for trusted AF, most companies proposed that AF could interact with NRF and VFL Clients directly.
Way forward1: for trusted AF, AF interact with NRF and VFL Clients directly.

## Slide 4: Issue 1 --- AF as VFL Server (3/3)
Observation 2: for untrusted AF, most companies agreed that a NEF is involved in VFL process, but the specific roles of NEF are different (e.g. whether NEF determine candidate sample for AF)
  NEF’s role:
    translates external and internal IDs (e.g., UE IDs).
    discover and select NWDAF clients.
    helps sample alignment for AF
    forwards intermediate results from NWDAF to AF, and that from AF to NWDAF.
    anonymizes network topology, e.g., using temporal NWDAF ID or temporary client identifier (controversial).
    integrates intermediate results from NWDAFs and forwards the message to AF (controversial).
For untrusted AF, the proposed way forward:
  A NEF is involved in VFL process
  The NEF follow the highlighted rules and others continue offline discussion
If needed, quickly handle S2-2402927 from Nokia / S2-2410005 from Ericsson
If needed, quickly handle S2-2409928 from Nokia (focusing on VFL training + inference when AF as VFL Server)

## Slide 5: Issue 2 --- Sample alignment and sample update
The following editor’s note is captured in TS 23.288, DP S2-2409790 and some CRs for VFL:
Editor’s Note: A possible need for a process of sample exchange between VFL server and VFL client is FFS. The process may be determined after agreement on sample and/or feature alignment. (9790)
Huawei (DP 9790):
  Only sample alignment needs to be exchanged in the VFL Training preparation procedure;
  There is no support for dynamic changes in the sample space for a given VFL training process (i.e., VFL correlation ID);
  Any change in the sample IDs of a sample space should be treated as VFL training process;
Apple (DP 10078):
  The client (NWDAF or AF) or the Server (NWDAF or AF) can trigger a sample update procedure during the course of training.
Ericsson (CR 10008):
  The preparation phase contains alignments. Possibility to lower or increase samples is introduced in VFL training phase.
Way forward: Sample alignment is necessary and an additional process for sample update is to be postponed in future Release due to limited time.

## Slide 6: Issue 2 --- Feature alignment
The following editor’s note is captured in TS 23.288, DP S2-2409790 and some CRs for VFL:
Editor’s Note: Whether and how to exchange feature between VFL server and VFL client is for FFS. The process may be determined after agreement on sample and/or feature alignment.
Observation: a few companies think that Feature is vendor specific and should not be transferred via signalling, while other a few companies think feature alignment need some standardized work to make it work.
Way forward: more discussion are needed to gather more wider view.
Newly added

## Slide 7: Issue 4 - ML Model ID or VFL Model Correlation ID or VFL Correlation ID
The following editor’s note is captured in TS 23.288, DP S2-2409790, S2-2409925 and some CRs for VFL:
Editor’s Note: It is FFS whether and how to use ML Model ID or VFL Model Correlation ID or VFL correlation ID in the VFL training process. (9790) (9925)
Observation:
Company | View
Huawei | the ML Model ID to identify a ML model that is being trained by NWDAF or AF; VFL Correlation ID to signal that the ML Model ID is associated with a VFL training process;
Ericsson | VFL correlation ID is acceptable and introduced
OPPO | VFL model correlation ID
Nokia | VFL model correlation ID
KDDI | VFL model correlation ID
Interdigital | VFL model correlation ID
Vivo | VFL model ID
Lenovo | VFL training ID
Way forward: more discussion are needed to gather more wider view

## Slide 8: Issue 3 --- existing FL capability or new VFL capability
The following editor’s note is captured in TS 23.288, DP S2-2409924 and some CRs for VFL:
Editor's note: Whether we can use the existing FL capability information IE, or a new VFL capability information IE is introduced, is FFS. (9924)
There are two options for VFL Capability:
  Option 1: existing FL capability
  Option 2: new VFL capability
Observation 1: 2 companies supports existing capability.
  Vivo proposed FL capability type as FL server, FL type (i.e. VFL),. --- 9678
  Lenovo proposed to extend the FL capability type by including VFL Server/VFL client capability. --- 9887
Observation 2: 4 companies supports new VFL capability.
  Nokia introduces a new capability indicator for VFL. --- 9924
  E/// using new VFL capability --- 10008
  ICS proposed VFL capability type (i.e. VFL server and/or VFL client) --- 9645
  HW introduce a new VFL capability information. --- 9788
Way forward: use new VFL capability as baseline.

## Slide 9: Issue 5 --- one procedure or two procedures
The following editor’s note is captured in TS 23.288, DP S2-2409790 and some CRs for VFL:
Editor’s Note: Whether one general procedure or two separate procedures for NWDAF/AF as server will be discussed and decided in future meeting when the procedures are stable. (9790)
There are two options for VFL procedure:
  Option 1: one general procedure
  Option 2: two split procedures
Company | Views | Details
Huawei | Two split procedures | Two split preparation procedures, suggests to Split the VFL Training Procedure between AF as VFL server and NWDAF as VFL. – 9789, 9790(DP)
Vivo | Two split procedures | Two split VFL sample alignment on VFL sample alignment, VFL Training and VFL Inference. - 9716, 9715, 9717
Nokia | Two split procedures | Document call flows when AF is VFL server separately from call flows when NWDAF is VFL server. - 9927
ETRI | Two split procedures | A VFL preparation when the AF as VFL Server. --- 10145
KDDI | Two split procedures | the VFL preparation, VFL Training and VFL Inference when the AF as VFL Server. – 10307, 10286, 10288, 10278 (DP)
OPPO | One general procedure | One general procedure for VFL inference. - 9733
Ericsson | One general procedures | one general preparation procedure, one general VFL training procedure and one general VFL inference procedure. - 10008
Way forward: use two split procedures.