## Slide 1: 5G Energy Efficiency

## Slide 2: Release 19 Study on energy efficiency and energy saving aspects of 5G networks and services
Several Work Tasks, among which WT-1: Left-overs from Rel-18
  Enery Consumption of 5G Network Functions
    Rel-17
      Focus on VM-based VNF/VNFCs
      EC is estimated based on vCPU usage of underlying virtual compute resource instance
    Rel-18
      EC can be estimated based on vCPU usage, vMemory usage, vDisk usage, I/O traffic
      Still focused on VM-based VNF/VNFCs

## Slide 3: Energy Consumption of a Network Function in Rel-19 (1/2)
To be addressed in Rel-19, wrt. Enery Consumption of 5G Network Functions
    Consider Container-based VNF/VNFCs (terminology under discussion in Rel-19 study on Cloud Aspects of Management and Orchestration)
    Two approaches being studied:
      Extend the Rel-17/18 approach for estimating the Energy Consumption of Container-based VNF/VNFCs
      New approach aiming at measuring the actual Energy Consumption of Container-based VNF/VNFCs
    Both approaches rely on new ETSI NFV measurements defined in IFA 027 v5.x.y (to be published).
    A potential solution is being investigated for both these approaches if the new ETSI NFV performance measurements defined in IFA 027 (to be published) collected from ETSI NFV MANO could be used.

## Slide 4: Energy Consumption of a Network Function in Rel-19 (2/2)
  Both approaches have pros and cons, and will be further investigated in SA5
  Other approaches may be studied, some of which may not be based on ETSI NFV MANO.
  Energy consumption KPIs at VNF and VNFC level would be required for container-based solution from ETSI NVF MANO to be used in SA5.

## Slide 5: Summary
  The current 3GPP SA5 Rel-19 study item on EE is expected to be completed by August 2024, and normative phase is planned for Sept. 2024 to Sept. 2025.
  SA5 expects that the two approaches (cf. previous slides) will have solutions in Rel-19.
  Requests to ETSI NFV:
    Energy consumption KPIs at VNF and VNFC level would be required for container-based solution from ETSI NVF MANO to be used in SA5.
    SA5 asks ETSI NFV to inform SA5 as soon as IFA 027 Release 5 has been published, so that SA5 can use it to investigate the potential solutions for new EE KPIs.

## Slide 6
Thank you !