3GPP TSG-SA5 Meeting #154 	S5-243220

Jeju, Korea (Republic Of), 27th May 2024 - 31st May 2024

# Source:	Nokia, Ericsson

# Title:	Rel-18 pCR 28.872 Add use case on Managing transactions

# Document for:	Approval

Agenda Item:	6.19.9 - Study on Management of planned configurations

# 1	Decision/action requested

The group is requested to discuss and approve the pCR below.

# 2	References

[1]		3GPP TS 28.872: "Study on Management of planned configurations"

# 3	Rationale

None.

# 4	Detailed proposal

The following changes are proposed for TR 28.872[1].

Begin of modifications

## 5.X	Use case #X: Managing transactions

### 5.X.1	Description

A transaction is a set of plans that need to be handled (validated, activated) together. For example, one plan may create a new cell and another plan may start the collection of measurements for the new cell.

The 3GPP management should enable to manage transactions.

### 5.X.2	Potential requirements

Req-1: The 3GPP management system should allow MnS consumers to manage transactions.

### 5.X.3	Potential solutions

#### 5.x.3.1	Potential solution #1: Grouping plans into transactions

A transaction is described with a set of properties. The main property is the "transactionPlanIds" property that identifies the planned configurations pertaining to the transaction.

Editor's note: It is ffs if the MnS producer should enforce the concurrent activation of all plans pertaining to a transaction, or if this responsibility should be left to the MnS consumer.

HTTP/JSON

The collection resource "configuration-transactions" is introduced at the same level as the resource "planned". An item of this collection resource describes a transaction.

Editor's note: It is ffs how to apply activation control parameters to transactions. For example, is it possible that a planned configuration is activated in best-effort mode whereas another one in all-or-nothing mode?

Example:

The following example demonstrates how a new transaction is created. The planned configurations "p1" and "p2" are part of this transaction. Both need to be activated successfully to create the URLLC slice.

POST 3gpp/ProvMnS/1900/configuration-transactions HTTP/1.1 Host: example.org Content-Type: application/json { "transactionPlanIds": [p1, p7], "transactionLabel": "urllcSlice", "transactionDescription": "This transaction creates a URLLC slice." }

After applying the POST request, the resource structure on the MnS producer looks as follows.

{ "configuration-transactions": { "t1": { "transactionPlanIds": ["p1", "p7"], "transactionLabel": "urllcSlice", "transactionDescription": "This transaction creates a URLLC slice." } } }

#### 5.x.3.1	Potential solution #2: Creating new plans for transactions

In this solution a new plan is created for a transaction. This plan is built from the other existing plans that form the set of plans pertaining to the transaction.

End of modifications