3GPP TSG-SA5 Meeting #154 	S5-243221

Jeju, Korea (Republic Of), 27th May 2024 - 31st May 2024

# Source:	Nokia, Ericsson

# Title:	Rel-18 pCR 28.872 Add use case on Managing alternative planned configurations

# Document for:	Approval

Agenda Item:	6.19.9 - Study on Management of planned configurations

# 1	Decision/action requested

The group is requested to discuss and approve the pCR below.

# 2	References

[1]		3GPP TS 28.872: "Study on Management of planned configurations"

# 3	Rationale

None.

# 4	Detailed proposal

The following changes are proposed for TR 28.872[1].

Begin of modifications

## 5.X	Use case #X: Managing alternative planned configurations

### 5.X.1	Description

A MnS consumer may desire to create multiple alternative planned configurations on a MnS producer. The alternatives may be used for different purposes: Planned configuration may exist for example for weekdays and weekends, or for different weather conditions.

### 5.X.2	Potential requirements

Req-1: The 3GPP management system should allow MnS consumers to manage alternative planned configurations.

### 5.X.3	Potential solutions

The set of alternative planned contributions needs to be tagged with the same identifier. Each alternative may have a dedicated name and a description under which conditions the alternative is used.

HTTP/JSON

The collection resource "configuration-alternatives" is introduced at the same level as the resource "planned". An item of this collection resource describes a set of alternative planned configurations.

Example:

The following example demonstrates how planned configurations can be grouped into a set of alternative planned configurations.

POST 3gpp/ProvMnS/1900/configuration-alternatives HTTP/1.1 Host: example.org Content-Type: application/json [ { "altPlanId": "p1", "altPlanLabel": "configurationWeekEnds", "altPlanDescription": "This configuration is for weekends." }, { "altPlanId": "p2", "altPlanLabel": "configurationWeekDays", "altPlanfDescription": "This configuration is for weekdays." } ]

After applying the POST request, the resource structure on the MnS producer looks as follows.

{ "alternatives-transactions": { "a1": [ { "altPlanId": "p1", "altPlanLabel": "configurationWeekEnds", "altPlanfDescription": "This configuration is for weekends." }, { "altPlanId": "p2", "altPlanLabel": "configurationWeekDays", "altPlanfDescription": "This configuration is for weekdays." } ] } }

Begin of modifications