3GPP TSG-SA5 Meeting #155 	S5-243297

Jeju, South Korea, 27 - 31 May 2024

# Source:	China Telecom

# Title:	potential solution for Management of connections between UPF on-board satellite and SMF

# Document for:	Approval

Agenda Item:	6.19.15

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1]	3GPP TR 23.700-29: " Study on integration of satellite components in the 5G architecture Phase 3".

[2]	3GPP TS 28.541: "Management and orchestration; 5G Network Resource Model (NRM); Stage 2 and stage 3".

# 3	Rationale

In Rel-19, SA2 has started a study TR 23.700-29 [1] on supporting of UE-satellite-UE communication under regenerative-based satellite access architecture. The definition of UE-satellite-UE communication is as follows.

--- Start of quote from TR 23.700-29 ---

UE-satellite-UE communication refers to the communication between UEs under the coverage of one or more serving satellites without the user plane traffic going through the ground network.

---End quote---

To support UE-satellite-UE communication for IMS voice and video as well as MCPTT services, 5GC network function(s) is necessary onboard the satellite(s), e.g. UPF. After three meetings, all solutions addressing Key Issue #3 required UPF on-board satellite.

Observation 1: For realizing UE-satellite-UE communication, SA2 requires the network to support the operation of the UPF on-board satellite.

The previous SA5 work 5GSATB_OAM did not fully support the operation of UPFs on-board satellites. This is because the previous work was based on the satellite backhaul architecture, so the information of the UPF on-board satellite was only configured in the backhaul information, as seen in TS 28.541 [2]. Therefore, using the existing information does

--- Start of quote from TS 28.541---

5.3.231	SatelliteBackhaulInfo <<dataType>>

5.3.231.1	Definition

This datatype defines information related to satellite backhaul category and corresponding information of (R)AN.

5.3.231.2	Attributes

| Attribute name | S | isReadable | isWritable | isInvariant | isNotifyable |
| --- | --- | --- | --- | --- | --- |
| nTNGlobalRanNodeID | M | T | T | F | T |
| satelliteBackhaulCategory | M | T | T | F | T |
| geoSatelliteId | CM | T | T | F | T |

5.3.231.3	Attribute constraints

| Name | Definition |
| --- | --- |
| geoSatelliteId S | Condition: Present if UPF is deployed on a GEO satellite. NOTE 1: In the present document, only the feature of deploying UPF on GEO satellite is supported. |

5.3.231.4	Notifications

The subclause 5.5 of the <<IOC>> using this <<dataType>> as one of its attributes, shall be applicable.

---End quote---

Observation 2: The existing SA5’s work cannot cover this use case.

Based on the above observations, we found that to support UE-Satellite-UE communication, 3GPP management system needs to be enhancement to support management of Core Network Function (e.g. UPF) on-board satellite.

Proposal: NRM enhancements need to be investigated to manage the Core Network Function (e.g. UPF) on-board satellite.

# 4	Detailed proposal

Start of 1st Change

### 5.4.1	Use case #1: UE-Satellite-UE Communication via UPFs on-board the satellites

#### 5.4.1.1	Description

SA2 R19 work has specified the requirement for architectural enhancements, including core network functions on-board satellite, to support new communication mode or service, such as UE-Satellite-UE. This introduces new management requirements, for example, when UPF on-board satellite and SMF on the ground, the N4 associations change frequently. So, the UPF and/or SMF need to know when to establish and release the N4 associations with which SMF and/or UPF. Another example, to support UE-satellite-UE communication, 3GPP management system configures indication information (i.e., indicates whether UPF is on-board satellite or not) enabling the SMF to know which UPF is on-board satellite. Thus, the UPF on-board satellite is selected to keep user plane traffic remain in the satellites.

An example diagram of the gNB and UPF deployed on satellite to enable UE-Satellite-UE is shown in Figure 5.4.1.1-1.

Figure 5.4.1.1-1: UE-Satellite-UE Communication via UPFs on-board the satellites

#### 5.4.1.2	Potential requirements

REQ-UE-SAT-UE-1：3GPP management service producer should have the capability to configure the associations between UPF on-board satellite and SMF on the ground.

REQ-UE-SAT-UE-2：3GPP management service producer should have the capability to configure the UPF or SMF enabling the SMF to know which UPF is on-board satellite.

#### 5.4.1.3	Potential solutions

##### 5.4.1.3.x	Potential solution #<x>: <Configuration of the UPF indicates whether the UPF is on-board satellite or on the ground>

This is a candidate solution to address the REQ-UE-SAT-UE-1.

This solution proposes to add new attributes or IOCs that required to be presented when the UPF is on-board satellite. It may contain the following attributes:

- 	Explicitly Indication whether the UPF is on-board satellite or on the ground.

-	Deployment information representing the satellite identification of the UPF deployed.

##### 5.4.1.3.y	Potential solution #<y>: <Pre-configuration of the N4 interface between SMF and UPF before connections between them are established or lost >

This is a candidate solution to address the REQ-UE-SAT-UE-2.

As described in Use case #1, the connections between UPF on-board satellite and SMF on the ground changes frequently, typically because the periodic connecting/disconnecting of the UPF on-board satellite to the gateways. Therefore, this solution proposes to take the connecting/disconnecting of the UPF on-board satellite to the gateways as an event that triggers the 3GPP management to perform configuration operations on the N4 interface.

The solution addresses the scenario where the UPF on-board satellite is connected to one or more gateways simultaneously during a given period, and the SMF on the ground associated with the gateway can be different or the same. Figure 5.4.1.3.x-1 shows an example deployment scenario.

-	Case I: UPF connects to the same SMF via a different gateway (e.g. UPF connects SMF 3 via Gateway 2 or Gateway 3).

-	Case II: UPF connects to a different SMF via a different gateway (e.g. UPF connects SMF 2 via Gateway 2).

The attribute in the EP_N4 indicating the UPF address will have different values if the connection between UPF and SMF is via the different gateway.

Figure 5.4.1.3.x-1	Example scenario of connections between UPF on-board satellite and SMF.

The 3GPP management system creates multiple EP_N4 instances to handle the multiple connectivity links between UPF on-board satellite and SMF on the ground, and adds new attributes representing the connection availability duration information in EP_N4 IOC.

Before the connection between UPF on-board satellite and gateway is lost, the 3GPP management system may removes/modifies the EP_N4 instances and removes/modifies the relevant connection availability duration information.

The connection availability duration information is a list that provides the time when the UPF has a connection to a SMF and the time when the connection is disconnected.