## Slide 1: Views on Rel-20 Enhancements for UAV/UAM

## Slide 2: Justification for Rel-20 enhancements for UAV/UAM
Toward 3D mobility in 6G
  3GPP introduced initial support of NR UAV in Rel-18. The introduced functionalities include aerial UE specific spectrum emission, flight path reporting, measurement report enhancements.
  UAV and UAM industry are expected to grow rapidly with estimated compound annual growth rate of 16% and 30%, respectively, until 2032.
  In Korea, K-UAM project is actively on-going. Several K-UAM consortiums are undergoing demonstration projects to launch pilot K-UAM services in 2025/2026. 3GPP specifications applicable for UAV/UAM are important sources of references for service design, project planning and milestones for K-UAM project participants.
  To enable 3GPP be well prepared for rapidly-growing UAV/UAM industry, continued enhancements in 3GPP Rel-20 for aerial UEs (UAV/UAM) are necessary.
  Furthermore, Rel-20 is the step-stone for 6G 3D mobility integrating TN and NTN including aerial and space network. Enhancements for aerial UEs in Rel-20 can pave the way for developing more integrated 6G 3D mobility to be applicable from 6G day 1.
Our view
  Enhancements to UAV/UAM in Rel-20 are necessary to be prepared for rapidly-growing UAV/UAM industry as well as 6G 3D mobility
Unmanned Aerial Vehicle
Urban Air Mobility
6G 3D mobility
The presence of passengers inside UAM vehicle UE imposes more stringent requirements on connectivity robustness and link performance over radio interface, compared to UAV aerial UEs.
NTN
Rel-17
Rel-18
Rel-19
Rel-20
Rel-21

## Slide 3: Potential Scope for Rel-20 UAV/UAM enhancements
Justification for connected mode mobility enhancements
  Altitude/zone based CHO execution conditions
    Altitude based measurement reporting conditions such as AxHy and Hy events were introduced for aerial UEs, but these conditions cannot be used as CHO execution conditions. AxHy can be useful for selecting a candidate cell and trigger mobility to the cell. For example, A3H1/A3H2 can be used to trigger conditional mobility for aerial UEs going upward/downward, respectively. Required specification efforts to support conditional AxHy are quite small. Altitude based CHO execution conditions can be generalized to zone-based CHO execution conditions.
  Altitude-dependent handover candidate cell list selection
    For aerial UEs, intended mobility candidates can be different for different UE altitude. For example, network may provide cells dedicated for aerial UEs with altitude higher than a threshold. In this scenario, if UE is handed over to a cell not intended for aerial UEs, connection status is less reliable and ping-ping or radio link failure may happen shortly after the handover. For more reliable connection status, UE at high altitude is desirable to avoid handover to a cell intended only for non-aerial UEs. Similarly, handover to a cell intended for aerial UEs is desirable for aerial UEs at high altitude. For this purpose, excluded/allowed list in measurement object for measurement report can be simply enhanced to support altitude-dependent excluded/allowed list.
    For CHO, altitude-dependent mobility candidate validation can be introduced, which is straightforward to implement in specifications.
  Measurement report enhancements
    In Rel-18, measurement report was enhanced to trigger measurement report only when more number of neighbor cells than threshold satisfy the reporting condition. While the enhancement intends to suppress continuous measurement report triggered by strong LOS neighbor cells, it may unintentionally suppress measurement report that were useful, if reported, for network to better understand interference situation. In our view, further enhancements to measurement is beneficial to achieve better trade-off between measurement report reduction and interference reporting.
Proposed scope
  Support of existing AxHy conditions for CHO execution conditions (R2).
  Support of altitude-dependent mobility candidate down-selection (R2)
    Altitude-dependent excluded/allowed list in measurement object for measurement reporting (RRC_CONN.)
    Altitude-dependent candidate cell validation for CHO (RRC_CONN.)
  Measurement report enhancements for better trade-off between interference reporting and measurement report reduction (R2)

## Slide 4: Potential Scope for Rel-20 UAV/UAM enhancements
Justification for idle mode mobility enhancements
  Altitude-dependent beam set selection
    In Rel-18, altitude-dependent RS sets are introduced to cope with vertically changing radio environments in RRC_CONNECTED. With the altitude-dependent RS sets, the effective coverage shape becomes less fragmented. Since altitude-dependent RS sets is not supported for UEs in RRC_IDLE/INACTIVE, aerial UEs experience line-of-sight propagation from neighbor cells and detect down-tilted beams of a far neighbor cell as good beams and consequently reselect the cell. In this case, the UE is likely to experience degradation of the cell quality shortly after reselecting the cell, and as a result, another selection would be triggered, i.e., ping-pong occurs frequently. To avoid unnecessary reselection, altitude-dependent RS set selection is beneficial.
  Altitude-dependent cell selection candidate down-selection
    For aerial UEs, intended mobility candidates can be different for different UE altitude. For example, network may provide cells dedicated for aerial UEs with altitude higher than a threshold. In this scenario, if aerial UE at high altitude happens to reselect a cell not intended for aerial UEs, it is likely that UE reselects another cell again in a short time due to fragmented cell coverage being experienced by the UE. To avoid unnecessary cell reselection, UE at high altitude is desirable to avoid reselecting a cell intended only for non-aerial UEs. Similarly, cell reselection to a cell intended for aerial UEs is desirable for aerial UEs at high altitude.
Proposed scope
  Support of altitude based beam set selection for measurements in RRC_IDLE/INACTIVE (R2)
  Support of altitude-dependent neighbor cell list (excluded/allowed list) in SIB3/4 for cell reselection (R2)

## Slide 5: Potential Scope for Rel-20 UAV/UAM enhancements
Justification
  Radio conditions of aerial networks are quite different from those of TN mainly due to strong LOS relation with multiple neighbor cells. Furthermore, since KPI of aerial UEs are strongly affected by temporary/local environmental factors, such as weather (wind, rain), optimization of aerial networks requires significant amount of data collection of radio channels and corresponding KPIs. These require mobile operators to invest growing expenditures for optimization of UAV/UAM networks.
  To reduce mobile operators’ expenditures in deploying and operating UAV/UAM network, SON/MDT enhancements dedicated to UAV/UAM are beneficial.
Proposed scope
    Enhancements for SON/MDT for aerial networks
    Aerial UE specific logging events, such as logging of orientation, vibration or any other vehicle movements caused by environmental factors, and altitude-related logging events.
    Note1: We look forward to hear views from operators and infra-vendors for the best scope of SON/MDT for UAV/UAM network optimization.
    Note2: Enhancements of SON/MDT for aerial networks can be done in Rel-20 SON/MDT WI, if SON/MDT WI is established.

## Slide 6: Conclusion
LGE view
    Enhancements to UAV/UAM in Rel-20 are necessary to be prepared for rapidly-growing UAV/UAM industry as well as 6G 3D mobility
Preferred Work Scope
  Connected mode mobility enhancements for aerial UEs (R2)
    Altitude/zone-based CHO execution conditions
      Support of using existing AxHy for CHO execution conditions.
    Altitude-dependent handover candidates selection
      excluded/allowed list in measurement object for measurement reporting
      Altitude-dependent candidate cell validation for CHO
    Measurement report enhancements for better trade-off between interference reporting and measurement report reduction
  Idle mode mobility enhancements for aerial UEs (R2)
    Support of altitude-based beam set selection for measurements
    Support of altitude-dependent neighbor cell list (excluded/allowed list) for cell reselection
  SON/MDT enhancements for aerial UEs (R2/R3)
    Aerial UE specific logging events, such logging of orientation, vibration or any other vehicle movements caused by environmental factors, and altitude-related logging events.
    Note1: We look forward to hear views from operators and infra-vendors for the best scope of SON/MDT for UAV/UAM network optimization.
    Note2: Enhancements of SON/MDT for aerial networks can be done in Rel-20 SON/MDT WI, if SON/MDT WI is established.