## Slide 1: Views on Rel-20 Ambient IoT
3GPP TSG RAN Meeting #106
Madrid, Spain, December 9-12, 2024
Agenda Item: 15.2
RP-242474

## Slide 2: Background
During Rel-19 NR standardization, study on solutions for Ambient IoT was performed[1][2]
  Rel-19 SI is expected to be completed in RAN#106 in December 2024
  Follow-up Rel-19 WI for the 1st phase of standardization of Ambient IoT for NR is expected to start
Standardization of Rel-20 NR will start from June 2025
  First package of Rel-20 WIs/SIs will be approved in RAN#108 in June 2025
  It is expected to start the 2nd phase of standardization of Ambient IoT for NR in Rel-20
In general, WI scope of Rel-19 Ambient IoT should focus on essential scenarios/features for the first step deployment based on the outcomes of Rel-19 study, where;
  Target scenarios/topologies focus on indoor, topology 1, DO-DTT and DT, and FR1 licensed FDD spectrum
  Target device types focus on device type 1 and 2a
  PHY layer design to support the target scenarios/topologies/device types
  L2 protocol structure and new A-IoT MAC PDU formats for data, control, and paging
  A-IoT paging (focusing on a single reader scenario) and random access
  RAN architecture and signaling and procedures for CN-RAN interface (NGAP enhancement)
  [1] RP-234058, New SID: Study on solutions for Ambient IoT (Internet of Things) in NR
  [2] 3GPP TR 38.769 V1.1.1, Study on solutions for ambient IoT (Internet of Things)

## Slide 3: Discussion on Rel-20 Ambient IoT (1)
Rel-20 Ambient IoT should expand use case scenarios with the support of extended scenarios/topologies and enhanced functionalities compared to Rel-19 Ambient IoT
For extended scenarios/topologies, we propose to support the following:
  Topology 2
    To support Deployment scenario 2 (device indoors, BS outdoors) for all devices (1/2a/2b)
  FR1 licensed TDD and DO-A traffic scenarios
    These two may require study for the first few months in Rel-20
  Device 2b
    To support the use cases that require ~ 50 meters or larger coverage
    To support FR1 licensed FDD spectrum without any spectrum regulation issues
  Large frequency shift for device type 2a (if feasible)
    To expand the use case scenarios in FR1 licensed FDD spectrum (e.g., to support the case where CW2D is in DL and D2R is in UL in FR1 licensed FDD spectrum without any spectrum regulation issues)
    To support the case where readers do NOT have (enough) in-band full-duplex (or SIC) capabilities

## Slide 4: Discussion on Rel-20 Ambient IoT (2)
For enhanced functionalities, we propose to support the following:
  Coverage extension
    To improve indoor coverage for Device 1/2a, or to improve indoor/outdoor coverage for Device 2b
    Depending on Rel-19 work scope, the techniques to enable this would include repetition, retransmission, CW node control/coordination, etc.
  Capacity enhancements
    To support the use cases that require larger connection density or shorter inventory latency compared to Rel-19
    Depending on Rel-19 work scope, techniques to enable this would include enhancements of resolution of TDMA/FDMA (e.g., support of sub-slot for TDMA, 2-dimensional TDMA and FDMA, etc.) and inter-reader coordination
  Enhancements of proximity detection accuracy/coverage
    To support the proximity services that require higher accuracy/coverage compared to Rel-19
    E.g., dedicated signals and/or procedures for proximity determination can be considered for improved accuracy/coverage

## Slide 5: Discussion on Rel-20 Ambient IoT (3)
For enhanced functionalities of RAN2, we propose to support the following:
  D2R scheduling enhancements
    To enhance D2R scheduling considering device’s remaining energy level, segmentation, and D2R message size information.
      A-IoT device may not have sufficient energy to perform the remaining D2R transmissions.
      If A-IoT message size is larger than the maximum TB size, segmentation functionality is required.
      If CN does not provide the D2R message size, message size reporting from device to the reader can be considered. It is also helpful for D2R scheduling.
    D2R scheduling enhancements for Rel-20 A-IoT includes:
      Energy status indication
      Segmentation (if required)
      Message size reporting (if required)
  Support of R2D FDMA
    If FDMA is applicable for R2D direction, the enhancements includes:
      Paging mechanism for R2D FDMA
      RA enhancements for R2D FDMA

## Slide 6: Discussion on Rel-20 Ambient IoT (4)
For enhanced functionalities of RAN2 and RAN3, we propose to support the following:
  A-IoT paging enhancement to support multiple reader scenario
    Paging associated to the same service request may be sent from multiple readers in case of paging for wide area covered by multiple cells, overlapped cell scenarios, and localization/positioning. In some scenarios, particularly, localization/positioning, duplicated responses from a device need to be allowed.
    Paging from multiple readers and duplicated responses from a device are considered.
  Support of topology 2
    The radio resources used by A-IoT radio interface between A-IoT devices and UE reader is controlled by network and the resources are configured to the UE reader via dedicated signaling according to the Rel-19 SI results.
    For support of topology 2, study and specify the followings:
      Down-selection on solutions (i.e., RRC-based, UP-based) for conveying A-IoT upper layer information
      A-IoT radio resource request/assist information from IN UE to gNB
      A-IoT radio resource control/allocation
      A-IoT radio resource validity

## Slide 7: Recommended scope of Rel-20 Ambient IoT WI (1)
Rel-20 Ambient IoT should include extension of scenarios/topologies and enhancements of functionalities supported by Rel-19 Ambient IoT standards
On top of Rel-19 standards, Rel-20 Ambient IoT standardization supports:
  Extended scenarios/topologies, i.e.,
    Topology 2, DO-A, and TDD
  Device type 2b
  Large frequency shift for, e.g., device type 2a
  Coverage extension by, e.g.,
    Repetition, retransmission, CW node control/coordination, etc.
  Capacity enhancements by, e.g.,
    Enhancements of resolution of TDMA/FDMA
    Inter-reader coordination
  Enhancements of proximity detection accuracy/coverage

## Slide 8: Recommended scope of Rel-20 Ambient IoT WI (2)
On top of Rel-19 standards, Rel-20 Ambient IoT standardization supports (continued) :
  D2R scheduling enhancements
    Energy status indication
    Segmentation (if required)
    Message size reporting (if required)
  Support of R2D FDMA
    Paging enhancements for R2D FDMA
    Random access enhancements for R2D FDMA
  A-IoT paging enhancements, i.e.,
    Enhancement to support paging from multiple readers and duplicated responses from a device
  Support of topology 2
    A-IoT radio resource request/assist information from IN UE to gNB
    A-IoT radio resource control/allocation
    A-IoT radio resource validity
    Down-selection on solutions (i.e., RRC-based, UP-based) for conveying A-IoT upper layer information

## Slide 9: Summary of views on Rel-20 Ambient IoT
WI scope of Rel-19 Ambient IoT should focus on essential scenarios/features for the first step deployment based on the outcomes of Rel-19 study
On top of Rel-19 Ambient IoT standardization, Rel-20 Ambient IoT should include extension of scenarios/topologies and enhancements of functionalities
  Details of recommended scope for Rel-20 Ambient IoT are listed in page 7-8 of this document