## Slide 1: Rel-20 enhancements for future deployments
3GPP TSG RAN Meeting #106 RP-242543
Madrid, Spain, 9-12 December 2024
Source: Vodafone
Agenda Item: 15.2

## Slide 2: Rel-20 enhancements for future deployments
Rel-20 should consider enhancements for future deployments of band n104 which was identified for IMT at WRC23 and is now starting to be allocated in certain jurisdictions.
  Justification:
  Band n104 is only specified for up to100 MHz UE channel bandwidth. If large bandwidths are assigned, greater spectral efficiency can be achieved if this is increased.
  Propagation differences between n78 and n104.
  Band n104 provides a possibility to improve beamforming efficiency with narrower beams and higher dimension MIMO.
  This band is expected to have collocated deployments with other bands e.g. n28, n1, n41, n78, etc.
  Objectives:
  Definition of larger bandwidth in FR1 -> Support of 200 MHz channel bandwidth.
  Increase the number of SSB beams from 8 (as legacy) to 16 (narrower beams) in FR1.
  Both UL and DL coverage enhancements (HPUE e.g. PC 1.5 for UL. At least both PDSCH and SSB for DL).
  Higher frequencies enable larger number of antenna ports -> MIMO improvements are beneficial.
  Inclusion of more inter-band combinations (only CA of n78 and n104 is currently specified).
  [1] Link to Press Release
  [2] Link to Press Release

## Slide 3: Thank you