## Slide 1: Proposal for Release 20 5G-Advacned MIMO
KDDI Corporation
3GPP TSG RAN Meeting #106
Madrid, Spain, December 9-12, 2024
RP-242561

## Slide 2: Motivation
Regarding NR MIMO, further functionality enhancements are desired from the following perspectives.
  For further performance improvement in FR1
    Multi-TRP deployment
      To further increase cell capacity and improve communication quality at the cell edge, it is desirable to increase the number of antenna elements for massive MIMO. However, Japan has high requirements for wind loading and it is difficult to install very large antenna panels, so a distributed deployment of antennas of a certain size is desirable.
      In the distributed deployment of antennas, it is desirable not only to use newly introduced massive MIMO antennas, but also to be able to divert existing antennas.
    TDD operation
      In TDD systems, it is common to utilize the reciprocity between uplink and downlink to generate a downlink MU-MIMO precoder, but there is a need for improved accuracy in link adaptation.
  To further increase the utilization of FR2
    Beam management
      The 28GHz (n257) in FR2 spectrums is not being fully utilized in Japan. To make FR2 more accessible, further advancements in MIMO beam management are also needed.

## Slide 3: Potential enhancement areas of NR MIMO in Release 20
For multi-TRP deployment
  Further improvement of communication quality in the cell edge area. ⇒ Increase in the number of TRPs that can be coordinated together is needed.
  Further enhancement of capacity. ⇒ Increase in the number of DMRS ports for MU-MIMO is expected.
  Improvement in the degree of freedom of deployment of distributed TRPs, including support of various types of TRPs and dynamic change in the number of antenna ports by network energy saving features. ⇒ Coordination of TRPs with different number of antenna ports and/or with different transmission power (TP).
For TDD operation
  Improvement of link adaptation accuracy. ⇒ Measurement reports of observed interference at UE.
For beam management
  To reduce beam application latency after a UE-initiated (UEI)/event-driven (ED) beam reporting. ⇒ If schemes such as pre-synchronization, activation without RRC and/or MAC CE signaling remain as leftovers from Rel. 19, they need to be specified in Rel. 20.
?
Interference
component
TDD
Different number
of antenna ports and/or different TP
UEI/ED beam reporting
ACK
Beam
application
1) Increase in the number of coordinated TRPs.
2) Increase in the number of DMRS ports.
3) TRPs with different number of antenna ports and/or different TP.
4) Measurement reports of observed interference at UE.
5) Leftovers related to BM from Rel. 19 if needed.

## Slide 4: Potential objectives
Potential objectives should include the following.
  Study, and if justified, specify the increased number of TRPs that can be coordinated together.
    Type-II codebook refinement for CJT, SRS enhancement and CJT calibration reporting enhancement can be considered.
  Study, and if justified, specify the increased number of DMRS ports for MU-MIMO.
  Study coordination of TRPs with different number of antenna ports and/or different transmission power.
    Consideration is needed starting with how to handle MIMO between TRPs with different numbers of antenna ports and/or different transmission power in the standard.
  Study, and if justified, specify measurement reports of observed interference at UE for TDD reciprocity-based MIMO.
  Specify schemes to reduce beam application latency after a UE-initiated/event-driven beam reporting if they remain as leftovers from Rel. 19.