## Slide 1: Discussion on checkpoints for Rel-19 XR

## Slide 2: Checkpoints for multi-modality in RAN
There are two checkpoints related to support of multi-modality in RAN.
All notes clearly said that SA2 and/or SA4 output/confirmation is required to specify something for this objective.
Thus, it is important to check reply LS from SA2 and SA4 for the RAN2 LS (R2-2409272) on multi-modality awareness sent in October RAN2 meeting.
Careful checking of SA2 and SA4 conclusion for multi-modality awareness is essential for this objective.

## Slide 3: SA2 conclusion on multi-modality awareness
SA2 discussed RAN2 LS (R2-2409272) on multi-modality awareness in November SA2 meeting and the following is revised as the final version of reply LS from SA2.
The reply LS shows that MMSID can be provided to the NG-RAN and RAN3 also confirm that it is technically feasible to enhance NGAP to provide the MMSID to NG-RAN node.
Even though approval of this SA2 reply is finally postponed to the next meeting due to urgent reply LS from SA4, the clear SA2 understanding is that MMSID can be provided to the NG-RAN. Based on this, the following in the first NOTE can be removed from the R19 XR WID.
  This is subject to alignment with SA2, e.g., if MMSID is not available from CN, then UE assistance information-based approach as an alternative.
UE assistance information-based approach for multi-modality in RAN is not needed and can be removed from the R19 XR WID.
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 4: SA4 conclusion on multi-modality awareness
SA4 also discussed RAN2 LS (R2-2409272) on multi-modality awareness in November SA4 meeting and the urgent reply LS is approved in S4-242223.
SA4 has concern and skeptical to have multi-modality awareness in NG-RAN due to following reasons and other WGs should respect SA4’s concern before adding a new work scope for this objective.
  Only the application layer can determine how to handle the case when the QoS flow for one modality cannot be established, e.g. due to RAN resource limitations.
  The conditions under which particular QoS flows are considered essential for an application to continue are application specific and cannot be determined by 5GS.
SA4 have skeptical to have multi-modality awareness in NG-RAN.
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 5: SA4 conclusion on multi-modality awareness
Another answer in the SA4 reply addressed two important points as shown below.
For packet level synchronization, SA4 indicate that the current mechanism can provide frame level synchronization which is sufficient for traffic synchronization and there is no evidence to suggest per packet inter-modal synchronization needed for XR services.
For PDU Set discard, SA4 recommended that not jointly discard packets across multi-modal flows since receiving packets for some modalities enables the application to use the received modalities to better manage the user experience.
SA4 have concerns to have traffic synchronization and PDU Set discard across QoS flows of the same multi-modal service considered in RAN2.
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 6: Conclusion and Proposal
Based on the following observations, it is doubtful to have an objective to support for multi-modality in RAN for UL and DL.
  Careful checking of SA2 and SA4 conclusion for multi-modality awareness is essential for this objective.
  Based on SA2 conclusion, UE assistance information-based approach for multi-modality in RAN is not needed and can be removed from the R19 XR WID.
  SA4 have concerns to have traffic synchronization and PDU Set discard across QoS flows of the same multi-modal service considered in RAN2.
  SA4 have skeptical to have multi-modality awareness in NG-RAN.
Thus, it is proposed to remove the objective for multi-modality support from the Rel-19 XR WID like below.