## Slide 1
3GPP TSG RAN #106 RP-242629
Madrid, Spain, December 9-12, 2024
Agenda Item: 15.2
Source: vivo
Title: Views on normative work for AIML based mobility enhancements in 5G-A Rel-20
Document for: Discussion & Decision

## Slide 2
Views on normative work for AI/ML based mobility enhancements (RAN2 led, WI)
Motivation:
  Study item “SID on AIML for mobility in NR” is to be finished within Rel-19. The preliminary simulation results in RAN2 so far have showed that the significant gains can be achieved (further simulations are ongoing).
    For Measurement reduction, at least for 50% measurement reduction can be achieved, without significant degradation in mobility performance compared with legacy L3 HO in the metrics such as HOF, Ping-pong, data interruption time, and average TOS;
    For Handover performance improvement, mobility performance can be significantly improved compared with legacy handover.
  LTM/CHO can significantly improve the handover performance and are very important features. It is expected that AI/ML based mechanism can also introduce gain for the existing LTM/CHO. The new use cases can be studied in Rel-20.

## Slide 3
Views on normative work for AI/ML based mobility enhancements (RAN2 led, WI)
Consider the following objectives as starting point:
  RRM measurement prediction with both UE-sided model and NW-sided model [RAN2]
    Both cell-level prediction and beam-level prediction (for RACH resource configuration).
    Temporal-domain prediction for HO performance improvement (Case A) and measurement reduction (Case B).
    Spatial-domain prediction for measurement reduction.
    Frequency-domain prediction for measurement reduction.
    Investigate and specify potential specification enhancements, e.g., measurement results derivation(including beam selection/consolidation and L3 filtering due to the introduction of prediction results), signaling enhancement based on the existing measurement configuration/report framework.
  Measurement event prediction with UE-sided model [RAN2]
    Focus on indirect event prediction based on RRM measurement prediction.
    Investigate and specify potential specification enhancements, e.g., new event-triggering scheme (e.g., TTT ignoring) based on prediction results.
  [RLF prediction with UE-sided model [RAN2]]
    Focus on indirect RLF prediction based on RRM measurement prediction.
    Investigate and specify potential specification enhancements
  Study potential new use cases, e.g., AI-based LTM, AI-based CHO
  Identify and specify AI mobility specific enhancement based on the LCM framework of AI/ML NR air interface in Rel-19 [RAN2]
    AI mobility specific data collection for model training and model management
  Identify RAN4 specification impact on testability, interoperability, and RRM requirements and performance [RAN4]