## Slide 1
Views on 5G-A WIs & SIs in Rel-20
3GPP TSG RAN Rel-20 workshop RP-242651
Madrid, Spain, December 9-12, 2024
Source: TCL
Agenda item: 15.1

## Slide 2: General consideration on Rel-20
Both 5G-A evolution and 6G study will discussd in parallel in Rel-20, and some feature could be the same or similar, considering the workload we propose:
Proposal 1: only the WIs with clear commercial prospects could be considered in 5G-A Rel-20.
Proposal 2: avoid overlapping discussion on the same or similar topics in 5G-A and 6G;
Proposal 3: work balance should be considered carefully (About 50% TUs for 5G-A and 6G respectively is perferable)
  AIoT enhancement (RAN1)
  NTN & IoT NTN enhancement (RAN2)
  XR phase 4 (RAN2)
  NES enhancement (RAN1)
  MIMO phase 6 (RAN1)
  Further evaluation of SBFD (RAN1)
  Further enhancements of MC (RAN1)
  Further coverage enhancements (RAN1)
  AI/ML for Air (RAN1)
  AI/ML for mobility (RAN2)
  ISAC (RAN1)
  Potential 5G-A WIs in Rel20
Performance enhancement
Capability extension
Network extension

## Slide 3: AI/ML for Air
Motivation:
In Rel-19, we already identified the theoretical benefits of the recommended use cases in PHY and RAN. In Rel-20, we should strive for a feasible solution to make these approaches practical for the air interface.
This work will lay a solid foundation for the next step of evolution towards an AI-oriented 6G. Enlightened by the studied use cases and related considerations, we may extend the solutions or schemes to other use cases.
  Objective:
Beam Management:
    A unified framework of beam management and beam failure recovery/detection based on prediction.
    Joint data collection in different LCM stage for overhead reduction.
Positioning accuracy enhancement
    Specification impact for 2nd priority cases, i.e., Case 2a and Case 2b.
Two-sided Model
    CSI Compression as a starting point: Temporal enhancement ,overhead reduction, residual error correction, etc.
    Study other use cases of two-sided model in PHY, e.g., the modulation/demodulation.
Other aspects
    Unified framework for model monitoring in different use cases.
    ID based AI/ML process control framework, e.g., the model/ functionality ID, associated ID, etc.
    Strive for a unified design across use cases
    Reduce overhead to achieve energy efficiency

## Slide 4: AI/ML for Mobility
Motivation:
In Rel-19, RAN2 focused on simulation results and observations on the agreed on prioritized scenarios and agreed assumptions, and evaluate the beneficial aspects based on the identified use cases.
In Rel_20, we will specify support for UE side and network side AI/ML based models for Mobility, including network signaling for configuration related to AI/ML based models and configuration for reporting predictions.
  Objective:
RRM measurement prediction:
    UE-side RRM measurement prediction:
    Consider the configuration and reporting mechanisms for different RRM measurement predition cases;
    NW-side RRM measurement prediction:
    Study how the NW can obatin the vaild inference input for the NW-side model.
Measurement event prediction:
    Consider the necessarity of studing measurement event prediction, such as unnecessary handover avoidance, HOF decrease;
    Clarify the representative use cases and performance metrics, the direct measurement event prediction can be regarded as a starting point.
RLF use case
    Further clarification on the use case e.g. metrics

## Slide 5: AIoT enhancement
Motivation:
Rel-19 focus on basic functionalities and applications
    Harmonized air interface design for device 1/2a/2b
    Focus on indoor scenarios to study
    Only consider inventory/command operation
    DT or DO-DTT is only considered for signaling design and random acess
    Co-existence and RF requirement study
Standardisation for Ambient IoT could span more than one releases, enhancment design for other types of device and scenarios could be studied in Rel-20 or later.
  Objective:
  Rel-20 could focus on enhancement design, including
    Extend to outdoor scenarios
    Device with higher capability may be discussed
      Device 3 compatible with device 1 and 2 capabilities, or with higher capability than device 2 could be discussed to support wider coverage and higher data rate
    Positioning and sensing services may be discussed
    DO-DOA may be discussed in Rel-20 to support sensing services

## Slide 6: MIMO phase 6
Motivation:
As one of the key technologies of the physical layer, MIMO effectively addresses capacity and coverage issues. MIMO has undergone five stages of evolution, the final version of NR should focus on resolving some issues left over from previous versions, while also addressing some critical commercial needs.
  Objective:
UL transmission enhancement
    Specify UL frequency selective or high resolution precoding;
    Rel-19 leftover items for UL 3Tx, e.g. partially and fully coherent codebooks, etc.
BM management enhancement
    Specify UE initial BM for multi-TRP, multi-event, or multi-CC;
M-TRP transmission enhancement
    Specify NCJT support for up to 4 TRPs;
    Uniform TCI framework supports up to 4 QCLs for CJT and NCJT.
Higher Dimension MIMO at cmWave bands
    Specify more DMRS ports;
CJT/NCJT transmission

## Slide 7: NTN & IoT NTN enhancement
Motivation:
Release 19 NTN and IoT NTN proposed further enhancements offering optimized performance especially in terms of capacity, coverage and flexible mobility. As an evolution toward Rel-20, there is a discussion in SA1 to
Enhance existing use-cases such as emergency services
Support IMS voice services (e.g., MMTel, MC call) over narrowband Geostationary (GEO) satellite and
To support new use-case such as multi-orbit & robust notification for an IMS call under instable coverage
Enhancements in RAN to support above objectives shall be considered along with Rel-19 leftover enhancements related to coverage, flexible mobility.
  Objective:
Specify enhancements to support emergency & voice over narrowband GEO satellite
    PWS and UE initiated emergency access over satellite in 5G NR
    Latency, header compression & overhead reduction related enhancement of VoNR over GEO
Study enhancements to improve Handover & reselection such as :
    Enhancements to CHO to address latency .
    Group Handover to support a group of UEs simultaneously switch to the same cell
    QoS based network selection or mobility
Study enhancements to support the following new capabilities
    gNB DU onboard
    NTN coexistence in NR & Iot NTN e.g., in guard band or in band in
    Multi-orbit satellite access such as Orbit aware selection & reselection
    Robust paging notification for UE within low LOS/SNR region

## Slide 8: NES enhancement
Motivation:
In Rel-18 and Rel-19, several NES techniques in time/frequency/spatial/power domain were specified as following.
  In Rel-20, further enhancements for NES could be specified.
  Objective:
UL WUS in connected mode
    UL WUS applying for connected mode to request the network to adapt UE specific signals.
Cell DTX/DRX enhancement
    cell DTX/DRX applying for IDLE/Inactive mode and common signals
On-demand SSB enhancement
    Flexibility on-demand SSB pattern design, including PBCH/PSS/SSS
    On-demand SSB measurement enhancement based on UE MG reducing
Adaptation of multi-TRPs
    Current adaptation in spatial domain mainly focus on single TRP, dynamical TRP activation/deactivation can be further enhanced for multiple TRPs.
Rel-18 | Rel-19
cell DTX/DRX mechanism in connected mode | on-demand SSB Scell in connected mode configured with CA
CSI enhancements for spatial adaptation and power adaptation | on-demand SIB1 for UEs in idle/inactive mode
SSB-less SCell for inter-band CA for FR1 and co-located cells | adaptation of common signal/channel transmissions including SSB, Paging, PRACH
CHO procedure enhancement | 

## Slide 9: Further coverage enhancements
Motivation:
Multiple PRACH transmissions with different Tx beams can enhance the coverage in some cases, additional 1~3dB gain can be achieved compared to multiple PRACH transmissions with the same beam. Additionally, indicating a Tx beam can be beneficial for subsequent uplink transmissions.
Msg5 PUSCH is the coverage bottleneck during the initial access, but it does not support repetition transmission yet.
  Objective:
Specify following PRACH coverage enhancements (RAN1, RAN2)
    Multiple PRACH transmissions with different Tx beams for 4-step RACH procedure.
    UL beam indication based on multiple PRACH transmissions with different Tx beam for Msg3.
  Note 1: The enhancements of PRACH are targeting for FR2, and can also apply to FR1 when applicable.
  Note 2: The enhancements of PRACH are targeting short PRACH formats, and can also apply to other formats when applicable.
  Note 3: The multiple PRACH are transmitted over ROs associated with the same SSB.
Specify enhancements to support PUSCH repetition scheduled by DCI 0_0 with C-RNTI (RAN1, RAN2)

## Slide 10: ISAC
Motivation:
In Rel-19, RAN1 has studied the ISAC channel model and the typical use cases. In Rel-20, an SI can be conducted first, followed by a WI, with the goal of supporting basic sensing functionalities. The full sensing functionalities will be studied in 6G.
  Objective:
Sensing signal design (RAN1)
    Signal design integrated commnication and sensing;
    only focus on the gNB-based mono-static or bi-static sensing;
    only focus on the UAV detection and tracking;
Architecture, functionalities and protocols (RAN3)
    Architecture and functionality definition;
    CP based or UP based data transmission on the interface to CN;

## Slide 11: XR phase 4
Motivation:
It is foreseeable that XR will remain a primary research direction in the Rel-20. The technical enhancements required for XR in RAN including further enhancement on multi-modal, PDU Set based discarding enhancement, Mobility enhancement for XR traffic.
  Objective:
PDU Set based enhancement(Based on SA2’s progress in Rel-19)
    PDCP discarding enhancement considering AL-FEC PDUs and QoS flows’s content ratio info;
    PDU Set Based Handling enhancement considering change of PDU Set QoS parameter AQP(Alternative QoS Profile);
    PDU Set Based Handling enhancement considering DSCP marking information.
Mobility enhancement for XR
    The enhancement to the handover procedure based on PDU Set handling;
    The enhancement for dataforwading, SN status transfer, path switch procedure to keep the timely transmission of XR traffic.
Multi-mode data synchronous transmission mechanism enhancement in RAN
    UAI for multi-modal support in UL;
    Synchronization management mechanism for multi-mode data flows from single UE/multiple UEs;
    Synchronous transmission mechanism for multi-mode data flows from single UE/multiple UEs in RAN;
    Resource allocation mechanism for multi-mode data flows from single UE/multiple UEs in RAN.
Application
Server
5G network
Service data flows
5G UE (gloves)
5G UE (VR glasses)

## Slide 12: Further evaluation of SBFD
Motivation:
TDD is widely used in commercial NR deployments, due to resource configuration limited, it’s may result in reduced coverage, increased latency and reduced capacity. SBFD operation at gNB side within a conventional TDD band can improve UL coverage, UL capacity, and reduce UL latency, SBFD will be continue evalution in Rel-20.
  Objective:
SBFD operation across carries by intra-band CA (e.g. FR2) with different TDD configurations
    More scheduling flexibility;
    Potential handling of direction collision between different carriers;
Random access in SBFD symbols
    Random access in SBFD symbols for RRC connected UEs
    Random access in SBFD symbols for RRC idle/inactive UEs
  Full overlapped SBFD at gNB side
    CLI handle
    UE-specific configured

## Slide 13: Further enhancements of MC
Motivation:
MC can be used to improve the throughput, and also can improve utilization of different frequency bands since the user can be connected to both of low frequency cell with good coverage and decent throughput. Further to evaluate MC in Rel-20 is necessary.
  Objective:
Multiple-carrier scheduling with 2 stage DCI
    The first stage DCI includes common information
    The second stage DCI includes dedicated data scheduling information
Cross-carrier for Re-Tx
Enables the simultaneous scheduling of multiple PxSCHs and multi-cell coordination through a single DCI

## Slide 14: Conclusion
  AI/ML for Air (RAN1)
  AI/ML for mobility (RAN2)
  AIoT enhancement (RAN1)
  MIMO phase 6 (RAN1)
  NTN & IoT NTN enhancement (RAN2)
  NES enhancement (RAN1)
  Further coverage enhancements (RAN1)
  ISAC (RAN1)
  XR phase 4 (RAN2)
  Further evaluation of SBFD (RAN1)
  Further enhancements of MC (RAN1)
  5G-A WIs in Rel20
Higher Priority WIs
Othrs
Based on previous discussion, we propose to prioritize 5G-A WIs in Rel-20 as following: