## Slide 1: Enhancements to support Inter-UE CLI across gNBs
RAN#106
Madrid, Spain
Dec 09-12,2024
Agenda 9.3.1.2
RP-242771

## Slide 2
  Inter-UE CLI for R19 SBFD
  For R19 SBFD operation, there exist Inter-UE CLI issue when a aggressor UE is transmitting in SBFD symbol of UL sub band to its serving cell, this may cause interference to neighbouring near by Victim UEs receiving in the downlink sub-band(s) of SBFD symbol as shown in below figure.
  Inter-CU CLI issue can happen across UEs within same gNB and between neighbor gNBs as well.
  To mitigate Inter-UE CLI issue, RAN1/RAN2 WGs are actively discussing about L1 based UE-UE CLI measurement configuration and reporting .
  Inter UE CLI measurements can be CLI RSSI and/or SRS-RSRP based on measurement configuration
    SRS-RSRP measurements are based on SRS resource configuration
    CLI RSSI measurements are based on CLI time and PRB resource configuration

## Slide 3
  Inter-UE CLI for SBFD : RAN1#119 Agreement
  For L1 UE-to-UE CLI measurement and reporting, CLI measurements is performed within the active DL BWP and the following are supported
    Method#1: UE measures RSSI within DL subband
    Method#2: UE measures RSRP of aggressor UE within UL subband
    Method#3: UE measures RSSI within UL subband

## Slide 4
  Proposed enhancement to support Inter-UE CLI measurements (1 of 2)
For Method#1: CLI-RSSI measurement within DL subband is measuring leakage of UL transmission in UL subband into DL subband, so the measured CLI-RSSI could be relatively weak.
In addition, serving gNB is expected to mute DL transmission in DL subband on symbols overlapped with CLI-RSSI resource to avoid serving gNB DL subband scheduling interfering with CLI-RSSI resource transmitted in UL subband.
However, there could be still inter-cell DL interference in the measured DL subband. CLI-RSSI measurement from victim UE may also capture received power from DL transmission of neighbor gNBs, which makes CLI-RSSI measurement in DL subband not accurate.
Therefore, it would be beneficial to mute DL subband transmission from neighbor gNBs, which requires gNBs align configuration of CLI-RSSI resource and associated DL muting in time domain. Hence, gNB can mute its own DL transmission overlapped with CLI-RSSI resource within DL subband of neighbor gNB based on inter-gNB coordination.
For Method#3 : In addition, in case of Inter-gNB/cell Inter-UE CLI measurements in UL subband , serving gNB has to provide neighbor gNB aggressor UE’s CLI-RSSI resource configuration to its victim UEs for accurate measurement.
Based on above discussion, we have following proposal
Proposal 1 : Support inter-gNB coordination of CLI-RSSI resources, so that DL transmission can be muted across inter-gNB cells when DL subband CLI-RSSI is measured by victim UEs. (for both method 1 and method 3)

## Slide 5
  Proposed enhancement to support Inter-UE CLI measurements (2 of 2)
For method#2, victim UE measures SRS-RSRP in UL subband : This assumes that a gNB serving the victim UE provides SRS configuration for L1 based SRS-RSRP measurements.
As per RAN1 LS to RAN4 (R1-241060) indicated that
  Based on RAN1 discussion so far, RAN1 agreements didn’t differentiate inter-cell vs intra-cell scenarios
  For inter-cell UE-to-UE CLI measurement, same design as R16 L3 inter-cell UE-to-UE CLI measurement can apply to SBFD, and RAN4 can further discuss whether to reuse the same requirement as R16 or any new requirement is needed for R19 SBFD operation. In addition, to enable inter-cell inter-UE CLI, there should be some information exchange of the SRS-resource configuration, which is not specified so far.
In case of Inter-gNB/cell Inter-UE CLI measurements , serving gNB has to provide neighbor gNB aggressor UE’s SRS configuration to its victim UEs. This neighbor gNB SRS configuration is not always static configuration and may change in time and frequency domain, which can be periodic/semi-persistent as well.
In order to enable serving gNB configure (to its served victim UEs) correct neighbor gNB used SRS configuration , it is necessary to exchange SRS configuration to be used for L1 based inter-cell inter-UE CLI SRS-RSRP measurements.
OAM based approach does not support Inter-vendor interoperable solution within a operator and is not desirable in this scenario
Thus, we propose
Proposal 2: Support inter-gNB SRS configuration to support serving gNB to decide when to configure SRS-RSRP measurements for victim UEs in UL subband for inter-cell inter-UE CLI measurements. (for method 2)
Revised WID for R19 SBFD is available in RP-242772.