## Slide 1: Discussion on NR NTN for Rel-19
NTT DOCOMO, INC.
3GPP TSG RAN #106
Madrid, Spain, December 9-12, 2024
Agenda Item: 9.3.2.2
Document for: Discussion
RP-242817

## Slide 2: Overview
DL coverage enhancement in R19 NR NTN WI
Check point with respect to link level enhancement and system level enhancement
This document includes discussion on these enhancements
Study and specify if beneficial downlink coverage enhancements targeting support for additional reference satellite payload parameters covering both GSO and NGSO constellations operating in FR1-NTN or FR2-NTN [RAN1, RAN2, RAN4]
Define additional reference satellite payload parameters assuming power sharing among satellite beams or different satellite beam patterns/size (i.e. wide or narrow) across the satellite footprint, such that satellite beams may not all be simultaneously active or may be active below the nominal EIRP density per satellite beam (see section 6.1.1 in TR 38.821) due to limited power and limited feeder link bandwidth.
Define the corresponding power sharing assumptions and necessary link level and system level evaluation methodology and relevant KPIs for evaluations of the coverage, to allow for identification of physical channels/signals and system-level aspects that need enhancements and the corresponding needed improvements.
Study and if needed specify solutions, including link level enhancements for FR1-NTN (e.g. for PDCCH, PDSCH) and/or system level enhancements for FR1-NTN and/or FR2-NTN, allowing dynamic and flexible power sharing between satellite beams or different satellite beam patterns/size (i.e. wide or narrow) across the satellite footprint.
  RAN1 to report at the latest by RAN#106 with the list of targeted physical channels/signals for link level enhancements (if any), and with the targeted system-level enhancements (if any)
  RAN1 should report on impact to backward compatibility, if any, for potential extension of the SSB periodicity at the latest by RAN#106, in conjunction with the targeted system-level enhancements.
Notes for this objective:
  SSB channel enhancement other than SSB periodicity extension is not considered
    RAN1 should consider issues such as UE’s cell search complexity and impact to initial cell selection, latency and success rate, for the above extension
  The SSB periodicity enhancements potentially defined in this WID only apply to NTN operation
  Antenna gain of UE shall be assumed to be -5.5dBi in case of smartphone in FR1-NTN, the UE is assumed to be a full duplex UE, and at least 2Rx are considered at the UE
  NGSO to be considered in priority: LEO Set-1 @ 600 km
  Rel-18 network energy saving techniques should be considered as baseline in the system level study

## Slide 3: DL coverage enhancement – link level enhancement
Agreement
Support PDCCH CSS Link level enhancement in Rel-19 for all CSS types except type 3.
The following techniques are for further study:
  PDCCH repetition, including:
    Option 1: Intra-slot PDCCH repetition
    Option 2: Inter-slot PDCCH repetition
  CORESET length (i.e. number of OFDM symbols) extension
  DCI format optimization (e.g. size reduction, etc)
Note: the same technique is intended to apply to all search space types targeted for link level enhancements
For the above techniques, at least the following aspects should be discussed for the relevant candidate techniques:
  Configuration
  Backward compatibility and UE behaviour of legacy UE
  Linked Search Space
  Blocking probability
  DCI format size budget
  Resource overhead
  Impact on CORESET0
Focus on coverage enhancement for set 1-3 with a target CNR of -8 dB for NR NTN DL coverage enhancements at link level.
FFS: whether to apply the selected solution to PDCCH CSS type3 and PDCCH USS
Agreement
For PDSCH with Msg4 Link level enhancement:
Support PDSCH repetition
  FFS: signalling design including number of repetitions
  FFS: impact on UE capability
Note: the target coverage enhancement to bridge the gap with respect to single Msg4 transmission is 2.8 dB
Focus on coverage enhancement for set 1-3 with a target CNR of -8 dB for NR NTN DL coverage enhancements at link level.
Agreement
For link level enhancement of PDSCH with SIB1:
Support PDSCH repetitions within 20 ms duration
  The number of repetitions is fixed to 2 repetitions
  Further discuss the specification impact for at least the following:
    Procedure and signaling (enabling repetitions, associated time resource determination, etc.)
Note 1: without the above PDSCH repetitions, the coverage gap is 2.2 dB to 4.6 dB depending on SIB1 size.
Note 2: Focus on coverage enhancement for set 1-3 with a target CNR of -8 dB for NR NTN DL coverage enhancements at link level.
Note 3: the above is not related to multiple SIB1 transmissions across 20 ms periodicities of SSB, which may not be available when the SSB periodicity is 160 ms or larger (if supported) depending on the SSB and CORESET multiplexing pattern.
Agreement
For PDCCH CSS (except Type-3) link level enhancements, support only PDCCH repetition for NTN.
FFS: intra-slot and/or inter-slot
RAN1 discussion status
  PDCCH, Msg4 PDSCH, and SIB1/SIB19 PDSCH were evaluated
  PDCCH for all CSS types except type 3, Msg4 PDSCH, and SIB1 PDSCH were agreed as R19 enhancement targets
  SIB19 PDSCH was discussed but there is no clear agreement so far
  For PDCCH for CSS type 3 and USS, no common understanding on whether the current spec is sufficient or not

## Slide 4: DL coverage enhancement – link level enhancement
Observation
  Naturally, enhancements of PDCCH / Msg4 PDSCH / SIB1 PDSCH can be within R19 scope
  For SIB19 PDSCH, although we believe that enhancement is necessary, it seems to be difficult to agree to introduce some enhancement
  For PDCCH for CSS type 3 and USS, although R17 M-TRP PDCCH repetition is applicable to NTN scenario with S-TRP, it seems that spec modification could be necessary for the following aspects:
    UE capability. FG 23-2-1 is defined without differentiation between M-TRP and S-TRP, which may imply NTN UE must support both to send this FG as “support”
    Blind decoding burden.
      The following two decoding behavior is assumed for M-TRP scenario since link status could be different e.g., due to blocking, and thus respective decoding is basically sufficient
        A: Two blind decoding (Decode of the first PDCCH + Decode of the second PDCCH)
        B: Three blind decoding (Decode of the first PDCCH + Decode of the second PDCCH + Decode of a soft-combined PDCCH)
      In R19 NTN scenario = S-TRP scenario, the issue is link budget and thus a single decoding with soft-combining will be enough. The above two decoding behavior may be excessive and undesirable from UE perspective
23-2-1 | PDCCH repetition | 1. Support of intra-slot PDCCH repetition based on two linked SS sets associated with corresponding CORESETs including PDCCH repetition for Type 3 CSS 2. Required number of BDs for the two PDCCH candidates 3. Support max number of overlaps when one of the linked PDCCH candidates uses the same set of CCEs as an individual (unlinked) PDCCH candidate per scheduled component carrier per slot | mTRP-PDCCH-Repetition-r17 { numBD-twoPDCCH-r17, maxNumOverlaps-r17, } | FeatureSetDownlink-v1700 | Component 2 candidate values: 2 or 3 Component 3 candidate values: {1,2,3, 5, 10, 20, 40} NOTE 1: UE supports PDCCH repetition for the following (basic) PDCCH monitoring capability: For type 1 CSS with dedicated RRC configuration, type 3 CSS, and UE-SS, the monitoring occasion is within the first 3 OFDM symbols of a slot. NOTE 2: for component 3, each unique pair of overlaps is counted as one. NOTE 3: This FG does not include supporting Two QCL-TypeD in time-domain overlapping CORESETs in FR2. | Optional with capability signalling

## Slide 5: DL coverage enhancement – link level enhancement
Proposal
  R19 NR NTN WI scope includes DL coverage enhancement of the following channels for link level
    PDCCH of CSS types except for type 3, Msg4 PDSCH, SIB1 PDSCH
  Discussion on PDCCH of CSS type 3 and USS is within R19 NR NTN WI scope
    RAN plenary to consider the following two options to update the WID text
      Option 1: keep the existing main bullet and the existing third sub-bullet of DL coverage enhancement, and add the above three channels to be specified
      Option 2: remove “study and specify if beneficial” “study and if needed specify solutions” from the WID text for DL coverage enhancement, while add a note not to preclude further discussion on PDCCH of CSS type 3 and USS
Study and specify if beneficial downlink coverage enhancements targeting support for additional reference satellite payload parameters covering both GSO and NGSO constellations operating in FR1-NTN or FR2-NTN [RAN1, RAN2, RAN4]
<Unchanged parts omitted>
Study and if needed specify solutions, including link level enhancements for FR1-NTN (e.g. for PDCCH, PDSCH) and/or system level enhancements for FR1-NTN and/or FR2-NTN, allowing dynamic and flexible power sharing between satellite beams or different satellite beam patterns/size (i.e. wide or narrow) across the satellite footprint.
  RAN1 to report at the latest by RAN#106 with the list of targeted physical channels/signals for link level enhancements (if any), and with the targeted system-level enhancements (if any)
  RAN1 should report on impact to backward compatibility, if any, for potential extension of the SSB periodicity at the latest by RAN#106, in conjunction with the targeted system-level enhancements.
  Specify repetitions of PDCCH of CSS types except for type 3, Msg4 PDSCH, and SIB1 PDSCH
<Unchanged parts omitted>
Study and specify if beneficial downlink coverage enhancements targeting support for additional reference satellite payload parameters covering both GSO and NGSO constellations operating in FR1-NTN or FR2-NTN [RAN1, RAN2, RAN4]
<Unchanged parts omitted>
Study and if needed specify the following solutions, including link level enhancements for FR1-NTN (e.g. for PDCCH, PDSCH) and/or system level enhancements for FR1-NTN and/or FR2-NTN, allowing dynamic and flexible power sharing between satellite beams or different satellite beam patterns/size (i.e. wide or narrow) across the satellite footprint.
  RAN1 to report at the latest by RAN#106 with the list of targeted physical channels/signals for link level enhancements (if any), and with the targeted system-level enhancements (if any)
  RAN1 should report on impact to backward compatibility, if any, for potential extension of the SSB periodicity at the latest by RAN#106, in conjunction with the targeted system-level enhancements.
  Specify repetitions of PDCCH of CSS types except for type 3, Msg4 PDSCH, and SIB1 PDSCH
    Note: It is not precluded to study, and specify if necessary, enhancments of PDCCH for CSS type 3 and USS
<Unchanged parts omitted>
Option 1
Option 2

## Slide 6: DL coverage enhancement – system level enhancement
RAN1 discussion status
  SSB periodicity extension up to 160 ms was agreed, though larger value is controversial
  Wider beam footprints for SSB and narrower beam footprints for PRACH and subsequent channels was discussed but there has been no consensus so far
Proposal
  Specify SSB periodicity up to 160 ms
    Periodicy beyond 160 ms is precluded
  Not include “Wider beam footprints for SSB and narrower beam footprints for PRACH and subsequent channels” within R19 NR NTN WI scope
Agreement
As part of the NTN DL coverage enhancements at both system level and link level, RAN1 to consider:
Extending the periodicity of the half frames with SS/PBCH blocks assumed by UE during initial access.
  Default value[s] with extended periodicity assumed by NTN UE for initial access can be:
    One [or more] values from the list {40ms, 80 ms, 160 ms, 320ms, 640ms}
Potential enhancements for transmitting the DL common channels using a wider beam footprint, while DL/UL dedicated channels (incl. PRACH) may be transmitted using a narrower beam footprint
Link-level enhancements for the following channels:
  PDCCH
  PDSCH with Msg 4
  PDSCH with SIB1/SIB19.
    Note: link-level enhancements for PDSCH with SIB1/SIB19 may be applicable to other SIBs, without additional specification impact.
  Note: the above does not imply that all the channels above will be enhanced, but all of them should be considered based on this agreement
Agreement
For NR NTN, support extended periodicity of the half frames with SS/PBCH blocks assumed by UE during initial access.
The maximum of the additional default value (apart from the existing 20ms value) is at least 160 ms.
  FFS: whether 320ms can be supported as the maximum of the additional default value instead of or in addition to 160ms
Observation
Backward compatibility for legacy UEs (i.e. Rel-17 and Rel-18 UEs) assuming a default SSB periodicity of 20ms is not guaranteed when SS/PBCH blocks periodicity is larger than 20ms within the cell used for initial frequency scan.
Legacy UEs (i.e. Rel-17 and Rel-18 UEs) are not expected to be able to camp on a cell with SS/PBCH blocks periodicity larger than 160 ms.