## Slide 1
Rel-20 AI/ML for Mobility
3GPP TSG RAN meeting #106
Madrid, Spain, Dec. 9th – 12th 2024
Ericsson
RP-242849

## Slide 2: Introduction
In Rel-19, the Study Item “Study on AI (Artificial Intelligence)/ML (Machine Learning) for mobility in NR” (RP-242393) is studying and evaluating the potential benefits and gains of the AI/ML aided mobility for network triggered L3-based handover.
The activity is studying the following:
  RRM measurement predictions [RAN2]
    Cell/beam-level measurement prediction including intra and inter-frequency
  HO failure/RLF predictions [RAN2]
  Measurement events predictions [RAN2]
RAN4 aspects are also considered, in particular the testability, interoperability, and impacts on RRM requirements and performances.
Simulation aspects take great part of the activity, since the focus is the evaluation of the prediction accuracy and the benefits on the network KPI

## Slide 3: Motivation
The Rel-19 activity for AI/ML for Mobility is ongoing and the results from simulations show that the usage of AI/ML is beneficial to L3-assisted mobility. This is an indication that the normative work can start in Rel-20, based on the outcome from the Rel-19 SI.
  Proposal 1: Approve a WI for AI/ML-assisted mobility for network-triggered L3 handover based on the outcome from the Rel-19 Study Item
However, the use cases which are most beneficial to the mobility should be prioritized during the normative phase, that is:
  RRM measurement predictions based on temporal/frequency/spatial predictions
  Measurement events predictions, based on indirect approach
Once the basic solution is agreed and specified, the usage of the cell clustering for the predictions might be considered, if time allows.
The remaining use cases i.e., RLF/HO failure predictions, may be de-prioritized
  Proposal 2: During the normative work consider the use cases from the study item which are most beneficial to mobility :
        Prioritize RRM measurement predictions based on temporal/frequency/spatial domain predictions and the measurement events predictions.
        If time allows treat the cell clustering as second priority, when the basic solution is done
        De-prioritize RLF/HO failure predictions

## Slide 4: Motivation
The scope of Rel-19 study is limited to L3 mobility only, however it might be beneficial to extend the usage of AI/ML to other mobility use-cases, as well. It was already discussed the possibility to include LTM during the Rel-19 activity, but this was rejected due to lack of time. Now, in Rel-20, an extension to LTM may be taken into consideration:
  An initial study phase is required to evaluate the benefits of AI/ML on LTM. However, we expect that most of the assumptions, simulations and evaluations from Rel-19 SI can be reused (at least for the LTM cell configuration phase).
  Additional simulations might be needed to evaluate the AI/ML benefits during the LTM pre-sync/execution phase.
  After the initial study phase, the LTM normative work can start during Rel-20, together with the L3 mobility normative work.
The Rel-19 study is limited to RRC_CONNECTED mode, whereas benefits could be achieved also by using AI/ML in RRC_IDLE/RRC_INACTIVE:
  An initial study phase is required to evaluate the benefits of AI/ML in RRC_IDLE/RRC_INACTIVE. However, it is expected that most of the outcome from RRM measurement prediction in Rel-19 SI can be reused.
  Benefits of AI/ML assisted early measurement reporting can be studied.
  Proposal 3: Include a study phase in the beginning of the WI, where the following use cases are studied, in parallel with the normative work:
      AI/ML assisted mobility for LTM
      AI/ML assisted measurements in RRC_IDLE/RRC_INACTIVE and reporting in early measurement reports.

## Slide 5: Proposals
To conclude, we have the following proposals for Rel-20 AI/ML for Mobility:
Proposal 1: Approve a WI for AI/ML-assisted mobility for network-triggered L3 handover based on the outcome from the Rel-19 Study Item
Proposal 2: During the normative work consider the use cases from the study item which are most beneficial to mobility:
  Prioritize RRM measurement predictions based on temporal/frequency/spatial domain predictions and the measurement events predictions.
  If time allows treat the cell clustering as second priority, when the basic solution is done
  De-prioritize RLF/HO failure predictions
Proposal 3: Include a study phase in the beginning of the WI, where the following use cases are studied, in parallel with the normative work:
  AI/ML assisted mobility for LTM
  AI/ML assisted measurements in RRC_IDLE/RRC_INACTIVE and reporting in early measurement reports.