## Slide 1
Views on Rel-20 5G-A Ambient IoT
China Unicom
3GPP TSG RAN#106
Madrid, Spain, December 9-12, 2024
Agenda Item: 15.2
RP-242917

## Slide 2
1 Motivation
Motivation
  R19 A-IoT is the first release of passive devices for 5G, 5G ecosystem should make more efforts to achieve commerial success for 5G-A vertical network.
  Based on R18 SA1 A-IoT requirements study and R18 RAN A-IoT SI TR, R20 A-IoT should focus on ourdoor scenario to support more use cases, such as outdoor inventory and command.
  The device price and network CAPEX should be taken into consideration from Day-1 design for R20 A-IoT.
    The device price is related to device design architecture, such as battery-less/ battery.
    The device price for R19 A-IoT could be comparable to RFID. For R20 A-IoT, the device price should be less than NB-IoT and the battery life should be longer than NB-IoT or even battery-less.
    R20 A-IoT deployment should reuse the existing BS sites location. and control the overall cost of network upgrading.

## Slide 3
2 Scenarios
Scenarios
  Ambient IoT is supported in Rel-19 for indoor scenario. Rel-20 Ambient IoT should focus on the outdoor scenario.
  Requirements on scenarios:
    Lower down the cost of network instruction and upgradation.
    Simplify the design of protocol and hardware.
    Support new use cases: logistics, sensor, power substation. The table below shows the views on different scenarios.
rUC | Applicable SA1 UCs / traffic scenarios | Views
rUC5: Outdoor inventory | 5.2 Medical instruments inventory management and positioning 5.4 Non-public network for logistics 5.7 Airport terminal / shipping port 5.16 Automated supply chain distribution | Indoor inventory has been supported in Rel-19, easy to be extended to outdoor scenario. High priority.
rUC6: Outdoor sensor | 5.3 Smart grids 5.19 Forest Fire Monitoring 5.22 Dairy farming 5.24 Smart manhole cover safety monitoring 5.25 Smart bridge health monitoring | New use cases and should be studied the traffic type and model. High prioriy.
rUC7: Outdoor positioning | 5.8 Finding remote lost item 5.9 Location service 5.12 Personal belongings finding | The Outdoor positioning is overpaid for current stage. Low priority.
rUC8: Outdoor command | 5.11 Online modification of medical instruments status 5.17 Device activation and deactivation 5.26 Elderly Health Care 5.30 Controller in smart agriculture | Indoor command has been supported in Rel-19, easy to be extended to outdoor scenario. High priority.

## Slide 4
3 Potential Objectives
Potential Objectives
  Use cases: Ambient IoT should prioritize rUC5 and rUC8. The rUC6 is also considered as high priority.
  Rel-20 Ambient IoT should support at least topology 1.
  The device types should support both battery-less devices and acitive device.
  Coverage: compared to outdoor macro BS coverage (>100m)
  Improving the networking capability
    Support large amount of battery-less devices and acitive devices;
    Support active devices with TX power of 0~10dBm.
  Frequency band for Ambient IoT
    Single band or dual-band: 900MHz, 2GHz;
    Spectrum: licensed FDD band.

## Slide 5
Thanks!