## Slide 1: Consideration on ISAC in 5G-A Rel-20
Agenda item: 15.2
Source: CATT
3GPP TSG RAN Meeting #106
Madrid, Spain, December 9-12, 2024
RP-243123

## Slide 2: Background
In Rel-19, channel modeling for Integrated Sensing And Communication (ISAC) is studied (RP-242348). The study aims to support object detection & tracking for the following sensing targets:
  UAVs
  Humans indoors and outdoors
  Automotive vehicles (at least outdoors)
  Automated guided vehicles (e.g. in indoor factories)
  Objects creating hazards on roads/railways, with a minimum size dependent on frequency
In RAN#105 checkpoint , there was no consensus to extend the scope in Rel-19
  Progress at RAN#105 was premature to pursue performance evaluation
It is expected that the study on ISAC channel modeling will be finished in time in Rel-19
  Progress after RAN#105 is smooth and good

## Slide 3: Motivation
It is desired to support sensing feature in 5G-A Rel-20
  To seize the urgent commercial need (e.g. low altitude economy) in 1~4 years from vertical industry, which can’t wait for the first version of 6G
  To extend 5G-A capability and life cycle, and accumulate experience for 6G standardization
Proposal 1: Support sensing feature in 5G-A Rel-20.
  At least support gNB-based sensing.
UAV detection & tracking
Sensing pedestrian/vehicle/obstacle
migrates
+
sensing

## Slide 4: Objectives in higher layer
High level consideration for gNB-based sensing
  Both gNB mono-static and gNB-to-gNB bi-static can be supported
  How to perform sensing by a gNB can be up to vendor’s implementation
  gNB-based sensing should be transparent to UE
Higher layer aspects for gNB-based sensing
  Architecture for sensing data transmission between RAN and sensing function
  Procedure for sensing data transmission between RAN and sensing function
  Coordination between NG-RAN nodes, e.g. for interference avoidance/reduction
Proposal 2: The following higher layer aspects are specified for gNB-based sensing,
  Architecture and procedure for sensing data transmission between RAN and sensing server;
  Coordination between NG-RAN nodes, e.g. for interference avoidance/reduction.
Sensing function
gNB#1
gNB#2
coordinate

## Slide 5: Objectives in physical layer
Performance evaluation
  Identification of sensing metric, sensing KPI, simulation assumption, etc.
  Performance evaluation, with specific waveform, RS, sensing mode, cooperation method, etc.
Physical layer aspects for gNB-based sensing
  Sensing measurement definition, node/mode/beam selection, etc.
  L1 enhancement, if necessary, e.g. multiplexing, waveform, RS design.
Proposal 3: The following physical layer aspects are considered for gNB-based sensing,
  Performance evaluation,
  Sensing measurement definition,
  L1 enhancement, if necessary.
Sensing function

## Slide 6: Conclusion
Proposal 1: Support sensing feature in 5G-A Rel-20.
  At least support gNB-based sensing.
Proposal 2: The following higher layer aspects are specified for gNB-based sensing,
  Architecture and procedure for sensing data transmission between RAN and sensing server;
  Coordination between NG-RAN nodes, e.g. for interference avoidance/reduction.
Proposal 3: The following physical layer aspects are considered for gNB-based sensing,
  Performance evaluation;
  Sensing measurement definition;
  L1 enhancement, if necessary.

## Slide 7
Notes: 万物互联，无限沟通
Universal Connectivity, Infinite Communication.