## Slide 1: Concerns on the proposed UE power class PC8 for FR2
Ericsson, Deutsche Telekom, Rogers, Vodafone, US Cellular, T-Mobile USA
3GPP TSG-RAN Meeting #106
Madrid, Spain, 9-12 December 2024
RP-243179

## Slide 2: The proposed lower power class PC8 for FR2
PC8 a UE with a ‘simpler antenna arrangement’: 6 dB lower peak EIRP, up to 9 dB lower UL spherical coverage and reduced DL coverage/performance than PC3 to simplify UE implementation and reduce UE power consumption
PC8 UEs would deteriorate further FR2 UL coverage and DL/UL performance overall in stadium and hot-spot scenarios; these scenarios are already challenging for PC3
  Concern that PC8 becomes the default implementation at the expense of PC3
No consensus at RAN4#113 on the introduction of PC8: TEI18 CRs not agreed
CCSA time plan an argument for its urgent introduction, but PC8 not discussed in CCSA
A ‘simpler’ UE antenna arrangement, but is degraded UL/DL performance good for E2E performance and promotion of FR2 deployment?
  a PC8 UE must implement all other FR2 features supported by PC3 handheld UEs

## Slide 3: Further background to PC8
Proposal in TEI18
  the PC8 antenna arrangement extended to all other UE types (April 2024), first wearables and later (Aug) extended to hot-spot and stadium scenarios
  a single 2 x 1 panel (like FR2 RedCap) instead of two 4 x 1 panels
WF at RAN4#112bis based on system simulations from one company [1]
The WF challenged at RAN4#113 based on NSA commercial traffic data and commercial devices; the impact of PC8 considered should this become the “default” for handheld UE [2]
No consensus in RAN4, restriction to China only or restriction to non-handhelds not agreeable either

## Slide 4: Proposal
Proposal:
consider methods for enhancing the (UE) FR2 ecosystem in a future study/work item – new power classes could be one objective – with due consideration of performance, instead of in a TEI item
  for all regions
Other observations:
FR2 power classes specified for FWA/Vehicular applications
RedCap UEs for smaller form factors, modules, CPE, industry terminals and wearables
FR2 PC3 for handheld UEs (also included in the CCSA standard)
The proposed PC8 essentially a PC3 with degraded UL coverage and UL/DL performance

## Slide 5: References
R4-2415628, “Discussion on introduction of new FR2 UE power class”, Huawei, HiSilicon (RAN4#112bis)
R4-2418873, “Reconsidering the proposed new FR2 power class 8 and its specification”, Ericsson, Telecom Italia, US Cellular