## Slide 1
Views on normative work for AIoT
3GPP TSG RAN meeting RAN#106
Madrid, Spain, December 9th – 12th2024
Agenda item: 9.1.1
RP-243181

## Slide 2: Views on WID Recommendation for RAN1
As per the Status Report on Ambient IoT provided by the Rapporteur(s) in RP-242965, the study on Ambient IoT is complete across all RAN Working Groups.
The following conclusions were agreed in the RAN1#119[1] meeting regarding the recommendation for the normative phase of the agenda on Ambient IoT.
Proposal 1: The inclusion or non-inclusion of design features such as line coding, proximity determination, CW waveforms, etc., for Ambient IoT should be based on detailed technical justifications. The decision for down-selection should be up to the WGs during the normative phase.
Proposal 2: The RAN Plenary should provide guidance on the inclusion of high-level features, such as device types, deployment scenarios, and topology considerations.

## Slide 3: Views of Harmonized Design
As per conclusion of the study, TR 38.769 indicates the feasibility for the harmonized design for the different device type.
We observe for bit rate of (5-7kbps) the coverage for device 1 to be (5m-25m) and 2b to be (15m- 4000m)[5].
Observation 1: There are significant differences in device characteristics across various device types based on their capabilities.
Proposal 3: The protocol design during the normative phase should take into account differences in device characteristics to ensure optimal utilization of their capabilities.

## Slide 4: View on Design Feature for Rel-19 RAN1 WID
Considering the workload and the time constraints associated with the Release-19 normative phase.
Proposal 4: AIoT should include two Release work items. For the Release-19 Work Item (WI), priority should be given to backscattering devices and limited deployment scenarios.
Based on our analysis [5], Topology 1 demonstrates superior performance compared to Topology 2 under the evaluation assumptions agreed upon for the Release-19 Study Item (SI). However, Topology 2 may be advantageous for coverage extension in outdoor-indoor deployments, where the reader is placed outdoors, and the device is indoors. Since a reader may not always be aware of whether the device is deployed indoors or outdoors, both D1T1 and D2T2 should be supported for effective deployment.
Proposal 5: For the Release-19 WI, both D1T1 and D2T2 should be prioritized.
Backscattering device types, such as Device 1 and Device 2a, rely on externally provided carrier waves (CW) for D2R transmissions. In Scenario A2, the serving reader or intermediate User Equipment (UE) provides the CW to the device, which introduces the constraint of requiring full-duplex capability at the serving reader or intermediate UE. In contrast, Scenarios A1 and B relax this requirement, eliminating the need for full-duplex capability at the serving reader or intermediate UE.
Proposal 6: For the Release-19 WI, Scenarios A1, A2, and B should be prioritized.
This approach ensures balanced development while addressing key deployment challenges and optimizing the performance of backscattering-based AIoT solutions.

## Slide 5: View on Design Feature for Rel-19 RAN1 WID
To support topology 2 the intermediate UE acting as a reader must be under the serving gNB control. For this control information should the provided to the intermediate UE to facilitate AIoT operation[4]. In our view option 2 (L1 signaling and higher layer signaling) provides higher degree of flexibility and efficient resource utilization.
Proposal 7: Option 2(L1 signaling and higher layer signaling) should be prioritized for controlling the intermediate UE in D2T2.
The line coding schemes for the R2D and D2R links various schemes were studied during the SI, in our analysis[2][3], and we found Manchester to perform better than PIE for R2D. Additionally, Manchester codes have constant transmission time due to 50-50 duty cycle unlike PIE.
Proposal 8: Manchester codes should be prioritized for the line coding schemes for the R2D link.
Considering the device complexity for modulation schemes on the R2D and D2R links, OOK 1 and OOK 4 should be supported based on the device's capabilities.
Proposal 9: For AIoT operation following modulation schemes should be considered:
  OOK1 and OOK4 should be prioritized for R2D.
  OOK and BPSK should be prioritized for D2R

## Slide 6: Conclusion
This section captures observations and proposals:
Observation 1: There are significant differences in device characteristics across various device types based on their capabilities.
Proposal 1: The inclusion or non-inclusion of design features such as line coding, proximity determination, CW waveforms, etc., for Ambient IoT should be based on detailed technical justifications. The decision for down-selection should be up to the WGs during the normative phase.
Proposal 2: The RAN Plenary should provide guidance on the inclusion of high-level features, such as device types, deployment scenarios, and topology considerations.
Proposal 3: The protocol design during the normative phase should take into account differences in device characteristics to ensure optimal utilization of their capabilities.
Proposal 4: AIoT should include two Release work items. For the Release-19 Work Item (WI), priority should be given to backscattering devices and limited deployment scenarios.
Proposal 5: For the Release-19 WI, both D1T1 and D2T2 should be prioritized.
Proposal 6: For the Release-19 WI, Scenarios A1, A2, and B should be prioritized.

## Slide 7: Conclusion
Proposal 7: Option 2(L1 signaling and higher layer signaling) should be prioritized for controlling the intermediate UE in D2T2.
Proposal 8: Manchester codes should be prioritized for the line coding schemes for the R2D link.
Proposal 9: For AIoT operation following modulation schemes should be considered:
  OOK1 and OOK4 should be prioritized for R2D.
  OOK and BPSK should be prioritized for D2R

## Slide 8: References
[1] Chair notes RAN1#119 (9.4 R19 Ambient IoT) v07
[2] R1-2408941, "Discussion on General aspects of physical layer design of AIoT", IIT Kanpur, Indian Institute of Tech (M), RAN1#118bis, Hefei, China, October 2024.
[3] R1-2410591, "Discussion on General aspects of physical layer design of AIoT", IIT Kanpur, Indian Institute of Tech (M), RAN1#119, Orlando, USA, November 2024.
[4] R1-2408943, "Discussion on Downlink and Uplink channel signal aspects for AIoT", IIT Kanpur, Indian Institute of Tech (M), RAN1#118bis, Hefei, China, October 2024.
[5] R1-2410590, "Evaluation assumption and results for AIoT", IIT Kanpur, Indian Institute of Tech (M), RAN1#119, Orlando, USA, November 2024.

## Slide 9
THANK YOU
Views on normative work for AIoT