## Slide 1: Rel – 20 Topics for NTN
Sourced by: CEWiT, Tejas Networks
Proposals on NTN enhancements for Rel 20 5G-A
3GPP TSG RAN Meeting #106
Madrid, Spain, Dec 09-12, 2024
Agenda Item: 15.2
RP-243185

## Slide 2: Background
NTN Deployments are ramping up, and 5G Advanced specifications are expected to be adopted worldwide.
Rel 18 and Rel 19 added necessary features to Rel 17 specifications to improve the NTN performance.
  This includes mobility enhancements, regenerative payload support, coverage enhancements, stored and forward operation, UE-Sat-UE feature, etc.
Release 20 should focus on the essential missing features that are important to enhance the NTN service adoption
Considering these facts, capacity improvement in the DL and resilient notification are the topics that should be prioritized in Rel 20.
This contribution provides the overview and possible RAN objectives on Resilient notification service enablement.

## Slide 3
Communication between Satellite and smartphone typically has minimal power margin and requires line of sight for best performance.
Mobile terminated calls/services, users with poor channel condition, might miss important calls/messages
Satellite access is the last option when a terrestrial network is not available, it will be beneficial to improve the user reachability in the satellite access system to achieve a better user experience.
This requires the satellite access system to be able to notify the user about missed incoming Mobile Terminated calls/messages etc.
SA 1 study concluded the possible consolidated proposed requirement and expected to be agreed as the normative requirement in the next meeting.
Stage 1 study refers to the Resilient notification service as a highly reliable and efficient notification mechanism that delivers notifications directly to user devices, such as smartphones, via satellite access.
CPR 7.1.2-1 on resilient notification in TR22.887 (S1-244656)
Subject to the operator’s policies, a 5G System with satellite access shall be able to support Resilient Notification Service to notify users, with valid subscription to the notification service, about a missed mobile terminated service when the user is unreachable via satellite access. NOTE: The Resilient Notification service can provide the user with service information e.g. caller’s information and service type.
Resilient Notification

## Slide 4
To enable resilient notification service RAN should define a channel carrying the notification message towards UE,
  Such channel should be highly reliable
Therefore, the proposed objectives are:
  Study and define robust channels for resilient notification service [RAN2, RAN1, RAN3].
    Study and define the protocol and signaling for resilient notification service [RAN 2].
    Study and define the physical layer channel and signaling for resilient notification service [RAN1].
    Study and define the NG interface signaling or resilient notification service [RAN3].
Proposed Objective

## Slide 5: Thank You !!