## Slide 1: Techniques for Network Energy Saving in 5G-A
RP-243186
3GPP TSG RAN Rel-20 workshop

## Slide 2
© CEWiT 2022
2
Introduction
Adapting the transmission/reception procedures at gNB to reduce energy consumption
  Based on traffic condition, UE feedback/assistance information, etc.
Motivation:
  Reduce energy consumption of network
  Reduce operational cost and environmental impacts
Rel. 18 studied various energy saving techniques in time, frequency, spatial and power domains
  Defined evaluation procedure, metrics and KPIs
  Analyzed various energy saving techniques in terms of Energy saving gains, effect on legacy operation and specification impacts.
The outcome of the study is captured in TR 38.864

## Slide 3
© CEWiT 2022
3
State of art
Rel. 18 WI focused on
  Adaptation of DTX/DRX pattern for gNB (Technique A-4)
    Configuration and activation/deactivation of DTX/DRX pattern
    Impact on various signals/channels and UE behavior
  Adaptation of spatial elements (Technique C-1)
    Port adaptation and TxRu adaptation
    Procedures and Configuration for determining the adaptation pattern
      Impacts on CSI-RS measurement and reporting framework
    Signaling exchanges and UE behavior
  Power adaptation (Technique D-1)
    Procedures and Configuration for determining the adaptation pattern
      Impacts on CSI-RS measurement and reporting framework
    Signaling exchanges and UE behavior

## Slide 4
© CEWiT 2022
4
State of art cont’d…
Rel. 19 WI focused on
  Adaptation of SSB and PRACH in time domain
    Dynamic adjustment of the SSB burst transmission periodicity for Scell based on network conditions
    PRACH adaptations
  On-demand SSB SCell operation for UEs in connected mode in CA
    Procedures and Configuration for indication of the adaptation of OD-SSB by gNB
      Signaling exchanges for OD-SSB
  On Demand SIB1 for UEs in idle/inactive mode for Case 2
    Case 2: UE obtains WUS configuration from Cell A, UE transmits UL WUS on NES Cell, UE receives on-demand SIB1 from NES Cell
    Procedures and signaling methods for WUS configuration and transmission of SIB1
    UE behavior

## Slide 5
Rel. 20 NES Proposals

## Slide 6
© CEWiT 2022
6
Enhancements for SSB adaptation in time domain
Rel. 19 SSB adaptation support
  Configuring multiple periodicities for SSB bursts for e.g., configuring two SSB patterns: One with large periodicity and other with smaller periodicity
  Enabling switching across the periodicities based on network conditions
Rel. 19 SSB adaptation is at SSB burst level with minimum flexibility
  Periodicities (both large and small) are common for all SSBs within the SSB burst
Rel. 19 SSB adaptation should be extended to SSB beams within a burst
  The network conditions (E.g., load, UE arrival rate, etc.) can vary across SSB beams within a burst
  Dynamic switching to lower/higher periodicity may not be needed for all beams within a burst
  Dynamic switching to lower/higher periodicity should be applicable at SSB beam(s) within an SSB burst
  Adapting number of transmitted SSBs within the SSB bursts for the SSB patterns with lower and higher periodicities

## Slide 7
© CEWiT 2022
7
Enhancements for SSB adaptation in time domain
Technique for adaptation SSBs within a burst was discussed in Rel.19 and dropped due to time constraints
  Adapting number of beams within SSB burst
  Periodicity adaptation for SSB beams
Impact on legacy UE can be minimized by
  Enabling the technique for scenario not involving legacy UEs (E.g., SSB configuration not applicable for legacy UE, enabling in Scell, etc.)
Performance evaluations
  Performance of adaptation of transmitted SSB within a burst is evaluated in a 21 cell deployment using Energy consumption model with set 1 and category 1 defined in TR. 38.864
  An NES gains of 35.18% & 31.92% is observed for low and light load scenarios respectively with a throughput degradation of -15.07 %.

## Slide 8
© CEWiT 2022
8
Extend Rel. 19 SSB time domain adaptations to beam(s) within an SSB burst
  Adapt different number of transmitted SSBs for the SSB patterns with lower and higher periodicities
  Procedures and signaling methods for extending SSB time domain adaptations to beam(s) within an SSB burst
Enhancements for SSB adaptation in time domain: Proposal 1

## Slide 9
© CEWiT 2022
9
Adaptation of Transmission Reception Points
Multi-transmission/reception point (m-TRP) was introduced in Rel. 16
  M-TRP can improve the reliability and throughput, especially in cell edge scenario
  Rel. 18 studied dynamic switching between single TRP and m-TRP operation for NES (Technique C-2)
  Significant energy saving is observed in TR 38.864 as given below
    Semi-static TRP adaptation: 36.9 % ~ 41.6 %
    Dynamic TRP adaptation: 19.7 % ~ 28.7 %
  No impact on legacy UE is foreseen, if implemented for UE specific signals/channels
Support adaptation of the number of TRPs transmitting and/or receiving signals and channels
  Dynamic switching between single-TRP and m-TRP operation based on network condition
  Procedures and signaling methods for adapting number of TRPs transmitting and/or receiving signals and channels

## Slide 10
© CEWiT 2022
10
Adaptation of Transmission Reception Points: Proposal 2
Support adaptation of the number of TRPs transmitting and/or receiving signals and channels
  Dynamic switching between single-TRP and m-TRP operation based on network condition
  Procedures and signaling methods for adapting number of TRPs transmitting and/or receiving signals and channels

## Slide 11
© CEWiT 2022
11
  Rel-18 DTX/DRX adaptation support configured DTX/DRX pattern, activated by RRC or DCI
  DTX/DRX pattern comprises start time, ON duration and periodicity
  This mechanism is limited to specific signals, such as PDSCH and a subset of PDCCH.
  DTX/DRX is not applicable to signals such as SSB
    Reduces sleep time of gNB and reduces NES gains
    Sparser SSB transmission occasions occurs in time when SSBs with longer period are enabled impacting meaurements and performance at UE
  Failure of DCI activating DTX/DRX adaptation results in uncertainty about DTX/DRX pattern
  Extending Cell DTX/DRX operation to cell specific signals is supported
  gNB perform SSB tranmissions with certain periodicity, only during active period of the cell DTX/DRX and no transmissions during inactive period
  Improve flexibility, performance and NES gains
  Impact on legacy UEs can be minimized by enabling the technique for scenario not involving legacy UEs (E.g., SSB configuration not applicable for legacy UE, adaptSCell, etc.)
Enhancements for DTX/DRX Adaptation

## Slide 12
© CEWiT 2022
12
Enhancements for DTX/DRX Adaptation: Proposal 3
The Rel. 20 WI phase should consider following enhancements for cell DTX/DRX mechanism
  Extending Cell DTX/DRX operation to include mandatory cell specific signals
    Transmission of SSBs with certain periodicities within active period of cell DTX and no transmission in non active period
  Procedures and signaling methods for adapting SSBs based on cell DTX
    Increasing reliability of activation/deactivation of DTX/DRX
    Impacts on specification

## Slide 13
© CEWiT 2022
13
  Rel-18 WI on spatial/power adaptation focused on
  adapting antenna elements and/or power for PDSCH transmissions
  Measurement and reporting framework for determining the adaptation pattern
  Spatial/power adaptation impacts BFR procedure
    Best beam is selected using measurements on CSI-RS and configured threshold
    PDSCH is to be transmitted using different spatial/power configuration compared to CSI-RS
    Measurements on CSI-RS w/o adaptation satisfy the threshold whereas the PDSCH may not
    Performance of the selected beam may not be the best for PDSCH
Enhancements for Spatial/power domain adaptation

## Slide 14
© CEWiT 2022
14
Rel-18 spatial and power adaptation increases UL resource consumption and UE power consumption
  Transmission of multiple CSI reports corresponding to various adaptation patterns
  UE reports configured CSI report quantity for all adaptation patterns
  Increase the measurement complexity, CSI payload and reporting
Enhancements to simplify CSI report framework
  Configured CSI report quantity can be redundant across the adaptation patterns
  Enhancements to avoid redundancy in reporting
  Rel-18 WI also dropped following aspects of spatial and power adaptation due to time constraints
  Enhancements for CSI report payload reduction
  Enhancements for BFR procedure
Enhancements for Spatial/power domain adaptation contd..

## Slide 15
© CEWiT 2022
15
  Rel. 20 should consider the following enhancements for spatial and power domain adaptations
  Enhancements for BFR procedure to support spatial and power domain adaptations
    Dynamic adaptation of threshold for beam selection based on adaptation pattern
  Methods to simplify the CSI reporting framework for NES adaptation
    CSI compression using correlation among various CSI report quantities for various adaptation patterns
Enhancements of BFR procedure for Spatial/power domain adaptation: Proposal 4

## Slide 16
© CEWiT 2022
16
Summary
Extend Rel. 19 SSB time domain adaptations to beam(s) within an SSB burst
  Adapt different number of transmitted SSBs for the SSB patterns with lower and higher periodicities
  Procedures and signaling methods for extending SSB adaptations to beam(s) within an SSB burst
Support adaptation of the number of TRPs transmitting and/or receiving signals and channels
  Dynamic switching between single-TRP and m-TRP operation
  Procedures and signaling methods for adapting number of TRPs
The Rel. 20 WI phase should consider following enhancements for cell DTX/DRX mechanism
  Extending Cell DTX/DRX operation to include mandatory cell specific signals
  Procedures and signaling methods for adapting SSBs based on cell DTX
  Rel. 20 should consider the following enhancements for spatial and power domain adaptations
  Enhancements for BFR procedure
  Methods to simplify the CSI reporting framework
Following NES techniques are supported for WI phase in 5G-A in Rel. 20

## Slide 17
© CEWiT 2022
17
Thank You