## Slide 1
Huawei, HiSilicon
Motivation and Scope for Rel-19 WID on Ambient IoT
3GPP TSG RAN#106 RP-243191
Madrid, Spain, December 9 - 12, 2024
Agenda item: 9.1.1

## Slide 2
Background
In RAN#102 (Dec 2023), the Rel-19 Ambient IoT SID was approved
  Target 12-month for SI completion
  Check in Dec’24 for conversion to WI or if necessary, continuation of SI
Rel-19 SI has identified details and feasible designs in all RAN WGs, and is complete
Considering the urgent market demand, it is necessary to standardize the first version of Ambient IoT in Rel-19
  Rapid growth is foreseen for the IoT markets requiring maintenance-free wireless devices with ultra-low cost
    Global market volume of RFID is predicted to increase from 20B in 2022 to 49B in 2031, with an accelerated growth from 2025 [1]
    RFID has been widely used in retail and clothing industries, and attracts attention from more industries such as logistics, manufacturing
  Missing the opportunity in the fast-growing market would lead to strenuous efforts to enter in the future
    Many industries become interested in pilot with RFID, while also looking for new solutions for long-life maintenance-free device based on other non-3GPP technologies e.g. WiFi, Bluetooth Low Energy (BLE or Bluetooth 4.0), Wiliot
    The IEEE 802.11 working group has started a new TIG/SG of AMbient Power (AMP) to support Ambient Power communication
    Once the huge amount of connections been captured, it is uncertain 3GPP technologies can regain the market share
  A first version of Ambient IoT in Rel-19 would attract the interests of industries on 3GPP technology
 | Customer | Use case | Requirement | Desired technology readiness | Values
Company A | White goods producer | Real-time visible production and logistics | Autonomous inventory, High success rate (e.g. 99.9%), Extreme low cost batteryless tag | ~2024 | Reduce logistics cost Reduce production line stoppages
Company B/C | Warehousing & logistics | Warehousing inventory and material container management |  | Urgent, as early as possible | 
Company D | E-commerce | Account management |  | ~2024 | Improve management efficiency
[1] Global RFID Sensor Market - Global Industry Analysis, Size, Share, Growth, Trends and Forecast 2021-2031, Transparency Market Research, June 2021

## Slide 3
Rel-19 Ambient IoT Focuses on Indoor Scenarios
A harmonized air interface design with minimized differences (where necessary) is recommended for Ambient IoT to enable devices with different power consumption
The scope of Rel-19 Ambient IoT WI should consider both market urgency and appropriate workload
In the Rel-19 Ambient IoT SI, the following objectives have been studied
 | Rel-19 SI scope
Use cases | Indoor inventory, Indoor command
Devices | 1 (~1 μW), 2a (≤ a few hundred µW, external carrier-wave), 2b (≤ a few hundred µW, internally-generated carrier-wave)
Deployment scenarios | D1 (Device indoors, basestation indoors), D2 (Device indoors, basestation outdoors)
Connectivity topology | T1 (BS ↔ Ambient IoT device), T2 (BS ↔ intermediate node ↔ Ambient IoT device)
CW deployment | Inside topology (CW node and D2R receiver are same or different), Outside topology
Spectrum | FDD
Traffic types | DO-DTT, DT

## Slide 4
A-IoT Rel-19 SI/WI timeline
Dec ‘24
RAN1
RAN1,2,3,4
Rel-19 SI phase
RAN1,2,3,4
RAN2,3,4
Sep ‘25
Jun ‘25
Rel-19 WI phase
Completed 12 month SI, with RAN1 starting first. See TR 38.769.
9 month WI until September 2025, with RAN1 scheduled to finish in June 2025
Mar ‘24
Jan ‘24

## Slide 5
Rel-19 WI Scope (1): Devices
Devices 1 and 2a (w/o large freq. shift) are in Rel-19
  Both have coverage and simple RF envelope detector filtering suitable for indoor use cases
  Same spec support for both devices
  Device 2a has added coverage
Device 2b with IF/ZIF receiver offers coverage beyond indoor use cases, and sophisticated filtering to combat interference → Rel-20
  An obvious starting point for outdoor use cases
  2b might benefit from more changes than a Rel-19 harmonized design, to reach outdoor coverage targets, and handle complex interference
Device 1: ~1 μW, backscatter, RF envelope detector
Device 2a: ≤ few hundred 00 μW, backscatter
RF envelope detector
Device 2b:
≤ few hundred μW
Internal RF carrier generation
Additional CFO cal. signal
RF-ED
IF-ED
Zero IF

## Slide 6
Rel-19 WI Scope (2): Topologies and Deployment Scenarios
D1:
Indoor to indoor
D2:
Indoor to outdoor
Topology 1:
Topology 2:
+
+
Topology 1 is the fundamental cellular network topology that must be in a first Release of A-IoT
T1 supports the focus use cases of Rel-19: Indoor inventory & command
Topology 2 is relevant to interesting use cases, but demands intricate designs in RAN1, RAN2, RAN3, SA2, SA3, together with RAN4 UE work that has no re-use from T1.
It is hard to see a realistic claim that TU are available for T2, no matter the duration of the WI
Commercialization of T2 would come much later than T1, even if standardized together

## Slide 7
Scenario | CW Inside/outside topology | Diagram of the scenario | CW spectrum | D2R spectrum | R2D spectrum
D1T1-A1 | CW inside topology |  | Inside topology, DL Inside topology, UL | Same as CW | At least DL
D1T1-A2 |  |  | Same as D1T1-A1 | Same as CW | At least DL
D1T1-B | CW outside topology |  | Outside topology, UL | UL | At least DL
Rel-19 WI Scope (3): Spectrum and carrier-wave deployment
Carrier-wave waveform 1: Single-tone unmodulated sinusoid, i.e. a ‘single tone’
Carrier-wave waveform 2: Two single tones
External CW node for Rel-19 minimizes work for speedy deployment of the first Release:
  No self-cancellation at the Reader, and spatial isolation (path-loss) from CW. Helps D2R link performance.
  Independent deployments of Readers and CW nodes can be optimized for coverage of each link
Single-tone CW waveform provides sufficient coverage with simplest spec work
  Simplest, hence most effective, RF and baseband interference cancellation at reader
  0 dB PAPR from CW transmission node → convenient to reach high PA efficiency

## Slide 8
General principle of WID scoping
Preceding slides are the critical high-level scope for a Rel-19 WI on a commercial basis:
  Indoor use cases for inventory and command
  Devices 1, 2a without ‘large frequency-shift’
  Topology 1
  R2D in FDD-DL, carrier-wave node outside topology in FDD-UL, hence D2R in FDD-UL by backscattering
WI will take in the decisions of the WGs, and content of the TRs
For design solutions, RAN WGs have reported several feasible options, especially RAN1
RAN can limit the technical scope to the choices really useful for further WI-level analysis
  There is no need to continue all possible options into WI debate, since in many cases the outcome is already quite clear, no matter how much longer a decision is postponed

## Slide 9
RAN1 scope
Aspect | R2D options in RAN1 | D2R options in RAN1
Waveform | CP handling: | N/A; backscattered for devices 1 & 2a
Modulation(s) |  | 
Multiplexing |  | 
Line code |  | 
Channel code |  | 
PHY channels |  | 
Device unavailability |  | 
Proximity determination (if included) |  | 
  (b) Non-orthogonal to NR/LTE
  (a) Orthogonal to NR/LTE
  OOK-1, OOK-4
  OOK, BPSK
  MSK
  TDMA
  FDMA (only for 2b IF/ZIF rx)
  TDMA, FDMA
  CDMA
  Manchester
  Pulse-interval encoding PIE
  Manchester
  Miller
  None
  convolutional code
  Direction 2: Reader can provide information to device indicating (un)availability times
  Direction 1: Reader does not provide information to device indicating (un)availability time
  (e.g.: Reader schedules paging messages with sufficient frequency for device to rx. while charged)
  (e.g.: Reader transmits message containing an indication of how long until next paging message)
  Solution 2: Reader successfully receives response from device & uses measurement at reader to decide proximity
  Solution 1: Reader successfully receives response from device
  PRDCH & PDRCH are the only physical channels
  LTE
  with pre/mid/postambles as needed
  From RAN1 recommendation
  Huawei view on minimum necessary scope

## Slide 10
Support | Scope control options
Paging | 
Temporary paging identifier | 
Random access | 
Data transmission | 
Segmentation | 
RAN2 layers | 
  3-step CBRA
  Unified solution for CBRA
  (b) Multiplex multiple paging identifiers in paging message
  (a) Include one paging Identifier in paging message
  Not supported
  D2R
  Essential parts of TR 38.769; 1-bit energy status report
  Only MAC
  R2D
RAN2 agreements on excluded functions, e.g. no ARQ, no mobility, non-supported protocol layers, etc. are taken into the WI
RAN2 scope
  (c) Page all (no identifier included)

## Slide 11
RAN3 scope
Specify necessary signaling and procedures between RAN and CN to support the following A-IoT functions, assuming an architecture of aggregated gNB:
  Inventory operation
  Command operation
  (If included) Device location reporting at reader ID granularity
Note: The above A-IoT functions are supported over the existing NG interface, or new protocol carried over NGAP, based on architecture(s) defined by SA2.

## Slide 12
RAN4 scope
Core part
Specify RF requirements for Ambient-IoT BS, device 1/2a, and CW
  RF requirements for Type 1-C Ambient-IoT BS
  RF requirements for device 1 and device 2a with RF envelope detector
  RF requirements for CW
Specify RRM core requirements for device 1/2a, including:
  Requirements for random access
Use band n8 as an example band
Performance part
Specify the necessary conformance test for Ambient-IoT BS
Specify test methodology for device 1/2a
Specify the necessary RRM performance requirements for device
Specify the necessary demodulation performance requirements for device and Ambient-IoT BS

## Slide 13: Thank you!