## Slide 1
Release 19 XR enhancements
- Way forward on WID scope revision
Agenda item: xxxx
Nokia (moderator)
3GPP TSG RAN#106 Tdoc RP-24xxxx
Madrid, Spain, December 9-12, 2024

## Slide 2
1. RAN3
- Adding TUs to cover RAN3 work from SA2 topics
Agree to add TUs for RAN3, TUs to start from March onwards for 3 RAN3 meetings
Add for the WID the following (either now or in March):
Support of PDU set based QoS handling enhancement [RAN3]
- the 5GC sends NG-RAN an indicator indicating the DL PDU Set Information Marking is supported. Based on the indicator, the NG-RAN may indicate the 5GC to perform the PDU Set Information marking.
- FEC Content ratio agreed to be provided over NGAP.
- Enhance Alternative UL/DL PDU Set QoS and Notification control for PDU Set QoS.
- QoS Handling when Traffic Characteristics Change Dynamically [RAN3]
- TTNB and burst size to be provided over GTP-U
- Enhancement for XR related network information exposure [RAN3]
- Support the report available data rate value for GBR QoS Flow

## Slide 3
2. Downlink congestion indication (in addition of the uplink)
- No WID update at this point in time
Proposed update was as follows:
Specify congestion signalling for DL and UL [RAN2]:
○ Specify in MAC layer XR rate control signalling per QoS flow/per DRB to enable faster
source rate adaption to congestion.
RAN2 to continue working on the uplink solution and to liaise with SA2/SA4 if there are issues if the same approach would be extended for the DL as well, assuming the solution extension for DL would not cause issues in RAN2 side (not more work than wat would be needed to prevent use of the solution for downlink direction)

## Slide 4
3. Multimodality
- Proposed way forward
TSG RAN view is to proceed based on MMSID (as specified in Release 18) as per TSG RAN#105 agreement, as the expectation is that it is feasible to obtain that information from the 5GC. RAN3 work is needed for the NG-interface, otherwise no further specification work needed.