3GPP TSG-RAN WG2 Meeting#126	R2-24xxxxx

# Fukuoka, Japan, May 20th – 24th, 2024

Agenda Item: 	7.11.2.1

Source:	Apple

Title:	Report of [AT126][004][R17 UP] HARQ RTT offline (Apple)

Document for:		Discussion and Decision

# Introduction

This document captures the outcome of the following email discussion:

[AT126][004][R17 UP] HARQ RTT offline (Apple)

Intended outcome: discussion on HARQ RTT

Deadline:  05-24-24

HARQ RTT Timer R2-2404669 Clarification on HARQ RTT Timer operation Apple, Nokia, Nokia Shanghai Bell, MediaTek Inc., ZTE CR Rel-18 38.321 18.1.0 1843 - F TEI18 R2-2405115 Correction on the start of HARQ RTT timer Huawei, HiSilicon CR Rel-17 38.321 17.8.0 1852 - F TEI17 R2-2405116 Correction on the start of HARQ RTT timer Huawei, HiSilicon CR Rel-18 38.321 18.1.0 1853 - A TEI17 R2-2405475 Clarification on HARQ RTT Timer operation LG Electronics, Samsung CR Rel-17 38.321 17.8.0 1868 - F TEI17 R2-2405476 Clarification on HARQ RTT Timer operation LG Electronics, Samsung CR Rel-18 38.321 18.1.0 1869 - A TEI17 R2-2404249 Impact on HARQ RTT timer handling due to UL and SL prioritization CATT discussion

Please provide your comments before the CB session on Friday.

# Discussion

## Background

According to MAC spec, the HARQ RTT Timer is started based on UL transmission, but companies have different interpretations and implementation on transmission. There are two interpretations:

- Interpretation 1: based on virtual transmission (according to the configured/indicated transmission)

- Interpretation 2: based on actual transmission in Uu interface.

Observation 1: About whether the HARQ RTT Timer is started based on actual transmission or virtual transmission, there are different understandings and implementations in the field.

In RAN2#125, RAN2 made the following agreement on the UL HARQ RTT Timer based on virtual transmission when drx-LastTransmissionUL is configured.

RAN2#125 agreement: When drx-LastTransmissionUL is configured, drx-HARQ-RTT-TimerUL is started after the last PUSCH transmission occasion of a bundle regardless of whether that last PUSCH transmission occasion is used for a PUSCH transmission for that bundle or not.

Observation 2: RAN2 agreed that the HARQ RTT Timer is started based on virtual transmission when drx-HARQ-RTT-TimerUL is configured.

In this meeting, there are several contributions/CRs are focusing on how to capture RAN2#125 agreement in the spec:

| TDoc | Proposals |
| --- | --- |
| R2-2404669 Apple, Nokia, Nokia Shanghai Bell, MediaTek Inc., ZTE | Rel | For R17, up to UE implementation. Reflect RAN2#125 agreement from R18. |
|  | TP | Capture RAN2 agreement in MAC spec. When drx-LastTransmissionUL is configured, drx-HARQ-RTT-TimerUL or HARQ-RTT-TimerUL-NTN is started after the last PUSCH transmission occasion of a bundle regardless of whether that last PUSCH transmission occasion is used for a PUSCH transmission for that bundle or not. |
| R2-2405115/ R2-2405116 Huawei | Rel | Reflect RAN2#125 agreement from R18. |
|  | TP | Capture RAN2 agreement in MAC spec. When drx-LastTransmissionUL is configured, the drx-HARQ-RTT-TimerUL or HARQ-RTT-TimerUL-NTN is started after the last PUSCH transmission occasion of a bundle regardless of whether that last PUSCH transmission occasion is used for a PUSCH transmission for that bundle or not. |
| R2-2405475/ R2-2405476 LG, Samsung | Rel | Reflect RAN2#125 agreement from R17. |
|  | TP | Modify the definition of drx-LastTransmissionUL drx-LastTransmissionUL (optional): the configuration to start drx-HARQ-RTT-TimerUL after the last transmission occasion within a bundle; |
| R2-2404249 CATT | Rel | Clarify the case that PUSCH transmission may be dropped due to UL and SL prioritization. |
|  | TP | Interpret the transmission for SL prioritization case as the virtual transmission way, i.e. regardless of whether PUSCH transmission occasion is used for PUSCH transmission or not. NOTE X: drx-HARQ-RTT-TimerUL and drx-HARQ-RTT-TimerDL are started as specified in this subclause, irrespective of the prioritization between uplink transmission and sidelink transmission or reception as specified in subclauses 5.4.2.2, 5.22.1.3.1a and in subclause 16.2.4.3.1 in TS 38.213 [6]. |

## Discussion

Discussion is focusing on whether and how to capture/reflect the RAN2 agreement in RAN2 spec, and if captured, from which release.

There are some options:

- Option 1: Reflect RAN2 agreement from R18. For R17, up to UE implementation;

- Option 2: Reflect RAN2 agreement from R17.

- Option 3: Not reflect RAN2 agreement in spec, i.e. up to UE implementation.

  - Clarify that it’s up to UE implementation in chairman notes, and no come back in the future until serious problem occurs in the field.

- Option 4: Reflect RAN2 agreement from R18, but with a new UE capability.

  - If UE indicates the capability, UE supports the operation based on virtual transmission.

  - If UE doesnot indicates the capability, UE doesnot support it.

##### Question 1: Which Option(s) are acceptable to you?

| Company | Option(s) | Comment |
| --- | --- | --- |

About how to reflect the agreement in spec, th

##### Question 2: Which Option(s) are acceptable to you?

- Option 1: capture RAN2 agreements in the spec. (R2-2404669, R2-2405115/ R2-2405116)

When drx-LastTransmissionUL is configured, drx-HARQ-RTT-TimerUL or HARQ-RTT-TimerUL-NTN is started after the last PUSCH transmission occasion of a bundle regardless of whether that last PUSCH transmission occasion is used for a PUSCH transmission for that bundle or not.

- Option 2: only modify the defination of drx-LastTransmissionUL. (R2-2405475/ R2-2405476)

drx-LastTransmissionUL (optional): the configuration to start drx-HARQ-RTT-TimerUL after the last transmission occasion within a bundle;

| Company | Option(s) | Comment |
| --- | --- | --- |

# Conclusion

Based on the above discussion, we propose that: