3GPP TSG RAN WG2 Meeting #126	                                        R2-2405873

# Fukuoka, Japan, 20th – 24th May 2024

Agenda item:		7.2.3

Source:			Lenovo

Title:		Report from offline discussion [AT126][405][POS] SLPP error causes (Lenovo)

Document for:	 	Discussion and decision

# Introduction

This report summarizes the offline discussion below that took place during RAN2#126 meeting:

[AT126][405][POS] SLPP error causes (Lenovo)

Scope: F2F offline to converge on a list of SLPP error causes.  If possible, determine whether to capture them in a common or method-specific way.

Intended outcome: Report to CB session in R2-2405873

Schedule: Wednesday 2024-05-22 0930-1030 in Brk3

Deadline:  Thursday 2024-05-23 1000 JST

# Reference

[1]	R2-2404518, Text proposal on error messaging in SLPP, Lenovo

[2]	R2-2405248, Remaining issues for SLPP, Qualcomm Incorporated

[3]	R2-2405268, Open SLPP issues, Nokia

# Discussion

## Motivation

Referring to the highlighted procedure description in SLPP, clause 5.4.3, the transmission of error information in the SLPP ProvideAssistanceData and ProvideLocationInformation shall be supported. Upon receiving the error information from the endpoint B, the endpoint A that sent the SLPP RequestAssistanceData or RequestLocationInformation aborts the ongoing procedure with that endpoint and may restart the aborted procedure  with the endpoint B taking into consideration the error that occurred at that endpoint during SL positioning operation.

Furthermore, with regards to assistance data, the endpoint A may be the Target or Server, and the endpoint B may be the Anchor or Server. With regards to location information, the endpoint A may be the Target or Server, and the endpoint B may be the Target or Anchor.

5.4.3 SLPP Error Detection Upon receiving any SLPP message, the receiving endpoint shall attempt to decode the message and verify the presence of any errors and: 1> if decoding errors are encountered: 2> if the receiver cannot determine that the received message is an SLPP Error or Abort message: 3> return an SLPP Error message to the sender and include the field sessionID (if PC5-U is used as transport layer) and the received transactionID, if they were decoded, and type of error; 3> discard the received message and stop the error detection procedure; 1> if the message is a duplicate of a previously received message: 2> discard the message and stop the error detection procedure; 1> if the field transactionID matches the field transactionID for a procedure that is still ongoing for the same session and the message type is invalid for the current state of the procedure: 2> abort the ongoing procedure; 2> return an SLPP Error message to the sender and include the field sessionID (if PC5-U is used as transport layer), the received field transactionID and type of error; 2> discard the message and stop the error detection procedure; 1> if the message type is an SLPP RequestCapabilities and some of the requested information is not supported: 2> return any information that can be provided in a normal response. 1> if the message type is an SLPP RequestAssistanceData or RequestLocationInformation and some or all of the requested information is not supported: 2> return any information that can be provided in a normal response, which includes indications on other information that is not supported.

## List of candidate SLPP error cause values

With regards to SLPP error cause values there are following proposals:

- In Lenovo [1]:

Proposal 1: Agree on the initial set of SL-specific error cause values as listed in Table 1. Table 1: Initial set of SL-specific error cause values Type Error cause value Applicable for Target Applicable for Anchor Applicable for Server General undefined X X X Measurement notAllRequestedMeasurementsPossible X X Assistance data assistanceDataMissing X X assistanceDataNotSupportedByServer X assistanceDataSupportedButCurrentlyNotAvailableBy Server X notAllRequestedAssistanceDataAvailableByServer X

- In Qualcomm [2]:

Proposal 5a: For the 'method'-AssistanceDataError IEs, define the following cause values: undefined, requestedInformationNotSupported, requestedInformationSupportedButCurrentlyNotAvailable. Proposal 5b: For the 'method'-ProvideLocationInformation IEs, define the following cause values: undefined, assistance-data-missing, unableToMeasureAnyUE, thereWereNotEnoughSignalsReceivedForUeBased.

- In Nokia [3]:

Proposal 6: RAN2 to support the reporting of general errors internalMeasurementFailure to indicate (internal) SL PRS measurement failure, and internalEstimationFailure to indicate (internal) location estimation failure, and externalSourceFailure to indicate (external) source unavailability / SL PRS absence together with the indication of the error source (eg, UE ID and / or SL PRS ID).

All proponents suggest to agree on an (initial) short set of error cause values in view of the oncoming Rel-18 ASN.1 freeze in June 2024. Based on the proposals made, rapporteur identified the following discussion points.

Discussion point 1: With regards to type of error information which option do companies prefer?

- Option 1: Type of error information similar to LPP as suggested by Lenovo [1] and Qualcomm [2].

- Option 2: New type of error information as suggested by Nokia [3].

Discussion: QC indicates that we already support error cause values in SLPP in common error IE for indicating protocol errors etc. Nokia would like to expose information about the source and type of information observed in the TX or RX. Lenovo comments that any issues on RX side can be inferred from the measurements. MTK understands the motivation for indicating the type of information at TX side. But they are not sure about the need of granularity on RX side. Ericsson wonders what will be action on errors at RX side. QC clarifies that the SL-PRS transmission/reception failures is up to lower layers. They wonder what can the server do if it knows about the lower layers problems. Intel does not see the need to indicate TX problems since there are no procedures specified to handle this type of errors. Criteria such as radio quality was discussed at the beginning of the WI phase but was not considered. Nokia proposes to agree on error cause values indicating TX problems. Intel indicates that for such error cause values we need to specify new procedures. Intel, Lenovo suggest to agree on option 1. Additional error cause values can be added later, if deemed necessary. Conclusion: Option 1 is agreed.

Discussion point 2A: If option 1 is preferred, which of the suggested error cause values do companies consider as useful to be adopted for SLPP?

| # | Error cause value |
| --- | --- |
| 1 | undefined |
| 2 | notAllRequestedMeasurementsPossible |
| 3 | assistanceDataMissing |
| 4 | assistanceDataNotSupported or requestedInformationNotSupported |
| 5 | assistanceDataSupportedButCurrentlyNotAvailable or requestedInformationSupportedButCurrentlyNotAvailable |
| 6 | notAllRequestedAssistanceDataAvailable |
| 7 | unableToMeasureAnyUE |
| 8 | thereWereNotEnoughSignalsReceivedForUeBased |
| 9 | Other? |

Discussion: Intel: 5, 6 and 8 may not be needed. We don’t need to copy everything from LPP. MTK: merge 4 and 5. We can name it “assistanceDataNotAvailable”. QC: 4 is not needed. Conclusion: The error cause values 1, 2, 3 and “assistanceDataNotAvailable” (new) are agreed.

Discussion point 2B: If option 2 is preferred, which of the suggested error cause values do companies consider as useful to be adopted for SLPP?

| # | Error cause value |
| --- | --- |
| 1 | internalMeasurementFailure together with its error source |
| 2 | internalEstimationFailure together with its error source |
| 3 | externalSourceFailure together with its error source |
| 4 | Other? |

Discussion: None. Conclusion: None.

## Options for introducing error cause values in SLPP

With regards to the options for introducing error cause values in SLPP there are following proposals:

- In Lenovo [1]:

Option 1: A common IE SL-ErrorCauses is defined that contains the SL-specific error cause values from Table 1. This common IE is then imported by each SL positioning method specific ASN.1 module and can be used in the concerned ProvideAssistanceData and ProvideLocationInformation IEs. This option is simple and requires only minor ASN.1 changes but has the drawback that the list of error cause values in the common IE SL-ErrorCauses may grow over time. If an error occurs it is then up to implementation to ensure that the correct error cause value among the set of defined error cause values is selected. A TP acc. to this Option 1 is provided in Annex A. Option 2: SL positioning method specific Error IE is defined and used only in the concerned ASN.1 module. Furthermore, the error cause values are grouped for server, target device and anchor device. This option requires more ASN.1 changes compared to Option 1. However, the advantage of this option is that the set of applicable error cause values for each SL positioning method and device type is clearly defined, so that the risk of selecting a wrong error cause value can be minimized. A TP acc. to this Option 2 is provided in Annex B. Proposal 2: Discuss and decide on the option for introducing SL-specific error cause values in SLPP.

- In Qualcomm [2]:

Proposal 4a: In each 'method'-ProvideAssistanceData message (where 'method' can be Common/Common-PRS, SL-AoA, SL-RTT, SL-TDOA, and SL-TOA) a 'method'-AssistanceDataError IE is included. Proposal 4b: In each 'method'-ProvideLocationInformation message (where 'method' can be Common/Common-PRS, SL-AoA, SL-RTT, SL-TDOA, and SL-TOA) a 'method'-LocationInformationError IE is included.

- In Nokia [3]:

Errors can be reported by two mechanisms – by using generic CommonIEsError, or more specific CommonIEsProvideLocationInformation. Either of the two options is suitable for error information delivery, the difference is in latency and scope. Proposal 7: RAN2 to support internal / external error reporting by using at least one of the following two options: Option 1: CommonIEsError / ErrorCause, Option 2: CommonIEsProvideLocationInformation / LocationFailureCause.

Based on the proposals made and the discussion in section 3.2, rapporteur identified the following discussion points.

Discussion point 3: Which option do companies prefer for introducing error cause values in SLPP?

- Option A: A common ErrorCause IE is defined that contains all defined error cause values. This common IE is then imported by each SL positioning method-specific ASN.1 module and used in the method-specific ProvideAssistanceData and ProvideLocationInformation IEs.

- Option B: A method-specific ErrorCause IE is defined and used in the method-specific ASN.1 module. This method-specific IE contains only the error cause values that is applicable for the method.

Discussion: MTK: do we need error cause IE in common PRS IE? Intel: we add error cause values in the common PRS IE, method-specific provide location information IE and provide assistance data IE. Conclusion: The new error cause values will be added in the common PRS IE, method-specific provide location information IE and provide assistance data IE. TP to SLPP will be provided by Lenovo.

Discussion point 4: If option B is preferred, do companies prefer to group the method-specific error cause values acc. to the type of device (Target, Anchor, Server) or type of message (ProvideAssistanceData, ProvideLocationInformation)?

Discussion: None. Conclusion: None.

# Conclusion

In accordance with the outcome of the offline discussion the following proposals are made:

Proposal 1: Define type of error information similar to LPP (“Option 1”). That means, an error cause value in SLPP will indicate that an error occurred at an endpoint without exposing any further information.

Proposal 2: Introduce the following error cause values: “undefined”, “notAllRequestedMeasurementsPossible”, “assistanceDataMissing” and “assistanceDataNotAvailable”.

Proposal 3: Add the new error cause values in the common SL-PRS methods ProvideLocationInformation IE and ProvideAssistanceData IE, method-specific ProvideLocationInformation IE and ProvideAssistanceData IE. TP to SLPP can be found in Annex B.

# Annex A

Reference: R2-2402792, Discussion on error messaging in SLPP, Lenovo, RAN2#125bis

Table 1: Candidate list of SL positioning method specific error cause values acc. to the type of error information and receiving device

| Type | Error cause value | Target error causes | Anchor error causes | Server error causes |
| --- | --- | --- | --- | --- |
| Measurements | unableToMeasureReferenceAnchor | X |  |  |
|  | unableToMeasureAnyAnchor | X |  |  |
|  | unableToMeasureTarget |  | X |  |
|  | notAllRequestedMeasurementsPossible | X | X |  |
|  | notEnoughAnchorReceived | X |  |  |
|  | rsrpMeasurementNotPossible | X | X |  |
|  | rsrppMeasurementNotPossible | X | X |  |
|  | angleMeasurementNotPossible | X | X |  |
|  | ueRxTxMeasurementNotPossible | X | X |  |
|  | rstdMeasurementNotPossible | X |  |  |
|  | rtoaMeasurementNotPossible |  | X |  |
| Location information | unableToEstimateRelativeLocation | X |  | X |
|  | unableToEstimateAbsoluteLocation | X |  | X |
|  | unableToEstimateDistance | X |  | X |
|  | unabletoEstimateDirection | X |  | X |
|  | unableToEstimateAbsoluteVelocity | X |  | X |
|  | unableToEstimateRelativeVelocity | X |  | X |
| Assistance data | adMissing | X | X |  |
|  | adNotSupportedByServer |  |  | X |
|  | adSupportedButCurrentlyNotAvailableByServer |  |  | X |
|  | notAllrequestedADAvailable |  |  | X |

# Annex B: TP for SLPP

## 6.6	SLPP PDU Common SL-PRS Methods Contents

#### –	CommonSL-PRS-MethodsIEsProvideAssistanceData

-- ASN1START

-- TAG-COMMONSL-PRS-METHODSIESPROVIDEASSISTANCEDDATA-START

CommonSL-PRS-MethodsIEsProvideAssistanceData ::= SEQUENCE {

sl-PRS-AssistanceDataInfo                        SEQUENCE (SIZE (1..maxNrOfUEs)) OF SL-PRS-AssistanceData                OPTIONAL,

sl-PRS-Error                       	 			 SL-PRS-AssistanceDataError                                    	     OPTIONAL,

...

}

SL-PRS-AssistanceData ::= SEQUENCE {

applicationLayerID            OCTET STRING,

sl-PRS-SequenceID             INTEGER(0..4095)              OPTIONAL,  -- SL PRS sequence ID for transmitting SL-PRS

anchorUE-LocationInformation  AnchorLocationCoordinates     OPTIONAL,

arp-LocationInfo              ARP-LocationInfo              OPTIONAL,

sl-PRS-TxInfo                 SL-PRS-TxInfo                 OPTIONAL,

...

}

AnchorLocationCoordinates ::= CHOICE {

ellipsoidPoint                                      EllipsoidPoint,

ellipsoidPointWithUncertaintyEllipse                EllipsoidPointWithUncertaintyEllipse,

ellipsoidPointWithAltitude                          EllipsoidPointWithAltitude,

ellipsoidPointWithAltitudeAndUncertaintyEllipsoid   EllipsoidPointWithAltitudeAndUncertaintyEllipsoid

}

ARP-LocationInfo ::= SEQUENCE {

referencePoint         ReferencePoint            OPTIONAL,

arp-LocationInfoList   SEQUENCE (SIZE (1..4)) OF ARP-LocationInfoElement

}

ReferencePoint ::= CHOICE {

location2D                          EllipsoidPointWithUncertaintyEllipse,

location3D                          EllipsoidPointWithAltitudeAndUncertaintyEllipsoid

}

ARP-LocationInfoElement ::= SEQUENCE {

sl-PRS-ARP-ID               INTEGER (1..4),

arp-LocationInfo            RelativeLocation

}

RelativeLocation ::= SEQUENCE {

milliArcSecondUnits  ENUMERATED { mas0-03, mas0-3, mas3, mas30},

heightUnits          ENUMERATED { mm, cm, m},

deltaLatitude        DeltaLatitude,

deltaLongitude       DeltaLongitude,

deltaHeight          DeltaHeight,

locationUNC          LocationUncertainty                             OPTIONAL

}

DeltaLatitude ::= SEQUENCE {

deltaLatitude        INTEGER (-1024..1023),

coarseDeltaLatitude  INTEGER (0..4095)        OPTIONAL

}

DeltaLongitude ::= SEQUENCE {

deltaLongitude        INTEGER (-1024..1023),

coarseDeltaLongitude  INTEGER (0..4095)        OPTIONAL

}

DeltaHeight ::= SEQUENCE {

deltaHeight        INTEGER (-1024..1023),

coarseDeltaHeight  INTEGER (0..4095)        OPTIONAL

}

LocationUncertainty ::= SEQUENCE {

horizontalUncertainty    INTEGER (0..255),

horizontalConfidence     INTEGER (0..100),

verticalUncertainty      INTEGER (0..255),

verticalConfidence       INTEGER (0..100)

}

SL-PRS-TxInfo ::=                 SEQUENCE {

sl-PRS-Priority                   INTEGER (1..8)                                 OPTIONAL,

sl-PRS-DelayBudget                INTEGER (0..1023)                              OPTIONAL,

sl-PRS-BW                         INTEGER (10..275)                              OPTIONAL

}

SL-PRS-AssistanceDataError ::= ENUMERATED { undefined,

assistanceDataNotAvailable,

...

}

-- TAG-COMMONSL-PRS-METHODSIESPROVIDEASSISTANCEDDATA-STOP

-- ASN1STOP

CommonSL-PRS-MethodsIEsProvideAssistanceData field descriptions

anchorUE-LocationInformation This field provides the location coordinates of a SL Anchor UE identified by applicationLayerID.

arp-LocationInfo This field provides the location coordinates of the ARPs of the UE identified by applicationLayerID.

applicationLayerID This field provides the application layer ID as defined in TS 23.287 [9] for which the SL-PRS-AssistanceData is applicable.

referencePoint This field provides the reference point used to define the location of ARPs provided in the arp-LocationInfoList. If this field is absent, the reference point is the same as in the previous entry of the sl-PRS-AssistanceDataInfo list.

sl-PRS-ARP-ID This field provides the ARP ID of an ARP. The ARP ID is used to uniquely identify an ARP associated with the UE identified by applicationLayerID.

sl-PRS-BW This field provides the number of PRBs corresponding to the bandwidth of SL-PRS transmission which is used in UEAssistanceInformation message as defined in TS 38.331 [2].and the SL-PRS resource request MAC CE as defined in TS 38.321 [15].

sl-PRS-DelayBudget This field provides the SL-PRS delay budget which is used in UEAssistanceInformation message as defined in TS 38.331 [2] and the resource selection as defined in TS 38.321 [15].

sl-PRS-Error This field provides SL-PRS error reasons.

sl-PRS-Priority This field provides the priority of SL-PRS which is used in UEAssistanceInformation message as defined in TS 38.331 [2] and the resource selection as defined in TS 38.321 [15]. Value 1 is the highest priority whereas value 8 is the lowest priority.

sl-PRS-SequenceID This field specifies the sequence ID used to initialize cinit value used in pseudo random generator for generation of SL PRS sequence for transmission on a given SL PRS Resource, as specified in TS 38.211 [6] for a UE identified by applicationLayerID. If an UE does not receive a sequence ID via this SLPP message, the sequence ID is based on the 12 LSB bits CRC of PSCCH associated with the SL PRS.

#### –	Common-SL-PRS-MethodsIEsProvideLocationInformation

-- ASN1START

-- TAG-COMMONSL-PRS-METHODSIESPROVIDELOCATIONINFORMATION-START

CommonSL-PRS-MethodsIEsProvideLocationInformation ::= SEQUENCE {

sl-POS-ARP-ID-Tx                                      SL-POS-ARP-ID-Tx-InfoList            OPTIONAL,

sl-PRS-Error                                          SL-PRS-LocationInformationError      OPTIONAL,

...

}

SL-POS-ARP-ID-Tx-InfoList ::= SEQUENCE (SIZE (1..4)) OF SL-POS-ARP-ID-Tx-Info

SL-POS-ARP-ID-Tx-Info ::= SEQUENCE {

sl-POS-ARP-ID                          INTEGER (1..4),

sl-PRS-ResourceIdList-Tx               SEQUENCE (SIZE(1..16)) OF SL-PRS-ResourceId-Tx

}

SL-PRS-ResourceId-Tx ::= SEQUENCE {

sl-PRS-ResourceId        INTEGER (0..16)                      OPTIONAL,

tx-TimeStamp             SL-TimeStamp

}

SL-PRS-LocationInformationError ::= ENUMERATED { undefined,

...

}

-- TAG-COMMONSL-PRS-METHODSIESPROVIDELOCATIONINFORMATION-STOP

-- ASN1STOP

## 6.7	SLPP PDU SL-AoA Contents

#### –	SL-AoA-ProvideAssistanceData

-- ASN1START

-- TAG-SL-AOA-PROVIDEASSISTANCEDATA-START

SL-AoA-ProvideAssistanceData ::= SEQUENCE {

sl-AoA-AssistanceDataInfo        SEQUENCE (SIZE (1..maxNrOfUEs)) OF SL-AoA-AssistanceData     OPTIONAL,

sl-AoA-Error					 SL-AoA-AssistanceDataError		  								 OPTIONAL,

...

}

SL-AoA-AssistanceData ::= SEQUENCE {

applicationLayerID                           OCTET STRING,

expectedSL-AzimuthAoA-AndUncertainty         INTEGER(0..3599),                      -- expected-SL-AoA-and-Uncertainty

expectedSL-ZenithAoA-AndUncertainty          INTEGER(0..1800)        OPTIONAL,  -- expected-SL-AoA-and-Uncertainty

...

}

SL-AoA-AssistanceDataError ::= ENUMERATED { undefined,

assistanceDataNotAvailable,

...

}

-- TAG-SL-AoA-PROVIDEASSISTANCEDATA-STOP

-- ASN1STOP

SL-AoA-ProvideAssistanceData field descriptions

expectedSL-AzimuthAoA-AndUncertainty This field provides expected SL-AzimuthAoA and uncertainty range to a measuring UE.

expectedSL-ZenithAoA-AndUncertainty This field provides expected SL-ZenithAoA and uncertainty range to a measuring UE.

applicationLayerID This field provides an application layer ID as defined in TS 23.287 [9] which is used to identify a UE.

sl-AoA-Error This field provides SL-AoA error reasons.

#### –	SL-AoA-ProvideLocationInformation

-- ASN1START

-- TAG-SL-AOA-PROVIDELOCATIONINFORMATION-START

SL-AoA-ProvideLocationInformation ::= SEQUENCE {

sl-AoA-SignalMeasurementInformation   SL-AoA-SignalMeasurementInformation    OPTIONAL,

sl-AoA-Error						  SL-AoA-LocationInformationError		 OPTIONAL,

...

}

SL-AoA-SignalMeasurementInformation ::= SEQUENCE {

sl-AoA-MeasList                         SEQUENCE (SIZE(1.. maxNrOfUEs)) OF SL-AoA-MeasElement,

...

}

SL-AoA-MeasElement ::= SEQUENCE {

applicationLayerID                    OCTET STRING,

sl-LCS-GCS-Translation                LCS-GCS-Translation       OPTIONAL,  -- sl-LCS-to-GCS-translation

los-NLOS-Indicator                    LOS-NLOS-Indicator        OPTIONAL,  -- sl-losNlosIndicator

sl-AngleQuality                       MeasurementAngleQuality   OPTIONAL,  -- sl-AngleQuality

sl-AoA-AdditionalPathList             SL-AoA-AdditionalPathList OPTIONAL,

sl-AzimuthAoA-Result                  INTEGER (0..3599)         OPTIONAL,  -- sl-PRS-AoA

sl-POS-ARP-ID-Rx                      INTEGER (1..4)            OPTIONAL,  -- sl-pos-arpID-Rx

sl-PRS-ResourceId                     INTEGER (0..16)           OPTIONAL,  -- sl-PRS-ResourceId

sl-PRS-RSRP-Result                    INTEGER (0..126)          OPTIONAL,  -- sl-PRS-RSRP

sl-PRS-RSRPP-Result                   INTEGER (0..126)          OPTIONAL,  -- sl-PRS-RSRPP

sl-TimeStamp                          SL-TimeStamp              OPTIONAL,  -- sl-Timestamp

sl-ZenithAoA-Result                   INTEGER (0..1799)         OPTIONAL,  -- sl-PRS-AoA

...

}

SL-AoA-AdditionalPathList ::= SEQUENCE (SIZE(1..2)) OF SL-AoA-AdditionalPath

SL-AoA-AdditionalPath  ::= SEQUENCE {

sl-AngleQuality                            MeasurementAngleQuality   OPTIONAL,  -- sl-AngleQuality

sl-AzimuthAoA-AdditionalPathResult         INTEGER (0..3599)         OPTIONAL,  -- additionalPath-SL-PRS-AoA

sl-AzimuthAoA-LCS-GCS-Translation          LCS-GCS-Translation       OPTIONAL,  -- sl-LCS-to-GCS-translation

sl-ZenithAoA-AdditionalPathResult          INTEGER (0..1799)         OPTIONAL,  -- additionalPath-SL-PRS-AoA

sl-ZenithAoA-LCS-GCS-Translation           LCS-GCS-Translation       OPTIONAL,  -- sl-LCS-to-GCS-translation

sl-PRS-AdditionalPathRSRPP-Result          INTEGER (0..126)          OPTIONAL,  -- additionalPath-SL-PRS-RSRPP

...

}

MeasurementAngleQuality ::= SEQUENCE {

azimuthQuality              INTEGER (0..255),

zenithQuality               INTEGER (0..255)        OPTIONAL

}

SL-AoA-LocationInformationError ::= SEQUENCE {  undefined,

assistanceDataMissing,

notAllRequestedMeasurementsPossible,

...

}

-- TAG-SL-AOA-PROVIDELOCATIONINFORMATION-STOP

-- ASN1STOP

SL-AoA-ProvideLocationInformation field descriptions

los-NLOS-Indicator This field specifies the UE's best estimate of the LOS or NLOS of the UE measurements (including RSTD, RTOA, RSRP, RSRPP, AoA and UE Rx-Tx time difference).

sl-AngleQuality This field specifies the angle quality for measurement results reported. Scale factor 0.1 degree.

sl-AoA-AdditionalPathList This field specifies the sidelink PRS measurements based on additional path of arrival.

sl-AzimuthAoA-Result This field specifies the first path result of SL-AzimuthAoA.

sl-AzimuthAoA-LCS-GCS-Translation This field provides the angles α (bearing angle), β (downtilt angle) and γ (slant angle) for the translation of a Local Coordinate System (LCS) to a Global Coordinate System (GCS) as defined in TR 38.901 [8].

sl-POS-ARP-ID-Rx This field indicates ARP ID of an ARP used for reception for per-ARP measurement reporting. The ARP ID is used to uniquely identify an ARP associated with a UE.

sl-PRS-ResourceId This field specifies the PRS resource ID used for SL positioning measurements.

sl-PRS-RSRP-Result This field specifies the sidelink PRS reference signal received power (RSRP) measurement.

sl-PRS-RSRPP-Result This field specifies the SL-RSRPP measurement based on first path of arrival.

sl-TimeStamp This field specifies the time instance at which the SL-PRS RSRP (if included) measurement is performed.

sl-ZenithAoA-Result This field specifies the first path result of SL-ZenithAoA.

sl-ZenithAoA-LCS-GCS-Translation This field provides the angles α (bearing angle), β (downtilt angle) and γ (slant angle) for the translation of a Local Coordinate System (LCS) to a Global Coordinate System (GCS) as defined in TR 38.901 [8].

## 6.8	SLPP PDU SL-RTT Contents

#### –	SL-RTT-ProvideAssistanceData

-- ASN1START

-- TAG-SL-RTT-PROVIDEASSISTANCEDATA-START

SL-RTT-ProvideAssistanceData ::= SEQUENCE {

sl-RTT-Error					 SL-RTT-AssistanceDataError		  								OPTIONAL,

...

}

SL-RTT-AssistanceDataError ::= ENUMERATED { undefined,

assistanceDataNotAvailable,

...

}

-- TAG-SL-RTT-PROVIDEASSISTANCEDATA-STOP

-- ASN1STOP

SL-RTT-ProvideAssistanceData field descriptions

sl-RTT-Error This field provides SL-RTT error reasons.

#### –	SL-RTT-ProvideLocationInformation

-- ASN1START

-- TAG-SL-RTT-PROVIDELOCATIONINFORMATION-START

SL-RTT-ProvideLocationInformation ::= SEQUENCE {

sl-RTT-SignalMeasurementInformation   SL-RTT-SignalMeasurementInformation    OPTIONAL,

sl-RTT-Error					 	  SL-RTT-LocationInformationError		 OPTIONAL,

...

}

SL-RTT-SignalMeasurementInformation ::= SEQUENCE {

sl-RTT-MeasList                         SEQUENCE (SIZE(1..maxNrOfUEs)) OF SL-RTT-MeasElement,

...

}

SL-RTT-MeasElement ::= SEQUENCE {

applicationLayerID                    OCTET STRING,

los-NLOS-Indicator                    LOS-NLOS-Indicator        OPTIONAL,  -- sl-losNlosIndicator

sl-POS-ARP-ID-Rx                      INTEGER (1..4)            OPTIONAL,  -- sl-pos-arpID-Rx

sl-PRS-RxTxTimeDiffMeasResult         SL-PRS-RxTxTimeDiffMeasResult,

...

}

SL-PRS-RxTxTimeDiffMeasResult ::= CHOICE {

single-SL-PRS-RxTxTimeDiff        SL-PRS-RxTxTimeDiffResult,

multiple-SL-PRS-RxTxTimeDiff          SEQUENCE {

sameSL-PRS-TxAndDiffSL-PRS-Rx         SEQUENCE (SIZE (2..4)) OF SL-PRS-RxTxTimeDiffResult    OPTIONAL,

sameSL-PRS-RxAndDiffSL-PRS-Tx         SEQUENCE (SIZE (2..4)) OF SL-PRS-RxTxTimeDiffResult    OPTIONAL

},

...

}

SL-PRS-RxTxTimeDiffResult ::= SEQUENCE {

sl-PRS-ResourceId             INTEGER (0..16)               OPTIONAL,  -- sl-PRS-ResourceId

sl-PRS-RxTxTimeDiffResult         CHOICE {

k0                                INTEGER (0..1970049),

k1                                INTEGER (0..985025),

k2                                INTEGER (0..492513),

k3                                INTEGER (0..246257),

k4                                INTEGER (0..123129),

k5                                INTEGER (0..61565)

}                                                           OPTIONAL,  -- sl-PRS-RxTxTimeDiff

sl-PRS-RSRP-Result            INTEGER (0..126)              OPTIONAL,  -- sl-PRS-RSRP

sl-PRS-RSRPP-Result           INTEGER (0..126)              OPTIONAL,  -- sl-PRS-RSRPP

sl-RTT-AdditionalPathList     SL-RTT-AdditionalPathList     OPTIONAL,

sl-TimeStamp                  SL-TimeStamp                  OPTIONAL,  -- sl-Timestamp

sl-TimingQuality              SL-TimingQuality              OPTIONAL,  -- sl-TimingQuality

tx-TimeInfo                   SL-TimeStamp                  OPTIONAL,  -- tx-Time-Info

...

}

SL-RTT-AdditionalPathList ::= SEQUENCE (SIZE(1..8)) OF SL-RTT-AdditionalPath

SL-RTT-AdditionalPath  ::= SEQUENCE {

sl-PRS-RxTxTimeDiffAdditionalPathResult    CHOICE {

k0                                         INTEGER (0..8191),

k1                                         INTEGER (0..4095),

k2                                         INTEGER (0..2047),

k3                                         INTEGER (0..1023),

k4                                         INTEGER (0..511),

k5                                         INTEGER (0..255)

}                                                                   OPTIONAL,  -- additionalPath-SL-PRS-Rx-Tx-TimeDiff

sl-PRS-AdditionalPathRSRPP-Result          INTEGER (0..126)         OPTIONAL,  -- additionalPath-SL-PRS-RSRPP

tx-TimeInfo                                SL-TimeStamp             OPTIONAL,  -- tx-Time-Info

...

}

SL-RTT-LocationInformationError ::= SEQUENCE {  undefined,

assistanceDataMissing,

notAllRequestedMeasurementsPossible,

...

}

-- TAG-SL-RTT-PROVIDELOCATIONINFORMATION-STOP

-- ASN1STOP

SL-RTT-ProvideLocationInformation field descriptions

los-NLOS-Indicator This field specifies the UE's best estimate of the LOS or NLOS of the UE measurements (including RSTD, RTOA, RSRP, RSRPP, AoA and UE Rx-Tx time difference).

sl-POS-ARP-ID-Rx This field indicates ARP ID of an ARP used for reception for per-ARP measurement reporting. The ARP ID is used to uniquely identify an ARP associated with a UE.

sl-PRS-ResourceId This field specifies the PRS resourde ID used for SL positioning measurements.

sl-PRS-RxTxTimeDiffResult This field specifies SL Rx-Tx time difference measurement based on first path of arrival. The mapping of the field is defined in TS 38.133 [13].

sl-PRS-RSRP-Result This field specifies the sidelink PRS reference signal received power (RSRP) measurement.

sl-PRS-RSRPP-Result This field specifies the SL-RSRPP measurement based on first path of arrival.

sl-RTT-AdditionalPathList This field specifies the sidelink PRS measurements based on additional path of arrival.

sl-TimeStamp This field specifies the time instance at which the SL Rx-Tx time difference and SL-PRS RSRP (if included) measurement is performed.

## 6.9	SLPP PDU SL-TDOA Contents

#### –	SL-TDOA-ProvideAssistanceData

-- ASN1START

-- TAG-SL-TDOA-PROVIDEASSISTANCEDATA-START

SL-TDOA-ProvideAssistanceData ::= SEQUENCE {

sl-PositionCalculationAssistanceTDOA    SL-PositionCalculationAssistanceTDOA    OPTIONAL,

sl-TDOA-Error					 	  	SL-TDOA-AssistanceDataError		  		OPTIONAL,

...

}

SL-PositionCalculationAssistanceTDOA ::= SEQUENCE {

sl-RTD-Info                              SL-RTD-Info    OPTIONAL,

...

}

SL-TDOA-AssistanceDataError ::= ENUMERATED { undefined,

assistanceDataNotAvailable,

...

}

-- TAG-SL-TDOA-PROVIDEASSISTANCEDATA-STOP

-- ASN1STOP

SL-TDOA-ProvideAssistanceData field descriptions

sl-RTD-Info This field provides synchronization information of SL Anchor UEs.

sl-TDOA-Error This field provides SL-TDOA error reasons.

#### –	SL-TDOA-ProvideLocationInformation

-- ASN1START

-- TAG-SL-TDOA-PROVIDELOCATIONINFORMATION-START

SL-TDOA-ProvideLocationInformation ::= SEQUENCE {

sl-RSTD-ReferenceUE-Info               SEQUENCE {

applicationLayerID                     OCTET STRING

}                                                                              OPTIONAL,

sl-TDOA-SignalMeasurementInformation   SL-TDOA-SignalMeasurementInformation    OPTIONAL,

sl-TDOA-Error					 	   SL-TDOA-LocationInformationError		   OPTIONAL,

...

}

SL-TDOA-SignalMeasurementInformation ::= SEQUENCE {

sl-TDOA-MeasList                         SEQUENCE (SIZE(1..maxNrOfUEs)) OF SL-TDOA-MeasElement,

...

}

SL-TDOA-MeasElement ::= SEQUENCE {

applicationLayerID                    OCTET STRING,

los-NLOS-Indicator                    LOS-NLOS-Indicator        OPTIONAL,  -- sl-losNlosIndicator

sl-POS-ARP-ID-Rx                      INTEGER (1..4)            OPTIONAL,  -- sl-pos-arpID-Rx

sl-PRS-ResourceId                     INTEGER (0..16)           OPTIONAL,  -- sl-PRS-ResourceId

sl-PRS-RSRP-Result                    INTEGER (0..126)          OPTIONAL,  -- sl-PRS-RSRP

sl-PRS-RSRPP-Result                   INTEGER (0..126)          OPTIONAL,  -- sl-PRS-RSRPP

sl-RSTD-Result                        CHOICE {

k0                                    INTEGER (0..1970049),

k1                                    INTEGER (0..985025),

k2                                    INTEGER (0..492513),

k3                                    INTEGER (0..246257),

k4                                    INTEGER (0..123129),

k5                                    INTEGER (0..61565)

}                                                                OPTIONAL,  -- sl-PRS-RSTD

sl-TDOA-AdditionalPathList            SL-TDOA-AdditionalPathList OPTIONAL,

sl-TimeStamp                          SL-TimeStamp               OPTIONAL,  -- sl-Timestamp

sl-TimingQuality                      SL-TimingQuality           OPTIONAL,  -- sl-TimingQuality

...

}

SL-TDOA-AdditionalPathList ::= SEQUENCE (SIZE(1..8)) OF SL-TDOA-AdditionalPath

SL-TDOA-AdditionalPath  ::= SEQUENCE {

sl-RSTD-AdditionalPathResult          CHOICE {

k0                                    INTEGER (0..1970049),

k1                                    INTEGER (0..985025),

k2                                    INTEGER (0..492513),

k3                                    INTEGER (0..246257),

k4                                    INTEGER (0..123129),

k5                                    INTEGER (0..61565)

}                                                               OPTIONAL,  -- additionalPath-SL-PRS-RSTD

sl-PRS-AdditionalPathRSRPP-Result      INTEGER (0..126)         OPTIONAL,  -- additionalPath-SL-PRS-RSRPP

...

}

SL-TDOA-LocationInformationError ::= SEQUENCE {  undefined,

assistanceDataMissing,

notAllRequestedMeasurementsPossible,

...

}

-- TAG-SL-TDOA-PROVIDELOCATIONINFORMATION-STOP

-- ASN1STOP

SL-TDOA-ProvideLocationInformation field descriptions

los-NLOS-Indicator This field specifies the UE's best estimate of the LOS or NLOS of the UE measurements (including RSTD, RTOA, RSRP, RSRPP, AoA and UE Rx-Tx time difference).

sl-POS-ARP-ID-Rx This field indicates ARP ID of an ARP used for reception for per-ARP measurement reporting. The ARP ID is used to uniquely identify an ARP associated with a UE.

sl-PRS-ResourceId This field specifies the PRS resourde ID used for SL positioning measurements.

sl-PRS-RSRP-Result This field specifies the sidelink PRS reference signal received power (RSRP) measurement.

sl-PRS-hRSRPP-Result This field specifies the SL-RSRPP measurement based on first path of arrival.

sl-TDOA-AdditionalPathList This field specifies the sidelink PRS measurements based on additional path of arrival.

sl-RSTD-Result This field specifies the SL-RSTD measurement based on first path of arrival.

sl-RSTD-ReferenceUE-Info This field indicates reference UE information for SL-PRS based RSTD measurement report.

sl-TimeStamp This field specifies the time instance at which the SL RSTD and SL-PRS RSRP (if included) measurement is performed.

## 6.10	SLPP PDU SL-TOA Contents

#### –	SL-TOA-ProvideAssistanceData

-- ASN1START

-- TAG-SL-TOA-PROVIDEASSISTANCEDATA-START

SL-TOA-ProvideAssistanceData ::= SEQUENCE {

sl-PositionCalculationAssistanceTOA    SL-PositionCalculationAssistanceTOA    OPTIONAL,

sl-TOA-Error					 	   SL-TOA-AssistanceDataError		  	  OPTIONAL,

...

}

SL-PositionCalculationAssistanceTOA ::= SEQUENCE {

sl-RTD-Info                             SL-RTD-Info    OPTIONAL,

...

}

SL-TOA-AssistanceDataError ::= ENUMERATED { undefined,

assistanceDataNotAvailable,

...

}

-- TAG-SL-TOA-PROVIDEASSISTANCEDATA-STOP

-- ASN1STOP

SL-TOA-ProvideAssistanceData field descriptions

sl-RTD-Info This field provides synchronization information of SL Anchor UEs.

sl-TOA-Error This field provides SL-TOA error reasons.

#### –	SL-TOA-ProvideLocationInformation

-- ASN1START

-- TAG-SL-TOA-PROVIDELOCATIONINFORMATION-START

SL-TOA-ProvideLocationInformation ::= SEQUENCE {

sl-TOA-SignalMeasurementInformation   SL-TOA-SignalMeasurementInformation    OPTIONAL,

sl-TOA-Error					 	  SL-TOA-LocationInformationError		 OPTIONAL,

...

}

SL-TOA-SignalMeasurementInformation ::= SEQUENCE {

sl-TOA-MeasList                         SL-TOA-MeasElement,

...

}

SL-TOA-MeasElement ::= SEQUENCE {

applicationLayerID                    OCTET STRING,

los-NLOS-Indicator                    LOS-NLOS-Indicator        OPTIONAL,  -- sl-losNlosIndicator

sl-RTOA-Result                        CHOICE {

k0                                    INTEGER (0..1970049),

k1                                    INTEGER (0..985025),

k2                                    INTEGER (0..492513),

k3                                    INTEGER (0..246257),

k4                                    INTEGER (0..123129),

k5                                    INTEGER (0..61565)

}                                                               OPTIONAL,  -- sl-PRS-RTOA

sl-POS-ARP-ID-Rx                      INTEGER (1..4)            OPTIONAL,  -- sl-pos-arpID-Rx

sl-PRS-ResourceId                     INTEGER (0..16)           OPTIONAL,  -- sl-PRS-ResourceId

sl-PRS-RSRP-Result                    INTEGER (0..126)          OPTIONAL,  -- sl-PRS-RSRP

sl-PRS-RSRPP-Result                   INTEGER (0..126)          OPTIONAL,  -- sl-PRS-RSRPP

sl-TOA-AdditionalPathList             SL-TOA-AdditionalPathList OPTIONAL,

sl-TimeStamp                          SL-TimeStamp              OPTIONAL,  -- sl-Timestamp

sl-TimingQuality                      SL-TimingQuality          OPTIONAL,  -- sl-TimingQuality

...

}

SL-TOA-AdditionalPathList ::= SEQUENCE (SIZE(1..8)) OF SL-TOA-AdditionalPath

SL-TOA-AdditionalPath  ::= SEQUENCE {

sl-RTOA-AdditionalPathResult               CHOICE {

k0                                         INTEGER (0..16351),

k1                                         INTEGER (0..8176),

k2                                         INTEGER (0..4088),

k3                                         INTEGER (0..2044),

k4                                         INTEGER (0..1022),

k5                                         INTEGER (0..511)

}                                                                OPTIONAL,  -- additionalPath-SL-PRS-RTOA

sl-PRS-AdditionalPathRSRPP-Result          INTEGER (0..126)      OPTIONAL,  -- additionalPath-SL-PRS-RSRPP

...

}

SL-TOA-LocationInformationError ::= SEQUENCE {  undefined,

assistanceDataMissing,

notAllRequestedMeasurementsPossible,

...

}

-- TAG-SL-TOA-PROVIDELOCATIONINFORMATION-STOP

-- ASN1STOP

SL-TOA-ProvideLocationInformation field descriptions

los-NLOS-Indicator This field specifies the UE's best estimate of the LOS or NLOS of the UE measurements (including RSTD, RTOA, RSRP, RSRPP, AoA and UE Rx-Tx time difference).

sl-TOA-AdditionalPathList This field specifies the sidelink PRS measurements based on additional path of arrival.

sl-POS-ARP-ID-Rx This field indicates ARP ID of an ARP used for reception for per-ARP measurement reporting. The ARP ID is used to uniquely identify an ARP associated with a UE.

sl-PRS-ResourceId This field specifies the PRS resourde ID used for SL positioning measurements.

sl-PRS-RSRP-Result This field specifies the sidelink PRS reference signal received power (RSRP) measurement.

sl-PRS-RSRPP-Result This field specifies the SL-RSRPP measurement based on first path of arrival.

sl-RTOA-Result This field specifies the SL-RTOA measurement based on first path of arrival.

sl-TimeStamp This field specifies the time instance at which the SL RTOA and SL-PRS RSRP (if included) measurement is performed.