3GPP TSG-RAN WG2 Meeting #126		R2-240xxxx

Fukuoka, Japan, 20th May – 24th May 2024

Title:	[Draft] Reply LS on 2-step RACH for eRedCap

Response to:	R2-2404113/R1-2403646

Release:	Rel-18

Work Item:	NR_redcap_enh-Core

Source:	vivo [to be RAN2]

To:	RAN1

Cc: 	-

# Contact Person:

# Name:	                Chenli

E-mail Address:	 Chenli5g@vivo.com

# 1. Overall Description:

RAN2 would like to thank RAN1 for the reply LS on 2-step RACH for eRedCap in [R2-2404113/ R1-2403646]. RAN2 has discussed this issue, and concluded on the following [wording to be updated based on offline discussion]:

- The only case when eRedCap UEs can do 2-step RA is on 2-step RA resources not associated with any feature combination. The UE uses this when there are no eRedCap 2-step RA resources.

Besides, RAN2 has capture the above agreements in RAN2 specification.

# 2. Actions:

# To SA WG 2:

# RAN2 kindly request RAN1 to take the above information into account during the following work, and provide feedback, if any.

# 3. Date of Next RAN2 Meetings:

TSG RAN WG2 Meeting #127		19th Aug. – 23rd Aug. 2025						Maastricht, NL

TSG RAN WG2 Meeting #127bis		14th Oct. – 18th Oct. 2025						TBD, China