3GPP TSG-RAN WG4 Meeting # 111					R4-240xyz

Fukuoka, Japan, 20th  –24th  May, 2024

Title:	LS on RAN4 feature powerBoostRel18 and powerBoostTSRel18

Response to:

Release:	Rel-18

Work Item:	NR_cov_enh2

Source:	RAN WG4

To:	RAN WG2

Cc:	RAN WG1

Contact Person:

Name:	Chunhui Zhang

E-mail Address:	Chunhui (dot) Zhang (at) ericsson (dot) com

Attachments:

1. Overall Description:

RAN4 discuss the feature [41-2] and [42-3] below and agree the additional feature applicability in the Note of table below.

| Features | Index | Feature group | Components | Prerequisite feature groups | Need for the gNB to know if the feature is supported | Applicable to the capability signalling exchange between UEs (V2X WI only)”. | Consequence if the feature is not supported by the UE | Type (the ‘type’ definition from UE features should be based on the granularity of 1) Per UE or 2) Per Band or 3) Per BC or 4) Per FS or 5) Per FSPC) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | Capability interpretation for mixture of FDD/TDD and/or FR1/FR2 | Note | Mandatory/Optional |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| powerBoostRel18 | 41-2 | Power boosting for DFT-s-OFDM pi/2 BPSK and QPSK transmissions without modified spectrum flatness requirement | 1. Support of UE power boosting for DFT-s-OFDM pi/2 BPSK and QPSK without modified spectrum flatness requirement for PC3 and PC2 MPR reduction, when applicable as defined in 6.2 of TS 38.101-1.The power boosting is only enabled when signalled via RCC powerBoostPi2BPSKRel18 for BPSK and powerBoostQPSKRel18 for QPSK | 1-6, 1-7 | Yes | N/A | UE cannot power boost without modified spectrum flatness requirement | Per FS | NO | FR1 only | N/A | this feature can be enabled by network in below scenarios: Case 1: FR1 single band with single uplink CC configured in the band where power boosting capability is indicated in this band. Case 2: FR1 inter-band DL CA with a single uplink CC configured in a band where power boosting capability is indicated in the band, power boosting feature can be enabled in this FR1 NR band. Case 3: FR1 inter-band UL CA/DC, where a single CC is configured in each of the uplink bands and power boosting capability is indicated in one of the bands, power boosting feature can be enabled only in one of the bands Case 4: FR1+FR2 UL CA, FR1+FR2 DC, where a single CC is configured in each of uplink bands, power boosting feature can be enabled in the FR1 NR band. | Optional with capability signalling |
| powerBoostTSRel18 | 42-3 | Power boosting for DFT-s-OFDM pi/2 BPSK and QPSK transmissions with modified spectrum flatness requirement shaping | 1. Support of UE power boosting for DFT-s-OFDM pi/2 BPSK and QPSK with modified spectrum flatness requirement for PC3 and PC2 MPR reduction, when applicable as defined in 6.2 of TS 38.101-1. The power boosting is only enabled when signalled via RCC powerBoostPi2BPSKRel18 for BPSK and powerBoostQPSKRel18 for QPSK | 1-6, 1-7 | Yes | N/A | UE cannot power boost with modified spectrum flatness requirement | Per FS | NO | FR1 only | N/A | this feature can be enabled by network in below scenarios: Case 1: FR1 single band with single uplink CC configured in the band where power boosting capability is indicated in this band. Case 2: FR1 inter-band DL CA with a single uplink CC configured in a band where power boosting capability is indicated in the band, power boosting feature can be enabled in this FR1 NR band. Case 3: FR1 inter-band UL CA/DC, where a single CC is configured in each of the uplink bands and power boosting capability is indicated in one of the bands, power boosting feature can be enabled only in one of the bands Case 4: FR1+FR2 UL CA, FR1+FR2 DC, where a single CC is configured in each of uplink bands, power boosting feature can be enabled in the FR1 NR band. | Optional with capability signalling |

2. Actions:

To RAN WG1/WG2 group.

ACTION: 	RAN4 would like RAN2 consider the above table on feature [41-2] and [42-3] defined above.

3. References:

4. Date of Next TSG-RAN WG4 Meetings:

TSG RAN WG4 Meeting #112		August 19-23 , 2024					Maastricht

TSG RAN WG4 Meeting #112bis		Oct 14-18 , 2024					China