3GPP TSG-RAN WG4 Meeting #111	R4-2410686

Fukuoka, Japan, May 20 - 24, 2024

Title: 	WF on Rel-19 non-collocated UE RF requirements

Agenda Item:	10.7.3

Source: 	KDDI

Document for:	Approval

# Topic #2:  Rel-19 Type-4

## Sub-topic 2-1: UE RF requirements for Type 4 EN-DC/NR-CA

< Issue 2-1-1:  Power imbalance requirements and REFSENS >

Agreement:

- Use 25dB power imbalance for 4Rx REFSENS + 1dB for Type 4

< Issue 2-1-2:  How to capture the power imbalance and REFSENS requirements >

Agreement:

- Define the Type 4 receiver imbalance requirements in the same table as for Type 2.

  - FFS on the details of modification

< Issue 2-1-3:  Minimum DL frequency separation >

Agreement:

- Center of BWanother relative to edge of BWwanted is assumed to be at least 80MHz+BWanother/2 away from the edge of the wanted CC.

- RAN4 doesn’t need specify anything in RAN4, but also needs to send LS to RAN5 same as LS R4-2316951(Ericsson) for Type 2 in the next meeting.

< Issue 2-1-4:  Maximum DL frequency separation >

Agreement:

- No limitation for maximum DL frequency separation

## Sub-topic 2-2: UE Capability(s)/UE behavior and network signaling for Type 4 EN-DC/NR-CA

< Issue 2-2-1:  New UE Capabilities for Type 4a(EN-DC) and 4b(EN-DC/NR-CA) >

Way Forward:

- Continue further discussion on the following two options and conclude it in the next meeting.

  - Option 1-1. Add new UE capabilities for Type 4a and Type 4b support indication.

  - Option 1-2. Add one new UE capability for Type 4a and Type 4b support indication.

< Issue 2-2-2:  Whether to support Type 2 capability by UE having Type 4 capabilities >

Agreement:

- If UE reports the Type 4 capability, Type 2 capability shall be deemed as support by default regardless of whether UE indicates Type-2 capability or not.

  - If UE reports the Type 4 capability, it is not necessary for UE to report Type 2 capability.

  - If the issue is identified for these bullets, RAN4 will revisit them.

< Issue 2-2-3:  New BS Signaling to switch between Type 4a/4b and Type 1(collocated) >

Way Forward:

- First, conclude discussions of whether to add new UE capability(s) for Type 4.

- And then, continue further discussion on BS signalling in the next meeting.

< Issue 2-2-4:  New BS Signaling to switch between Type 4a/4b and Type 2 >

Way Forward:

- First, conclude discussions of whether to add new UE capability(s) for Type 4.

- And then, continue further discussion on BS signalling in the next meeting.

< Issue 2-2-5: When to inform RAN2 the demand on new UE capability(s) and new BS signaling(s) >

Way Forward:

- Given the discussions on UE capabilities and network signalling, it is not hurry to send this.

< Issue 2-2-6:  UE behavior between Type 1, Type 2 and Type 4a/4b with new BS Signaling >

Way Forward:

- First, conclude discussions of whether to add new UE capability(s) and BS signalings for Type 4.

- And then, continue further discussion on BS signalling/UE behavior in the next meeting.

## Other aspects (incl. clarification of contiguous LTE CCs)

< Issue 2-3-1:  The number of B42 CCs for EN-DC >

Way Forward:

- Check the number with operators until next meeting again.

< Issue 2-3-2:  The number of NR CCs for EN-DC and NR-CA >

Way Forward:

- Check the number with operators until next meeting again.

< Issue 2-3-3:  Terminology for power imbalance requirement to take into account multiple B42 CCs >

Way Forward:

- Align to the agreed WF R4-2406628(Huawei) in the last meeting.