## Slide 1: WayForward on handling of legacy bands n81, n261 and n262
CMCC, Apple
3GPP TSG-RAN5 Meeting #105 R5-246698
Orlando, United States, Nov 13 - 17, 2024

## Slide 2: How to handle legacy bands n81, n261 and n262
In the last RAN5#105 meeting, CMCC brought a paper ( R5-245711) to discuss how to handle legacy bands n81, n261 and n262 and called for Interested Operators/Deployers for those bands after RAN5#104. After one meeting cycle, the status of interested deployers for legacy bands is shown below:
Observation 1: The status of interested deployer for Ongoing legacy bands so far
  For n81, no interested deployer and the band is completed;
  For n261, 1 interesed deployer "Verizon"and the band is completed;
  For n262, no interested deployer and the band is still incomplete
Based on the received request and the handling methods proposed in R5-245711, the following proposals are given:
Proposal 1: For n81, since there is no interested deployer for it, to capture "Lack of interested deployer" in "Comments" Column of PRD21 to give the eco-system (including TE vendoer) a heads-up on this.
draft PRD21 excel v1.11.0

## Slide 3: How to handle legacy bands n81, n261 and n262
Proposal 2: For n261, to replace "legacy" with interested operator "Verizon" in PRD21.
Observation 2: For n262, there are some incomplete snippets existing in TS 38.521-2, including cl. 6.2.1.1.3.3, 6.2.4, 6.2D.1.1, 6.2D.1.2, 6.6.1, 6.6.2, 7.3.2, 7.3.4, 7.5, 7.5A.0, 7.6.2, 7.6A.2 and Annex K.1.11
Proposal 3: For n262, to remove all the incomplete snippets above in Observation 2 from TS 38.521-2 and to capture the Tdoc numbers of the clear-up CRs in the “Comments” Column for n262 in PRD21 excel list. To revise the status of n262 back into “pending”.
draft PRD21 excel v1.11.0
draft PRD21 excel v1.11.0

## Slide 4: Thank you!