## Slide 1: Demonstration of test frequency calculation tool
Implemented in Python
R5-247045, CR3387
3GPP TSG-RAN5 Meeting #105
Orlando, United States, 18th Nov 2024 - 22nd Nov 2024

## Slide 2: Supported Functionality of the Tool
Python tool
User input (GUI)
( Configuration, Band, SCS, UL/DL -> Table )
3GPP Tables
(38.101, 38.213, 38.508)
3GPP parameters, hard coded in python.
(38.101, 38.213, 38.508)
3GPP Tables, coded in python.
(38.101, 38.508)
Manual insertion
Input parameters in CSV format, as a reference.
Single Freq
TDD, FR1, FR2
Intra CA Contiguous
TDD, FR1, FR2
Intra CA Noncontiguous UL, TDD, FR1
More Types
DL
DL&UL
Possibly in JSON format, outside python.
More Types
Test frequencies and Coreset#0 in CSV format.
SSB and Coreset#0 Calculation

## Slide 3: What types of frequency calculations does the tool support at this stage? (38.508-1, Annex C)
C.3: Determination of SSB and CORESET#0
C.2.1.1: Determination of test frequencies for Low-, Mid- and High-Range, (FR1 and FR2), excluding UL testfrequencies for FDD.
C.2.4.2.2: Determination of test frequencies for Low-, Mid- and High-Range, for NR Intra-band Contiguous CA, FR1 and FR2, for 2 carriers only.
C.2.4.3: Determination of test frequencies for NR Intra-band Non-Contiguous CA , only FR1, only 2 carriers.

## Slide 4: What is not supported in 38.508-1, at this stage?
Potentially all clauses above are possible to implement.
Further studies are required.
C.2.1.1: Determination of test frequencies for Low-, Mid- and High-Range, for UL testfrequencies (FDD Bands).
C.2.1.2: Determination test frequencies for Mid-Low and Mid-High-Range for signalling tests.
C.2.2: Determination of test frequencies for asymmetric NR bands and symmetric uplink and downlink channel bandwidth combinations.
C.2.3: Determination of test frequencies for asymmetric uplink and downlink channel bandwidth combinations.
C.2.4.2A: Determination of test frequencies for FR1 NR Intra-band Contiguous CA without UL CA for bands with uplink bandwidth less than downlink bandwidth.
C.2.5: Frequency determination for supplemental uplink.
C.2.6: Frequency determination for EN-DC configurations.
C.4: Determination of SSB and CORESET#0 for RRM testing with SSB SCS 120 kHz and 240 kHz.

## Slide 5: Proposal 1
Make this python tool a part of the standard to support calculations of test frequencies that is not added in test frequency tables due to too many bandwidth combinations.
In addition, the tool can be used to generate data as input to CRs for new bands/CA combinations. This will still require updates of the tool for specific band/CA configurations.

## Slide 6: What is the way forward (if any)?
Two options:
1. Add functionality to “automatically” generate CRs/test frequencies for new Bands/CA configurations
  Represent all needed input tables in JSON format. This will make it possible for the tool to collect all needed input and provide data for a new table of test frequencies. (Notes will still be a separate problem to solve). Representing tables in JSON is, to my understanding, ongoing in RAN4 today by the use of a tool.
2. Add functionality in terms of more configuration types (see slide 4) that then also will require manual input of parameters for every specific configuration.

## Slide 7: What is next?
Put tool on the 3GPP Forge, GIT server.
Move hardcoded input outside Python code (in JSON format?) to make it possible to include bands/configurations without updating python code.
Represent input 3GPP Tables in JSON format (today, they are represented python).
Represent output in JSON (today the format is in .CSV format).
Represent input tables from specs (38.101, 38.213, 38.508), that today is manually read, in JSON format. This will remove need for any hardcoded band/configuration specific parameters in the tool and will then possibly make the tool support any band/CA configuration, as long as the needed input is available in RAN4 specs. (Long term)