## Slide 1
China Mobile’s View on 5G-A R20

## Slide 2: Items proposed for 5G-A R20
Energy saving and efficiency
Voice over satellite, and related enhancement
AIML
XR and immersive media enhancement
NG-RTC enhancement
Total TU estimation of 1-9 is 66
Ambient IoT
ISAC
Service based UPF and Edge Computing
Redundant transmission
Digital Twin(leading by SA5)

## Slide 3: Over view on Rel-20 5G-A Content
S.NO. | Title | Brief Description and Key Objectives | TU estimation | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Energy saving and efficiency | Candidate Work tasks: Enhancement of energy information exposure with including renewable energy, carbon footprint; RAN enhancement to support per-UE energy consumption information exposure. Network enhancement to satisfy UE energy status requirement Interaction between PCF and EIF to help policy adjustment or reducing the service performance with user consent/regulatory(Depending on R19 progress). | 4+4 | TR22.883 SA1 | SA2 | Maybe | SA5
2 | Enhancements on NTN | Candidate Work tasks: support of efficient IMS voice over GEO with NB-IoT 5GC onboard and onboard traffic processing (LEO) support of UE-sat-UE communication without IMS-AGW onboard(LEO NR-NTN) Enhanced support for emergency communications and mission critical services using satellite access Define an ultra low rate codec with considering IMS over GEO performance requirements(leading by SA4). | 4+4 | TR22.887 SA1 | SA2 | Yes | SA4
3. | AI/ML enhancements for 5GS Service | Candidate Work Tasks: New Use Case: AI Exposure for Optimizing OTT application, Study the mechanisms of NWDAF interacting with AF to implement a closed-loop capability. Leveraging AI Technologies: Study whether and how to enhance architecture to support AI/ML Model Evaluation and Transmission, Online Learning and Reinforcement Learning. Feature enhancement: VFL with UE involvement | 3+3 | No | SA2 | No | SA3 for security

## Slide 4
S.NO. | Title | Brief Description and Key Objectives | TU estimation | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
4 | Extended Reality and media service (XRM) | Candidate Work Tasks: 1. Further enhancement for MoQ (Media Over QUIC),e.g. introduction of content delivery based on MoQ; 2. Coordination enhancement of XRM services and network, including multi-modal services for multiple users and QoS handling enhancement; (Depending on R19 progress). 3.Service continuity assurance to support wide-area mobility scenario; 4.Potential architecture enhancements to support new service scenarios e.g., holographic video, volumetric video, and mixed reality. 5.Identify and define relevant immersive media formats and codec to support XR and immersive media enhancement. (leading by SA4) | 4+4 | SA1 Multi-modality requirement TS22.261 | SA2 | Maybe | SA4
5 | NG RTC enhancements | Candidate Work Tasks: support exposure of IMS capability for voice/video/messaging completion on DC3/DC4 interfaces to support P2A2P DC procedures of adding BDC/ADC to a voice call before alerting phase support one-way audio/video between different PLMNs | 3+3 | eMMTel | SA2 | No | No
6 | Ambient IoT | Candidate Work Tasks includes: 1. Overall architecture and function enhancement to support for Type C devices and the traffic type of DO-A. 2. Network enhancements for device management, e.g. mobility management and location, for all types of Ambient IoT devices. 3. Enhancements for roaming. | 3+3 | No | SA2 | Yes, Major | SA3 for security, SA5 for charging
Over view on Rel-20 5G-A Content

## Slide 5
S.NO. | Title | Brief Description and Key Objectives | TU estimation | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
7 | ISAC | Candidate Work Tasks： Architecture and function enhancements to support sensing, e.g., data collection and transport. Service authorization and revocation. This includes investigating mechanisms for authorization and revocation sensing service requests from the service consumer (e.g. 3rd party application, 5GC NF). Discovery and selection of sensing entities (e.g. gNB, 5GC NF) based on service requirements triggered by the service request and capability of the sensing entities. | 5+5 | Yes, TR 22.837，TS 22.137 | SA2 | RAN dependencies for WT-1/4 are minor, while RAN dependencies for WT-2/3/5 are major. | SA3 for security, SA5 for charging
8 | Service based UPF and Edge Computing | Candidate Work Tasks: Support multiple types of protocol message identification, reporting and handling. User plane service awareness. Support UE to dynamically aware the service requirement and support dynamically adjustment in UPF. Enhance the interaction between UE->UPF to support this adjustment. Support E2E time delay measurement and exposure to enable flexible EAS discovery(flow level). Enhance service based UPF to support module design and deployment, e.g., supporting data storage and data processing. Support service based N4 interface | 4+4 | No | SA2 | No | SA3 for security, SA5 for charging
Over view on Rel-20 5G-A Content

## Slide 6
S.NO. | Title | Brief Description and Key Objectives | TU estimation | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
9 | Redundant transmission | Candidate Work Tasks: Only support NR(TN)+NR(TN) case. Support single UE to access two gNBs with establishment of two PDU sessions to support high reliability. FRER enhancement based on TSN architecture Dynamic 5G LAN(decouple the DNN/S-NSSAI with the 5G LAN) | 3+3 | No | SA2 | No | No
10 | Network digital-twins enhancement | Candidate Work Tasks: 1.NDT role in the management loop and relationship with the existing network functions/entities including e.g., NWDAF and MDAS. 2.The data synchronization mechanism with the NFs and NEs. 3.The nested NDT and NDT Instance collaboration mechanism 4. New feature enhancements, e.g., NDT for Intent negotiation |  | No | SA5 | Yes | SA2 for data synchronization
Over view on Rel-20 5G-A Content

## Slide 7: Energy saving and efficiency Ph2
New service requirement in SA1
Services provided on different energy consumption levels can be selected based on UE power status.
Energy consumption and CO2 equivalent calculation and exposure.
Users’ carbon footprint information exposure.
Tolerance for QoS degradation caused by network energy saving
Further requirement based on R19 work
RAN is configured to provide per-UE level energy consumption information to 5GC.
UE/PDU session/flow level energy consumption information estimation.
Enhancement based on Architecture of energy saving and efficiency in R19
Enhancement of energy information exposure with including renewable energy, carbon footprint;
RAN enhancement to support per-UE energy consumption information exposure.
Network enhancement to satisfy UE energy status requirement
Interaction between PCF and EIF to help policy adjustment or reducing the service performance with user consent/regulatory(Depending on R19 progress).
Candidate Work Tasks

## Slide 8: Enhancements NTN
Further enhancement of TN/NTN convergence to better support some TN fundamental services, e.g., voice and mission critical services in 5G-A era
Features left from R19 because of the TU limitation e.g. S&F for 5GC
Candidate Work Tasks
  support of efficient IMS voice over GEO based on NB-IoT
  5GC onboard and onboard traffic processing (LEO)
  support of UE-sat-UE communication without IMS-AGW onboard(LEO NR-NTN)
  Enhanced support for emergency communications and mission critical services using satellite access
Scenario | UE type | Transmissiondata rate |  | Call setup time
 |  | UL | DL | 
IMS voice call using GEO | Handheld | [1-3] kbit/s | [1-3] kbit/s | [4-30] s NOTE 2
Potential KPI Requirements for IMS Voice Call Using GEO

## Slide 9: AI/ML enhancements for 5GS Service
Motivation: The work of AI/ML for 5GS in Rel-20 is proposed to expand the scope of network AI capabilities and services by introducing new Use Case, enhancing the existing AI/ML feature and leveraging new AI technologies.
Usage scenario: Up to Rel-19, the SA2 has studied and specified the AI-enabled network architecture and leveraged Artificial Intelligence (AI)/Machine Learning (ML) to enable 5GC in terms of data collection, ML model training, analytics inference, and closed-loop procedures by consuming data analytics, etc.
WT#1 AI Exposure for Optimizing OTT application
  Study whether and how to further expose analytics data via NWDAF.
  Study the mechanisms of NWDAF interacting with AF to implement a closed-loop capability.
WT#2 Feature enhancement
  Study network architecture enhancement to support vertical federated learning, allowing UE domain to exchange necessary intermediate information to assist E2E data analysis without exposing RAW data.
WT#3 Leveraging AI Technologies
AI/ML Model Evaluation and Transmission: Study the model evaluation and transmission mechanism for guaranteeing model perfomance and efficiency before the AI/ML model provisioning.
Online Learning: Study network architecture enhancement to support online learning, able to quickly adjust the model in real-time based on online feedback data, enabling the model to reflect changes in a timely manner and improve the accuracy of prediction.
Reinforcement Learning: Study network architecture enhancement to support the mechanism of reinforcement learning.
Candidate Work Tasks

## Slide 10: Extended Reality and media service (XRM)
MoQ (Medio Over QUIC) based new media network enhancement
  Enhancements on user plane to support MoQ based service content sharing, including content caching, storage, duplication, distribution, etc., in order to reduce transmission latency and bandwidth
  Flexible mapping between MoQ metadata and PDU Set related information
Coordination enhancement of XRM services and network
  Coordination of multi-modal data flows for multiple users, considering the synchronization information of multiple data flows (e.g. flow level, packet level) and service characteristic related information
Service continuity assurance for XR services to support wide-area mobility scenario
Potential network architecture enhancements and technical solutions for new service e.g., holographic video, volumetric video, and mixed reality, in order to support the system capacity, end-to-end latency, spatial reconstruction, spatial positioning, etc.
Identify and define relevant immersive media formats and codec to support XR and immersive media enhancement. (leading by SA4)
Service Provider
UPF
（relay）
UPF
（relay）
UPF
（relay）
Mesh Storage
Glasses-free 3D
AR/VR
Cloud Game
Distribution
Global Index
AMF
SMF
PCF
AS
UPF
AF
RAN
UE
2. Multi-modal service coordination config
1. Multi-modal service coordination policy
3. In-band QoS adjustment
Audio
Video
Tactile, other sensors

## Slide 11: NG RTC enhancements
The architecture and the procedures has been defined during two phases of NG_RTC to provide a DC based architecture to support real time services of AR, Avatar and the exposure of IMS capability
Some aspects of IMS capability exposure needs further enhancements
  In R19 IMS capability for IMS session management of voice/video is assumed based on OMA APIs, which requires two sets of APIs to support an IMS session with audio/video media and DC media.
  It is still not clear how DC3 and DC4 supports interactions to manage P2A2P DC, which is not specified in previous releases
  It is not yet supported that BDC/ADC is added in a voice call before the alerting phase, which can be useful to provide customized early media
  It is not clear how to handle the one-way audio/video service between different PLMNs, e.g. PLMN A wants to send a one-way audio/video to User B, and PLMN B wants to send a one-way audio/video to User A, the sdp between PLMN A and PLMN B is sendrecv, but the SDP sent to User A and User B should be sendonly.
Candidate Work Tasks
  support exposure of IMS capability for voice/video/messaging
  completion on DC3/DC4 interfaces to support P2A2P DC
  procedures of adding BDC/ADC to a voice call before alerting phase
  support one-way audio/video between different PLMNs

## Slide 12: Ambient IoT
Scenarios and Motivation
  By R19, SA2 has studied network architecture, identifiers, and services to support Ambient IoT indoor application scenarios using low-end Ambient IoT device types without DO-A capability.
  However, SA2 did not study Ambient IoT outdoor application scenarios using high-end IoT devices (e.g., Type-C devices with Do-A capability).
  The study item in Rel-20 is proposed to focus on supporting various outdoor/roaming use cases by using high-end Ambient IoT devices (e.g., Type C devices with DO-A capability).
Candidate Work Tasks
  Enhancements in architecture, management, and service support for Type C devices and the traffic type of DO-A.
  Enhancements of device management, e.g. mobility management and location, for all types of Ambient IoT devices..
  Study how to manage the devices when the devices move to another PLMN.
  Enhancements to support encryption, authentication, and secure connection of a group of Ambient IoT devices moving between different PLMNs.

## Slide 13: Integrated Sensing and Communication
Motivation
  32 scenarios have been introduced in SA1, involving 6 aspects: Smart transportation, UAV, Smart living, Smart city, Smart factory, data privacy/security.
  With the integration of sensing, 5GS is able to setup the connection between the physical and digital world, and enable various new services for public and industry customers.
  Some operators such as CMCC already did some early trail, but without standardized solution
Candidate Work Tasks
  Architecture and function enhancements to support sensing, e.g., data collection and transport.
  Service authorization, revocation and exposure. This includes investigating mechanisms for authorization and revocation sensing service requests from the service consumer (e.g. 3rd party application, 5GC NF).
  Discovery and selection of sensing entities (e.g. gNB, 5GC NF) based on service requirements triggered by the service request and capability of the sensing entities.

## Slide 14: Enhancement for Service based UPF
Support E2E QoS adjustment to improve user experience
  UE dynamic aware the requirements and request to UPF to adjust the QoS
  Support header identification, for example, in IETF, the in-band signaling, the UPF identifies the message and perform specific data handling
Module design and deployment
  UPF support data storage, data collection and processing.
  Service based N4 interface.
Service level N6 delay measurement and exposure
  N6 delay includes the delay to EAS and to CAS. Support the delay measurement to CAS.
  Support the N6 delay measurement exposure.
  Under different configuration of DSCP, support the flow level N6 delay measurement.

## Slide 15: Redundant transmission
Simultaneous transmission on dual 3GPP access, especially over NR + NR, providing redundant transmission, switching and splitting may provide better user experience.
For redundant transmission which only support NR+NR(TN only):
  Support single UE to access two gNBs with establishment of two PDU sessions to support high reliability.
  FRER enhancement based on TSN architecture
  For 5G LAN management, it is proposed to have dynamic 5G LAN groups establishment
  Dynamic 5G LAN(decouple the DNN/S-NSSAI with the 5G LAN)
1
2
4
5
I/O stream
Frame Replication
stream2
stream1
Frame Elimination

## Slide 16: Network digital twin enhancements
Candidate Work Tasks:
1.NDT role in the management loop and relationship with the existing network functions/entities including e.g., NWDAF and MDAS.
2.The data synchronization mechanism with the NFs and NEs.
3.The nested NDT and the NDT Instance collaboration
  An NDT service may use or rely on other NDTs as layered/nested components. The DTs that are components of the NDT are composed in a particular way to provide a specific modelling service.
  4.New feature enhancements, e.g., NDT for Intent negotiation.
  Conduct collaborative study on NDT and intent, using NDT to validate network intent strategies, enhance the reliability of strategy execution, and achieve an autonomous closed-loop for business operation and maintenance.
Service intent
Network intent
NDT
Network
Intent1
Report Intent1
Simulation:Intent1
Result:Intent1
Service
The nested NDT and the
NDT instance collaboration
NDT for Intent negotiation