## Slide 1: SA Topics for 5G A Release 20
Lenovo

## Slide 2: Outline
XRM enhancements
AI/ML & Analytics
Energy Saving
Multi-Access enhancements
Further enhancements on existing
5GA Features
Enhanced Traffic Management
Ambient IoT (normative work)
Sensing (dependency on RAN WG studies)
New 5GA
Features
Release 20 5G Advanced Considerations
Allocate at most 50% of available TUs to 5G Advanced Topics
Dedicated SID/WID per topic with well-defined objectives  Avoid combing objectives from different topics into one generic SID

## Slide 3: Overall View on Rel-20 5G-A Content
Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
Analytics/AIML including Enablement Layer (See slides 5, 6) | AIML Radio CN aspects Reinforcement learning Transfer Learning R19 Leftovers |  | SA2 | RAN WG1, RAN WG2, RAN WG3 | SA3 for security
 | Improvements to analytics/model correctness Roaming / multi-operator scenarios Vertical-tailored solutions Cross-domain AI/analytics R19 Leftovers |  | SA6 | No | SA2 (maybe), SA3
Ambient IoT (See slide 7) | Prioritize Rel-19 study conclusion Normative work (based on Rel-19 conclusion) in Rel-20 No Phase 2 study in parallel until normative work completes | FS_AmbientIoT, AmbientIoT | SA2 | Yes | SA3
Energy Saving (see slide 8) | Policy creation based on Energy credit control Interaction with Charging System for energy credit managements Introduce energy related analytics (e.g., from NWDAF) and how they can be used in other 5GC NFs | FS_EnergyServ, EnergyServ | SA2 | Maybe | SA3, SA5, SA6

## Slide 4: Overall View on Rel-20 5G-A Content
Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
Enhanced Traffic Management (see slide 9) | Identify enhancements for traffic management when the application session is fully encrypted |  | SA2 | No | SA3, SA4
Improvements for Multi Access (see slide 10) | Support energy-efficient traffic steering in the UE Support a MA PDU Session with two PSAs to enable multiaccess for edge services Help the network create traffic steering policy based on assistance information provided by the UE Improve efficiency of RTT/PLR measurements (measurements may consume a lot of radio resources and battery) |  | SA2 | No | SA3
XRM (See slide 11) | Study how to support XRM services over Multi-Access PDU session, NWDAF analytics enhancements in order to optimize support for XRM services Dynamic network information exposure |  | SA2 | Maybe | SA3, SA4
Sensing (see slide 12) | Study RAN based sensing for 5GA, applicable to a study led by RAN3 with limited study scope for the UAV use case with gNB-based sensing No implications to RAN1 and RAN2. No UE involvement. | FS_Sensing, Sensing | SA2 | RAN WG3 | SA3

## Slide 5: AIML/Analytics (SA2 Lead)
Topics from Rel 19 AIML_CN
  Study of AIML radio CN aspects (strong dependency on RAN requirements/agreements)
    Focus on Key Issue 1 (data collection from UE), Key Issue 2 (model transfer/delivery to UE) and Key Issue 3 (model identification alignment)
  Leftovers from Vertical Federated Learning (depends on R19 conclusions). Potential topics:
    Support of Distributed Inference where NWDAF Server and Clients support AnLF only.
    Further enhancements for Vertical Federated Learning sample/feature alignment (e.g. definition of Feature(s), sharing of Feature information during sample alignment, role of the NEF)
    Support roaming scenarios for VFL (e.g., when the NWDAF client is in the VPLMN and NWDAF server is in the HPLMN)
New AI/ML topics
  Further integration of NWDAF to 5G core by enhancing NWDAF to offer services beyond analytics
    Use of NWDAF to indicate to consumer whether an action had positive or negative impact to the system (i.e., using Reinforcement Learning)
  Support energy efficient operation: Define energy efficient operation for data collection and model training.
  Core Network enhancements for supporting Transfer Learning enabled ML operations
  Define mechanism to support efficient model training by re-using existing ML models and re-train them for new purpose. For example, use transfer learning and re-train an ML model to support additional service areas.

## Slide 6: AIML/Analytics (SA6 Lead)
In Rel-19 the normative phase introduced the AIMLE capabilities.
Possible enhancements can be covered in Rel-20:
  Improvements to ML-enabled ADAE analytics correctness and AIMLE service performance monitoring
  Support AIMLE capabilities assuming roaming / multi-operator scenarios
  Investigate vertical-specific issues and solutions (i.e. V2X, UAS,..)
  Support end-to-end AI/analytics and potentially coordinate with other AI-related work in SAx groups (e.g. for cross-domain ML operations).

## Slide 7: Ambient IoT
Before planning for Rel-20, the decision should be drawn for normative phase based on the Rel-19 AIoT study (depending on RAN WG decisions)
Proposed Way Forwards
  Extend the current study (Phase 1 AIoT) until March 2025 to finish the remaining open issues (taking into account SA3 conclusions)
  Normative phase (based on study conclusions) to be part of Rel-20. Normative work starts in April 2025 with target end Nov 2025 (5 meetings)
  No other AIoT phase 2 study in parallel until AIoT phase 1 normative work completes in Rel-20
  Phase 2 study can include DO-A operations, SA1 use cases from TS 22.361 (e.g. sensor data collection).

## Slide 8: Energy Saving
In Rel-19 the normative phase introduces basic functionality. Enhancements in Rel-20 can be helpful to have a full feature in 5GA.
Potential Topics (depends on R19 conclusions):
  Policy creation based on Energy credit control
  Interaction with Charging System for energy credit managements
  Introduce energy related analytics (e.g., from NWDAF) and how they can be used in other 5GC NFs

## Slide 9: Enhanced Traffic Management
Scope is to study enhancements which can facilitate the following:
  Support encrypted traffic detection (i.e. for the scenarios where the Application Session between the UE and the AS is fully encrypted, e.g. using QUIC).
  Enhancements to allow the core network to identify multiplexed media flows (in both UL and DL) for the case where the traffic between the UE and AS is fully encrypted.
  Enhancement to optimise exposure of network information to Applications

## Slide 10: Improvements for Multi Access
Support energy-efficient traffic steering in the UE
Support a MA PDU Session with two PSAs to enable multiaccess for edge services
Help the network create traffic steering policy based on assistance information provided by the UE
Improve efficiency of RTT/PLR measurements (measurements may consume a lot of radio resources and battery)

## Slide 11: XRM enhancements
New XRM Features
  Study how to support XRM services over Multi-Access PDU session, e.g., PDU set aware packet routing between two accesses
  Study NWDAF analytics enhancements in order to optimize support for XRM services (e.g. identifying optimal PDU Set QoS for an XRM service based on analytics)
  Study dynamic network information exposure to the application layer (e.g., via user plane)
Rel-19 leftover
  Further enhance PDU set handling in non-3GPP network, e.g., UL DSCP-PSI mapping, GRE enhancement to support PDU set based handling

## Slide 12: Sensing
To decide: Two-phase process.
  Phase 1: RAN based sensing for 5GA
  Phase 2: RAN and UE based sensing as a 6G Feature.
Proposal
  Phase 1: Study RAN based Sensing for 5GA in Rel-20.
    Applicable to a study led by RAN3 with limited study scope for the UAV use case with gNB-based Sensing (subject to RAN agreeing RAN WG3 study).
    No implications to RAN1 and RAN2. No UE involvement.
  Phase 2: Study RAN and UE based Sensing as a 6G Feature.
    Phase 2 starts after Phase 1 completes.

## Slide 13: Thanks!