## Slide 1: Views on Rel-20 5G-A IoT NTN Voice
Spreadtrum
SP-241629

## Slide 2: Views on Rel-20 5G-A IoT NTN Voice
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1. | IMS Voice Call Using GEO with NB-IoT access technologies (i.e., IMS voice over IoT NTN) | The study item aims at supporting IMS Voice Call Using GEO with NB-IoT access technologies Key Work Tasks 1.Study and Specify necessary simplification/optimization on IMS protocols and procedures for IMS voice over IoT NTN. (SA2) 2.Study and Specify a low codec mechanism, e.g. AI/ML media compression algorithms, etc. (SA4) | FS_5GSAT_Ph4, 5GSAT_Ph4 | SA2 | Unknown | SA4

## Slide 3
Motivation on Rel-20 IoT NTN Voice
Supporting IMS voice calls using GEO is one of the objectives of Rel-20 SA1 FS_5GSAT_Ph4 and 5GSAT_Ph4.
Due to the unique challenges of GEO satellites (e.g. substantial distance from earth, limit transmit power, etc.), narrow-bandwidth access technology is the choice.
Potential KPI for Voice Call Using GEO Access is quoted in the following table [TR 22.887].
  Issue 1: With the IMS message size tested in a commercial deployed network, using [1~3] kbps transmission data rate, Call set-up time can be [29~86] s (Note a).
    Note a: an IMS voice call procedure example
    Call set-up time ≈ (Msg 1 Length + … + Msg 8 Length) * 8 / [1~3] kbps = (2392+120+…+986+60) * 8 / [1~3] kbps ≈ [29 ~ 86] s
  Potential solution: Simplify IMS protocols and procedures
Figure 1: IMS voice call procedure example
Table 1: Potential KPI for IMS voice

## Slide 4
The limited transmission data rate as quoted in table 1 also brings challenge to IMS voice codec.
  Issue 2: A low bitrate codec (e.g. 1.2 kbps, etc.) is needed to match low transmission date rate, while the current 3GPP codec (e.g. AMR, AMR-WB, etc.) bitrate [Note b] is too high. Additionally, a low codec will be beneficial to improve system capacity.
    Note b: - AMR: 4.75 – 12.2 kbps, - AMR-WB: 6.6 – 23.85 kbps, - EVAS: 5.9 – 128 kbps
  Potential solution: Design a low bitrate codec mechanism (e.g. 1.2 kbps, etc.) in SA4, e.g. by using AI/ML media compression algorithms to achieve low bitrate, etc.
Motivation on Rel-20 IoT NTN Voice (con.)

## Slide 5
Proposal for Rel-20 IoT NTN Voice
IMS Voice Call Using GEO with NB-IoT access technologies (i.e., IMS voice over IoT NTN) should be supported in R20
  Scope:
    Study and Specify necessary simplification/optimization on IMS protocols and procedures for IMS voice over IoT NTN. (SA2)
    Study and Specify a low codec mechanism, e.g. AI/ML media compression algorithms, etc. (SA4)
Summary