## Slide 1: InterDigital views on 5GA Release 20

## Slide 2: Outline
R20 considerations for 5GA
Overall view on 5GA content
Summary

## Slide 3: R20 5GA considerations
R20 is the last release of 5G
  Focus should mostly be on enhancements of the current features (e.g. R19 enhancements)
  Baseline R20 scope can be based on agreed WTs for R19 studies as a starting point
Consider 6G allocation when scoping up 5GA
  Balance must be considered in terms of TU allocation between 5GA and 6G study
    5-7 items with a mix of smaller/larger SIDS/WIDS seems appropriate

## Slide 4: View on Rel-20 5GA Content (1/2)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Integrated Sensing & Communications | Key Work Tasks includes defining - Enhancements to 5GS to support gNB sensing. Sensing data fusion support for non-3GPP sensing Exposure and use of sensing data to NFs and AFs | Yes, TS 22.837 | SA2 | Yes | SA3 for security, SA5 for charging
2 | Ambient IoT (WID) | 5G system support for enabling Ambient IoT services for a selection of device types, connection topologies (Topology 1 and 2) and services (Inventory and Command) that have been studied in SA2/3 and RAN WGs. Key Work Tasks includes defining - Overall architecture and function enhancement to support Topology 1 and Topology 2. Ambient IoT device management including device identifier format, subscription management, authentication/authorization, etc. Ambient IoT service procedures including Reader selection/authorization, data/message delivery/aggregation/forwarding, service exposure to AIoT AF, assistance for radio resource control, etc. | Yes, TS 22.369 | SA2 | Yes | SA3 for security, SA5 for charging
3 | Immersive/XRM | Key Work Tasks includes defining - Support ATSSS with the PDU Set Feature Send Multi Modal Service information to RAN. RAN can use this information when making resource allocation decisions and in admission control (S2-2411300). | Yes | SA2 | Yes | SA4

## Slide 5: View on Rel-20 5GA Content (2/2)
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
4 | AIML | For Rel.19, two main components have been considered: AI/ML alignment and convergence for Air interface and 5G Core network, and Architecture enhancements to support 5G Core Intelligence Note that there are still WTs in Rel.19 that have not been addressed, and in addition there are requirements on direct network connection were not addressed in Rel.19 Key Work Tasks includes defining - Complete WT1.1 related to UE-side Data Collection, and Address requirements for direct device connection, to enable UEs to transmit data via direct device connection, e.g., to execute AI/ML federated learning task | Yes, TS 22.261 | SA2 | Yes | SA3 for security, SA5 for charging
5 | User Ids (slide 6 for details) | In Rel-19, support was added for QoS Differentiation for non-3GPP devices. Conclusions were not reached for identifying human users due to concerns about roaming and interworking. SA2 did not study addressing SA1’s requirements on identifying application instances. Also, adding support for exposing information about the user’s local non-3GPP connection will enable operators to configure QoS on their subscribers’ local network connections. Key Work Tasks includes defining - Continue the Rel-19 work on identifying human users by addressing how solutions will work when the UE is roaming and interworking with EPC. Add support in the 5G System for identifying application instances. Preferably by building on the human user solutions. Add support for exposing information about the UE’s local non-3GPP access connection (e.g. SSID or BSSID and local IP address) so that operators can configure QoS on the UE’s access network connection. How the QoS is configured is out of 3GPP’s scope. | Yes, TS 22.101 and TS 22.115 | SA2 | No | SA3 for security, SA5 for charging
The entries in this table are in no specific priority order

## Slide 6: User identities scope R20
In the context of this work, the user to be identified could be an individual human user using a UE with a certain subscription or an application running on or connecting via a UE.
In Rel-16, SA1 completed normative work for requirements related to user identities.
The point of this proposal is to continue the stage-2 and stage-3 work on user identities in Rel-19.
What new use cases or opportunities would be enabled?
  The operator could identify the person using a UE and/or an application instance and adjust network settings (e.g., QoS or enable parental controls when a child is using a smartphone).
  When a UE is shared (e.g., a UE embedded in a vehicle), the operator could identify this user of the UE, adjust network settings, and charge the user independent of the subscription.
  Information about a UE’s local connection (e.g. SSID, BSSID, and local IP address) could be exposed so that a network operator can use the exposed information to configure QoS on the UE’s local link.

## Slide 7: Summary
Ambient IoT to be considered only as a WID in R20
Sensing may be the only new feature for 5GA in R20 with limited scope
AIML/XRM/Sensing/Ambient IoT have major RAN dependencies
  It is suggested to have early coordination with RAN on these items