## Slide 1: Discussion on Ambient IoT device definition
Philips International B.V, OPPO, Huawei, Interdigital, MediaTek

## Slide 2: Background
SA WG1 specifies the requirements on the 5G system in TS 22.261. This includes e.g. security requirements as referred to incoming LS SP-241812 from SA WG1.
TS 22.261 defines “User Equipment” and “IoT Device” as follows:
  “User Equipment: An equipment that allows a user access to network services via 3GPP and/or non-3GPP accesses.”
  “IoT Device: a type of UE which is dedicated for a set of specific use cases or services and which is allowed to make use of certain features restricted to this type of UEs.
    NOTE 5: An IoT device may be optimized for the specific needs of services and application being executed (e.g. smart home/city, smart utilities, e-Health and smart wearables). Some IoT devices are not intended for human type communications.
These definitions do not have any technical requirement on what a UE consists of.

## Slide 3: Background (ctd.)
Since Ambient IoT device is defined as a type of IoT device, by inference it could be seen a type of UE according to TS 22.261.
Potential issue: downstream working groups (e.g. SA2, SA3) typically use the definition of User Equipment of TR 21.905 (as specified by SA) which explicitly mentions UICC support.
It needs to be clarified that using the term UE in SA WG1 requirements does not automatically imply the use of UICC because of the definition in TR 21.905.
Requiring a UICC is particularly problematic for an Ambient IoT device given its extremely low energy characteristics, which is also why the Ambient IoT requirements are largely documented in a separate TS 22.369. Hence, clarifying the implications of these definitions is important.

## Slide 4: Proposals
Proposal 1:
  SA agrees that term “User Equipment” in TR 21.905 is different from term “User Equipment” in TS 22.261 and does not apply directly to the requirements in TS 22.261.
Proposal 2:
  SA agrees that whether UICC is a feasible solution for Ambient IoT is a discussion that is independent of the definition of “User Equipment” in TR 21.905 and TS 22.261.

## Slide 5: Conclusion
Request for SA to agree/endorse the proposals on slide 4 and if needed send a clarifying LS to SA WG3 and SA WG1.
In future, SA may also need to consider clarify the definition of “User Equipment” or add e.g. definitions for IoT Devices (similar as done by SA1) to TR 21.905.