## Slide 1: Discussion on roaming traffic offloading in HPLMN TEI19 HSBO Samsung
SA WG2 Meeting #166 S2-2411534
14 - 18 November, 2024, Orlando, US

## Slide 2: Identified issues/requirements [S2-2400266]
H-UPF selection based on serving PLMN (VPLMN)
  H-SMF should be able to select H-UPF based on the Serving PLMN to apply HSBO for each operator
Establishment of a new HR PDU session to react UP path failure
  H-UPF is connected to multiple V-UPFs, and network disconnections may occur only in certain VPLMNs. When a network disconnection is detected, the corresponding VPLMN should revert to the conventionally used home-routed roaming service to minimize UE impact. Additionally, the V-UPFs that are not affected by the failure should not experience any service impact.
Provisioning DNS information available at VPLMN region
  The H-SMF and H-UPF are physically located in different places and may have different network subnets. It is difficult for the H-SMF to manage DNS addresses for all DNS Address near in VPLMN region. Additionally, the UPF can select the optimal DNS address for the UE based on the serving PLMN and the UE’s location information. Therefore, the DNS address for UE should be delivered from the H-UPF to the UE via H-SMF.
Notes: The interworking between H-UPF and V-UPF can also use VPN for security purposes. Depending on the use of VPN, additional Security Protocol Headers (e.g.Ipsec) may be required. To prevent unnecessary fragmentation, UE should be able to adjust the MTU size based on the V-UPF or Serving PLMN.

## Slide 3: UPF Selection and Failure Recovery per Serving PLMN (1/2)
Scenario for UPF selection and failure recovery per serving PLMN discussed in S2-2400266
[S2-2400266]

## Slide 4: UPF Selection and Failure Recovery per Serving PLMN (2/2)
Issue discussed in SA2#165 meeting
  Not clear whether and how to intentionally select a new H-UPF deployed in home region
Observation 1: H-SMF can select a new H-UPF deployed in home region when establishing a new HR PDU Session
  if it is aware of UP path failure of H-UPF deployed in visited region; and
  if it is configured with operator policy to support roaming traffic offloading at the H-UPF
Observation 2: H-SMF can manage/maintain the information related to UP Path Failure report as node-level
  UP Path Failure detection is reported via node level procedure, i.e., PFCP node report, which can be considered as node-level info
  Node-level information can be managed/maintained in SMF as long as the PFCP association is established while Session level context (PDU Session context) can be deleted
PFCP association can be maintained (temporally)
Proposal 1: H-SMF can select a new H-UPF in home region when establishing a new HR PDU Session establishment due to UP path failure for the path between the H-UPF deployed in visited region and V-UPF

## Slide 5: Proposed SMF operation in HSBO scenario & conventional restoration procedure
Conventional SMF’s restoration operation upon UP path failure (TS 23.527)
  When the SMF receives the PFCP Node Report Request with a User Plane Path Failure Report, the SMF may:
    delete the PDU session contexts associated with the path in failure; or
    maintain the PDU session contexts associated with the path in failure during an operator configurable maximum path failure duration. The SMF shall delete the PDU session contexts associated with the path in failure if the path is still down when this duration expires; or
    …
  When deciding to delete the PDU session contexts associated with the path in failure, the SMF shall modify or delete the affected PFCP sessions in the UPF.
As described in the above, the removal of the affected PFCP session during restoration can be stage 3 level operation. However, PDU Session re-establishment triggering and selection of H-UPF during the re-establishment is in the scope of stage 2.
Proposal 2: Up on UP path failure occurrence in HSBO scenario, SMF may trigger release of the HR PDU Session and include a cause value indicating that a PDU Session re-establishment is requested to immediately re-establish an HR PDU Session with a H-UPF in home region

## Slide 6: Provisioning DNS information available at VPLMN region
The use of DNS server in VPLMN region, is needed to return the address of application servers in VPLMN region instead of servers in HPLMN region ※ Note that the use of DNS server in VPLMN region offers lower DNS response delay
H-SMF and H-UPF are physically located in different places and may have different network subnets. It is difficult for the H-SMF to manage DNS addresses for all DNS Address near in VPLMN region
Especially, for a case where UE IP address is allocated by H-UPF, H-SMF would not be aware of IP topology of the visited region while H-UPF can be aware of/configured with IP topology of visited region
DNS server deployed along with the H-UPF on the public cloud in the visited region
  Due to the inherent characteristic of such a cloud environment, the DNS server address can be changed occasionally, which leads to configuration updates accompanies with overhead between management systems of the two remote sites.
  Management system of the public cloud of the visited region would be separated from the HPLMN operator system in the home region.
  Not easy to keep H-SMF locally configured with up-to-date DNS server information, especially noting that H-SMF is located in the home country.
Proposal 3: H-UPF in the visited region can be configured with information for DNS server available at the visited region and may provision it to H-SMF via N4.

## Slide 7: Further discussions
In the last meeting, for reaction to UP path failure occurrence between H-UPF and V-UPF, only the SSC mode 2 is addressed.
  It does not need to limit the case to SSC mode 2, rather it is more appropriate to make such reaction to be generic, e.g., triggering PDU Session release and re-establishment

## Slide 8: Summary
Proposal 1: H-SMF can select a new H-UPF in home region when establishing a new HR PDU Session establishment due to UP path failure for the path between the H-UPF deployed in visited region and V-UPF
Proposal 2: Up on UP path failure occurrence in HSBO scenario, SMF may trigger release of the HR PDU Session and include a cause value indicating that a PDU Session re-establishment is requested to immediately re-establish an HR PDU Session with a H-UPF in home region
Proposal 3: H-UPF in the visited region can be configured with information for DNS server available at the visited region and may provision it to H-SMF via N4.